## Slide 1
XD12R
The RGB LED Current Sink Driver IC
General Description
The XD12R is a 12-channel constant current sink RGB LED driver for display backlight systems.
While conventional RGB backlight systems require separate three channels for red, green, and blue LED pixels, the XD12R achieves multiplexed driving for full-color RGB backlight pixels with one or two channels.
This approach allows single-layer BLU implementation, significantly reducing PCB layers.
Each channel supports up to 40mA of output current and a maximum output voltage of 40V and can time-share up to three LEDs per channel.
This device can support max 14-bit PWM dimming resolution and a 12-bit DAC global brightness resolution.
To ensure stable, flicker-free RGB time-sequential operation, the device features optimized subframe timing control and precise current regulation to effectively suppress flickering caused by rapid color transitions.
Integrated self-protection features include LED open/short detection and overheating shutdown. A feedback control function is also included to optimize the VLED voltage during LED operation, improving power efficiency.
The XD12R can be controlled with several commands through a XC24R controller or directly by a MCU. Multiple XD12R devices can be daisy-chained and controlled via a serial interface from a single XC24R, enabling scalable, high-channel-count RGB LED backlight systems for large-area displays.
12 Channels
Application
RGB LED Backlight for TV and Monitor.
RGB Backlight for Automotive Display.
  (Cluster, Center Information, Entertainment)
Global Technologies

## Slide 2
XD12R
Features
Specialized to support RGB backlight dimming
Flexible for various LED pixel configuration:
Type-1(RGB, 12CH), Type-2(R/GB, 6CH), Type-3 (GB, 12CH)
Bi-directional 1-wire daisy chain (31 serial) connection with configurable data rate
Support Interface parity function
12-channel output sink drivers with programmable max. current 40mA
12-bit global brightness control
Configurable 12-bit PWM or 14-bit PWM
Support internal OSC frequency spread function for EMI rejection
Programmable output headroom voltage
Configurable dimming directions, head shift lighting and tail shift lighting
Sync controllability between daisied devices (sync-generation)
Optimal IC pin configuration allows for single layer PCB
Supply voltage 3.0 ~ 3.6V
Maximum 40V output driver working (headroom) voltage
Programmable LED SHORT detection level
Enable/disable OPEN detection
Programmable FEEDBACK detection level
Programmable Over-Temperature Shutdown (Typ. 130 ℃)
Enable/disable Over/Under-Voltage detection
Latch-up Immunity, ILATCH (JEDEC JESD78D Nov 2011) : ±100mA
ESDHBM (JEDEC JS-001-2017 Human Body Model) : ±2KV
Compact QFN3030-24 pin package

## Slide 3
Application Circuit
Block Diagram
XD12R
Figure 1. Block Diagram
Figure 2. Application scheme

## Slide 4
Pin diagram (Top View)
XD12R
Pin Name | Pin No. | I/O | Type | Description | Remark
VDD | 1 | - | Power | Supply voltage | 
VSS | 2 | - | GND | Ground | 
VSS | 3 | - | GND | Ground | 
VSS | 4 | - | GND | Ground | 
DIO | 5 | I/O | Digital | Data In/Out | Internal PD, 48KΩ
SVI | 6 | I | Digital | External sync. Input | External svsync (+vsync)
O3 | 7 | O | Current Load | Current Sink 3 | If unused, connect to GND
O4 | 8 | O | Current Load | Current Sink 4 | If unused, connect to GND
O7 | 9 | O | Current Load | Current Sink 7 | If unused, connect to GND
O8 | 10 | O | Current Load | Current Sink 8 | If unused, connect to GND
O11 | 11 | O | Current Load | Current Sink 11 | If unused, connect to GND
O12 | 12 | O | Current Load | Current Sink 12 | If unused, connect to GND
SVO | 13 | O | Digital | External sync. Output | External svsync (+vsync)
DDIO | 14 | I/O | Digital | Daisied Data In/Out | Internal PD, 48KΩ
Pin description
Figure 3. Pin diagram
T-Pad
VDD
VSS
VSS
O12
O11
O8
O4
O1
O2
O5
O9
VDD
VSS
VSS
DDIO
O6
O10
VSS
O7
O3
VSS
DIO
1
6
8
9
10
11
7
12
20
21
22
23
19
24
18
13
SVO
SVI
2
3
4
5
17
16
15
14

## Slide 5
XD12R
Pin Name | Pin No. | I/O | Type | Description | Remark
VSS | 15 | - | GND | Ground | 
VSS | 16 | - | GND | Ground | 
VSS | 17 | - | GND | Ground | 
VDD | 18 | - | Power | Supply Voltage | 
O10 | 19 | O | Current Load | Current Sink 10 | If unused, connect to GND
O9 | 20 | O | Current Load | Current Sink 9 | If unused, connect to GND
O6 | 21 | O | Current Load | Current Sink 6 | If unused, connect to GND
O5 | 22 | O | Current Load | Current Sink 5 | If unused, connect to GND
O2 | 23 | O | Current Load | Current Sink 2 | If unused, connect to GND
O1 | 24 | O | Current Load | Current Sink 1 | If unused, connect to GND
Pin description
Table 1. Pin Description
Equivalent Circuits of individual pins
Pad Name | I/O | Internal Circuit | Description
DIO | I/O |  | Data In/Out
DDIO | I/O |  | Daisied Data In/Out

## Slide 6
XD12R
Equivalent Circuits of individual pins
Figure. 4 Equivalent Circuits of individual pins
Pad Name | I/O | Internal Circuit | Description
O1 ~ O12 | Current Sink |  | Current Load
VDD | - |  | Supply voltage
VSS | - |  | GND
SVI | I |  | Schmit trigger
SVO | O |  | TTL output
VDD

## Slide 7
XD12R
Maximum Absolute ratings (Ta = 25℃ unless otherwise noted)
Parameter | Symbol | Value | Unit
Supply voltage | VDD | -0.3 ~ 6.0 | V
Sink output pin voltage | VO | 40 | V
Sink output current | IO | 40 | mA
DIO to GND | VDIO | -0.3 ~ VDD+0.3 | V
DDIO to GND | VDDIO | -0.3 ~ VDD+0.3 | V
Thermal Resistance |  |  | 
Junction to Ambient | RθJA | 68 1) | ℃/W
Junction to Case | RθJC | 4.0 1) | ℃/W
Power Dissipation on package | PTOT | 1.0 1) | W
Ambient temperature | TA | -20 ~ 85 | ℃
Operating Junction temperature | TJ | -20 ~ 150 | ℃
Storage temperature | TSTG | -45 ~ 150 | ℃
Relative Humidity (non-condensing) | RHNC | 5 ~ 85 | %
Moisture Sensitivity Level | MSL | Maximum Floor Life-time of 168 hr | 3
Table 2. Maximum Absolute ratings
Note :
1) Surface mounted on FR-4 substrate PC Board 1” x 1” inch 2-oz copper plate, VHD = 2.0V IOUT= 40mA TA = 55℃
2) Stresses beyond the Maximum Absolute ratings may cause permanent damage to the device
3) Exposure to absolute maximum rating conditions for extended periods may affect device reliability.
ESD Ratings
Table 3. ESD ratings
Parameter | Symbol | Value | Unit | Remark
Electrostatic Discharge HBM | ESDHBM | ±2000 | V | Norm: JEDEC JS-001-2017
Electrostatic Discharge CDM | ESDCDM | ±500 | V | Norm: JEDEC JESD22-C101F Oct 2013

## Slide 8
XD12R
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
Supply voltage |  |  |  |  |  | 
Operating voltage | VDD1) |  | 3.0 | 3.3 | 3.6 | V
Supply current |  |  |  |  |  | 
Quiescent Current | Is | Standby state, No LED current | - | 2.00 | - | mA
Operating Current | IDD | All output 100% Independent of duty sink | - | 3.00 | - | mA
Oscillator |  |  |  |  |  | 
Internal MCLK | fOSC |  | 35 | - | 75 | MHz
In/Out |  |  |  |  |  | 
DIO, DDIO | VIL VIH | Input logic low level | - | - | 0.8 | V
 |  | Input logic high level | 2.0 | - | VDD | 
 | VOL VOH | Output logic low level | - | - | 0.5 | V
 |  | Output logic high level | VDD*0.8 | - | VDD | 
 | RPD | Internal pull-down resistance | - | 48 | - | KΩ
Logic long time 2) | T1H, T0L | as a receiver | 6 | - | 63 | MCLK
Logic short time 2) | T1L, T0H | as a receiver | 3 | - | 32 | MCLK
Propagation delay | TD_DS | Downstream (DIO to DDIO) | - | 9.0 | 14 | ns
Propagation output skew3) | TDSKEW_DS | DDDIO T1H=T1H-TDSKEW_DS @downstrm | - | 1.5 | 2.6 | ns
Propagation delay | TD_US | Upstream (DDIO to DIO) | - | 9.5 | 14.5 | ns
Propagation output skew3) | TDSKEW_US | DDIO T1H=T1H-TDSKEW_US @upstream | - | 1.4 | 2.3 | ns
Electrical Characteristic (VDD =3.3V, Ta=25.0℃ unless otherwise noted)
Logic ‘1’
T1H
T1L
T0H
T0L
Logic ‘0’
Note : 1) The operation below VDD, 3.3V will limit a maximum LED sinking current and affect a current variation.
2) The conditions, ①T1H ≥ T0H* 2 ② T0L ≥ T1L* 2 ③ (T1H +T0H) = (T0L+T1L) < 90 are normally recommended.
However, the value depends on the baud-rate of the XC.
3) On downstreaming (or upstreaming), the T1H of DDDIO (or T1H of DDIO) is shorted as many as TDSKEW_DS (or TDSKEW_US), but the total of 1 bit cycle will remain the same.
So, the proper value for T1H and T0L must be carefully determined based on the daisy size.

## Slide 9
XD12R
Electrical Characteristic (VDD =3.3V, Ta=25.0℃ unless otherwise noted)
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
Output |  |  |  |  |  | 
Driving voltage | VO | Headroom voltage VHD : 0.38V@ IO 4mA, 0.40V@ IO 8mA 0.43V@ IO 12mA, 0.45V@ IO 16mA 0.47V@ IO 20mA, 0.50V@ IO 24mA 0.52V@ IO 28mA, 0.55V@ IO 32mA 0.57V@ IO 36mA, 0.60V@ IO 40mA | VHD | - | 40 | V
Short detection voltage 4) | VSD | Short detection level VSD : 3b’000=3.5V, 3b’001=4.5V 3b’010=6.5V, 3b’011=9.0V 3b’100=13.5V,3b’101=17.5V 3b’110=26V, 3b’111=32V | VSD | - | - | V
Open detection voltage 4) | VOD |  | - | - | 0.3 | V
Sink current | IO | Device max current level : IO 4’b0000 = 4mA, 4’b0001 = 8mA 4’b0010 = 12mA, 4’b0011 = 16mA 4’b0100 = 20mA, 4’b0101 = 24mA 4’b0110 = 28mA, 4’b0111 = 32mA 4’b1000 = 12mA, 4’b1001 = 16mA 4’b1010 = 20mA, 4’b1011 = 24mA 4’b1100 = 28mA, 4’b1101 = 32mA 4’b1110 = 36mA, 4’b1111 = 40mA | - | - | 40 | mA
Current accuracy 5) | % | @ a trimmed point (Room temperature at 25℃) | -1.5 | - | +1.5 | %
LED off current | IOFF | Vo = 40V | - | - | 300 | nA
Feedback |  |  |  |  |  | 
FB threshold voltage (Logically ORed for 12-ch) | VFBA | FB level VFBA : 3’b000 = 0.45V, 3’b001 = 0.55V 3’b010 = 0.65V, 3’b011 = 0.75V 3’b100 = 0.90V, 3’b101 = 1.05V 3’b110 = 1.20V, 3’b111 = 1.35V | - | VFBA | - | V
FB hysteresis voltage | VFBH |  | 40 | 60 | 110 | mV
Thermal protection |  |  |  |  |  | 
Thermal cut off @TJ | TCUT | Default OFS_TEMP [3:0] = 0x8 | - | 130 | - | ℃
Thermal cut off hysteresis @TJ | THYS |  | 10 | 20 | 30 | ℃
Note : 4) If LED open or short event is happened, the corresponding channel will be turned-off under the function
enabled. If the thermal is happened, all channels output will be turned-off under the function enabled.
5) Under satisfying the power dissipation specification.

## Slide 10
XD12R
Electrical Characteristic (VDD =3.3V, Ta=25.0℃ unless otherwise noted)
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
VDD Ramp up and VLED Start |  |  |  |  |  | 
VDD Ramp up time | TVDD | from 0 to stable 3.3V | - | - | 2.0 | ms
VLED Start time | TSU_DIM | after TSU_DIM is completed | 6) | - | - | ms
Initialization after VDD, 3.3V stable |  |  |  |  |  | 
Internal Initial time | TINIT | from stable 3.3V | 100 | - | - | ms
Allowed 1st command | TFCMD | after TINIT is completed | 5 | - | - | ms
Timeout : Internal timer starts after completing to receive a read-back command and stops after first response bit from a last daisied device. This depends on the frequency of MCLK. |  |  |  |  |  | 
Internal Timeout 7) | TTIMEOUT |  | - | 131,071 | - | MCLK
VSYNC daisy out @ EXT_VS_E = 1 |  |  |  |  |  | 
VSYNCO delay | TVSOD | from VSYNCI to VSYNCO | - | 5.0 | 9.0 | ns
Note : 6) The time depends on the system configuration, the daisied XD12R number and Baud-rate.
7) If the timeout will be expired, the internal communication logic will go to an initial state, so new command
transaction will be possible. The timeout function is configurable.
Power Sequence
Important statement
Global Technologies reserves the right to change the above-mentioned information without prior notice.
Table 4. Electrical Characteristic
Figure 5. Power up sequence and Ramp-up time
3.3V stable
VDD
accessible
TVDD
VLED
TINIT
1st Command to XD12R
TSU_DIM
Set-up for dimming
XD12R setup for dimming
TFCMD

## Slide 11
XD12R
Layout for Power Lane for single-layer PCB
As shown in the figure below, it is recommended that a bypass capacitor should be placed as close to the pin 1 and pin 18 as possible in below.
XD12R (Example) Recommended Routing Guidelines for single layer PCB
PCB : single layer
PSR over lab area size : 2.2 x 0.7 mm
PSR thickness : 25~35um↑ To ensure insulation in the overlapping area between the T-PAD and
the Power VDD pattern, a PSR thickness of 25 to 35 µm or more is recommended.)
Clearance : Min 0.17mm ↑ (PAD to PAD, PAD to Pattern, Pattern to Pattern)
Power Pattern width : Please design the power pattern thickness to the maximum thickness as shown in the image
below.
Test Pin location : It is recommended to place the test point (TP) for the LED output pin within 30 mm of the IC,
as it should be located close to the IC.
The test point for control signal lines can be placed anywhere along the net.

## Slide 12
XD12R
Functional Description
The XD12R can be controlled with several commands through a XC24R controller or directly by MCU.
The access protocol and frame format are as follows and if several XD12R is connected in daisy, the commands should be repeated successively as many as the XD12R number in daisy chain.
Serial Communication Protocol
Table 5. Serial communication protocol @ PC_EN = 0
The serial communication protocol and the packet formats are shown in below for more details.
41
41
41
41
41
41
LD_TYP=01,PWM_RES=1
XC24R
or
MCU
28bit로 되어있는데
24 bit이 아닌지 확인요?

## Slide 13
XD12R
Functional Description
PWM Configuration
The PWM behavior depends on PWM configuration set to the PWM_RES and SUB-FRAME
(ex: LD_TYPE =1, svsync / 3) as shown in the Table 6. LD data is applied to the next frame.
LD_TYPE = 1, LD_DIR = 1, SUB_FRAME = 4
RED : sub-frames # with max. duty = 3
GREEN : sub-frames # with max. duty = 2
BLUE : sub-frames # with max. duty = 1
(example)
Table 6. PWM Configuration
don’t care
x
sub-frames # with max. duty
step # in sub-frame without max. duty
PWM_ RES | sub- frame # | LD data[13:0] |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 (12-bit) | 4 | x | x | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 8 | x | x | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 16 | x | x | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 32 | x | x | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 (14-bit) | 4 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 8 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 16 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 32 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 14
XD12R
Functional Description
The XD12R supports three LEDs(red, green, blue) dimming. Type-1 allows for time-division drive of three LEDs(red, green, blue) per channel. The three LEDs can be configured for different RGB colors, and the XC24R sets the time-division drive times for each RGB LED within a frame and transmits them to the XD12R as SVI signals.
The XD12R can independently control the current of each RGB LED by driving VREF1/2/3 at separate SVI intervals. Meanwhile, the XC24R provides external VLED selection signals (GATE1/2/3) for time-division drive.
RGB PWM Dimming
TYPE-1 (RGB, 12CH)
Figure. 6 PWM Dimming sequence @ LD_TYP = 01, LD_DIR = 1, SYNCMODE = 0
GATE3
GATE2
GATE1
VLED1
VLED2
VLED3
CHx
CHx+1
ld_type = 01
XD12R
Table 7. XD12R driving type for LED backlight
LD_TYPE | LED Type | No. ch. per pixel | No. pixel per IC | Full-time driving | Time sequential driving
1 | RGB or BGB | 1 | 12 | - | LED1/LED2/LED3
2 | R-GB | 2 | 6 | LED1 | LED2/LED3
3 | GB | 1 | 12 | - | LED3/LED3

## Slide 15
XD12R
Functional Description
RGB PWM Dimming
TYPE-2 (R/GB, 6CH)
The XD12R supports three LEDs(red, green, blue) dimming. In Type-2 mode, odd channels independently drive one LED(red), while even channels support brightness control by time-divisionally driving two LEDs(green, blue).
Brightness control for odd channels is implemented within a single frame, regardless of the SVI value, while brightness control for even channels is implemented within two SVI intervals for two LEDs within a single frame.
Figure. 7 PWM Dimming sequence @ LD_TYP = 10, LD_DIR = 1, SYNC_MODE = 0
GATE2
GATE3
VLED1 (: GATE1)
VLED2
VLED3
CHx
CHx+1
CHy
CHy+1
ld_type = 10
XD12R

## Slide 16
XD12R
Functional Description
RGB PWM Dimming
TYPE-3 (GB, 12CH)
The XD12R supports two LEDs(green, blue) dimming.
Type-3 mode supports time-division dimming for two LEDs (green/blue) per channel..
Figure. 8 PWM Dimming sequence @ LD_TYP = 11, LD_DIR = 0, SYNC_MODE = 0
GATE3
GATE2
VLED2
CHx
CHy
ld_type = 11
XD12R
VLED3

## Slide 17
XD12R
Functional Description
PARITY
The XD12R supports parity function for interface communication with XC24R.
TYPE | EVEN PARITY If the number of 1s in the data bits is odd, the parity bit is set to 1.
COMMAND | Supporting all commands except LD transfer command.
RANGE | All area of protocol.
FAIL | If the parity does not match, the command is not executed (daisy transmission is stopped).
Figure 9. Serial communication protocol @ PC_EN = 1

## Slide 18
XD12R
Functional Description
Transition a frame frequency without a flicker
Figure 10. PWM 12-bit
Figure 11. PWM 14-bit

## Slide 19
Register Map
XD12R
Bits | Fields |  | Descriptions
11 | RST | 0 1 | NOP All internal logics are initialized to a default state and this bit will be auto-cleared after internal initialization.
10 | VS_RST | 0 1 | NOP If this bit is set, then the serializer and de-serializer of XD12R will be initialized to a default state at every vsync. This bit set does not affect all internal registers and buffers. This bit can’t be set at the same time as the E_RST bit.
9 | E_RST | 0 1 | NOP If this bit is set, then the serializer and de-serializer of XD12R will be initialized to a default state at the last third pwm clock. This function starts from the first vsync input. So, it is careful that the XD12R access at the back of the frame should be avoided for proper operation. This bit set does not affect all internal registers and buffers. This bit can’t be set at the same time as the VS_RST bit.
4:0 | ID |  | These bits are read only. If the XD12R will receive the ID-Gen command from the XC24R controller, then the ID value is automatically generated. The ID value is needed for proper reading, so, the ID-Gen command must be firstly executed by the XC24R controller before executing any commands. If all XD12R drivers daisied will receive the ID-Gen command, the last-located device will have the first number of ID, and the first located device will have the last number of ID, that is, the number of daisied devices. The ID value can not be written by a Host.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x00 | 0x000 | RST | VS_RST | E_RST | x | x | x | x | ID [4:0] |  |  |  | 
RESET / ID

## Slide 20
XD12R
Bits | Fields | Descriptions
 |  | This register determines the dimming sequence. Even if the LD_MODE and LD_DIR value will be changed in the middle of the current frame, the value will affect the dimming sequence from the next frame after completing the current frame process.
11:8 | LD_SIZE | This value determines how many LD data will be transmitted for one time. This value is not needed to match with the number of enabled channels in the CHANNEL ENABLE register. It keeps in mind that the LD data to be transmitted will be mapped sequentially from channel 1 to channel n regardless of the corresponded CHx_EN bit activation.
7 | PC_EN | This bit determines parity check. 0 parity check disable. 1 parity check enable.
6 | VREFMODE | This bit determines whether to use VREF3. 0 used VREF2 and VREF3. 1 not used VREF3 ( VREF2 = VREF3 )
5 | SYNCMODE | This value determines VSYNC input. 0 command 1 SVI
4 | PWM_RES | This bit determines the PWM resolution. 0 12-bit PWM resolution (max steps 4,095) 1 14-bit PWM resolution (max steps 16,383)
3:2 | LD_TYPE | These bits determine the RGB PWM Dimming (LED1/2/3 PWM Dimming) 0 NOP 1 Type-1 (RGB, 12CH) 2 Type-2 (R/GB, 6CH) 3 Type-3 (GB, 12CH)
1 | LD_DIR | This bit determines the direction of modulated edge with increasing on time from a vsync. 0 Head Shift Lighting 1 Tail Shift Lighting
0 | LD_MODE | This bit determines the x8 mode. 0 Normal mode 1 x8 mode.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x01 | 0x000 | LD_SIZE [3:0] |  |  |  | PC_EN | VREFMODE | SYNCMODE | PWM_RES | LD_TYPE |  | LD_DIR | LD_MODE
LD CONTROL

## Slide 21
Bits | Fields | Descriptions
11 7:0 7:0 | FPWM_DIV1/2/3 | These registers determine the PWM reference clock. The PWM reference clock can be created by dividing the MCLK frequency by the setting value + 1. Even if the setting value will be changed in the middle of the frame, the value will be applied immediately from the next vsync assertion. Refer to the Tabel 6. for other relevant sets. FPWM_DIV1[8:0] : PWM reference clock for RED LED ( LED1 ) FPWM_DIV2[7:0] : PWM reference clock for GREEN LED ( LED2 ) FPWM_DIV3[7:0] : PWM reference clock for BLUE LED ( LED3 )
5:0 (0x02) | SF_NO | This bit determines sub-frame NO. in 1-frame. 4 : #4 sub-frames 8 : #8 sub-frames 16 : #16 sub-frames 32 : #32 sub-frames Other register values ​​are unused.
SVSYNC NUMBER / FPWM DIVIDER
Bits | Fields | Descriptions
11:0 | CHx_EN | These bits should be set if the corresponding channels are to be used. The number of enabled channels in these registers does not need to match the LD_SIZE value. It is careful that the number of enabled channels should be the same as the LD_SIZE value, but the number can be smaller than the LD_SIZE value like the special mapping below.
CHANNEL ENABLE
XD12R
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x02 | 0x000 | PWMCLK_DIV1[8] | x | x | x | x | x | SF_NO[5:0] |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x05 | 0x000 | CH12_EN | CH11_EN | CH10_EN | CH9_EN | CH8_EN | CH7_EN | CH6_EN | CH5_EN | CH4_EN | CH3_EN | CH2_EN | CH1_EN
CH1_EN | CH2_EN | CH3_EN | CH4_EN | CH5_EN | CH6_EN | CH7_EN | CH8_EN~CH12_EN
1 | 0 | 1 | 1 | 0 | 1 | 1 | all 0
the number of
enabled channels = 5
the amount of LD data to be transmitted for one time
LD_SIZE = 7
wherein, the LD data of the disabled channels, CH2 and CH5, can be any value
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x03 | 0x000 | FPWM_DIV2 [3:0] |  |  |  | FPWM_DIV1 [7:0] |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x04 | 0x000 | FPWM_DIV3 [7:0] |  |  |  |  |  |  |  | FPWM_DIV2[7:4] |  |  | 

## Slide 22
XD12R
Bits | Fields | Descriptions
7:6 | O_SLEW | This bit determines slew control for PWM drivers. It is recommended to use the default value
5 | FB_MODE | This bit determines FB MODE. 0 FB1, FB2, FB3 : vled1, vled2, vled3 different from each other 1 FB1, (FB2 ¦¦ FB3) : vled2 and vled3 using a same vled
4 | S_DET_E | This bit setting enables to detect the SHORT event, and the event can be detected in only case the corresponding channel’s PWM output is ON status and its channel’s headroom is above the set value in the SHORT_LEVEL register.
3 | O_DET_E | Setting this bit will allow the OPEN event to be detected at the point where the PWM on that channel transitions from On to Off. This event will only be detected when the headroom for that channel is less than 0.25V.
2 | T_OFF_E | This bit setting makes all channels’ output be off in case the THERMAL event happens, and all channels will be activated again after the THERMAL event is cleared.
1 | S_OFF_E | This bit setting makes the SHORTed channel’s output be off in case the SHORT event happens.
0 | O_OFF_E | This bit setting makes the OPENed channel’s output be off in case the OPEN event happens.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x06 | 0x040 | x | x | x | x | O_SLEW[1:0] |  | FB_MODE | S_DET_E | O_DET_E | T_OFF_E | S_OFF_E | O_OFF_E
FAULT CONTROL
Bits | Fields | Descriptions
8:0 | FB1/2/3_LEVEL | The FB_LEVEL determines the level at which a FB event occurs. 3b’000 : < 0.45V 3b’001 : < 0.55V 3b’010 : < 0.65V 3b’011 : < 0.75V 3’b100 : < 0.90V 3’b101 : < 1.05V 3’b110 : < 1.20V 3b’111 : < 1.35V FB1_LEVEL : FB LEVEL for LED1 FB2_LEVEL : FB LEVEL for LED2 FB3_LEVEL : FB_LEVEL for LED3
8:0 | SHORT1/2/3_LEVEL | The SHORT_LEVEL determines the level at which a SHORT event occurs. 3b’000 : > 3.5V 3b’001 : > 4.5V 3b’010 : > 6.5V 3b’011 : > 9.0V 3b’100 : > 13.5V 3b’101 : > 17.5V 3b’110 : > 26.0V 3b’111 : > 32.0V SHORT1_LEVEL : SHORT LEVEL for LED1 SHORT2_LEVEL : SHORT LEVEL for LED2 SHORT3_LEVEL : SHORT_LEVEL for LED3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x07 | 0x124 | x | x | x | FB3_LEVEL [2:0] |  |  | FB2_LEVEL [2:0] |  |  | FB1_LEVEL [2:0] |  | 
FAULT LEVEL
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x08 | 0x124 | x | x | x | SHORT3_LEVEL [2:0] |  |  | SHORT2_LEVEL [2:0] |  |  | SHORT1_LEVEL [2:0] |  | 

## Slide 23
Bits | Fields | Descriptions
11:0 | MAX_CURR_ LEVEL3/2/1 | The MAX_CURR_LEVEL determines the physical maximum current level of the device. The max dimming sink-current set by the MAX_CURR_VREF can not be beyond the MAX_CURR_LEVEL.
MAX CURRENT LEVEL
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0A | 0x000 | MAX_CURR_LEVEL3 [3:0] |  |  |  | MAX_CURR_LEVEL2 [3:0] |  | x | x | MAX_CURR_LEVEL1 [3:0] |  | FB_LEVEL [1:0] | 
XD12R
Bits | Fields | Descriptions
11 | TIMEOUT_ERR | The TIMEOUT_ERR bit indicates no readout case within the count time set in 0x19.
5 | THERMAL | The THERMAL bit indicates whether the THERMAL event due to overheating happens, and this bit will keep asserted as long as the THERMAL event is not cleared. The event threshold can be set by the OFS_TEMP in the TEMP register. If the T_OFF_E bit of the FAULT CONTROL register is set, all output sink drivers will be turned-off as long as the event is asserted, and turned-on again after internal temperature goes down below the set level of the OFS_TEMP. This bit involves other fault events in the readout information, MISS_VS, OV15 and UV15 at the FAULT_(AUTO)_READ transaction.
4 | SHORT | The SHORT bit indicates whether the SHORT event happens. The event can be detected in case some channel’s headroom goes above the set value in the SHORT_LEVEL of FAULT LEVEL register and its channel’s PWM out is ON status. If the S_OFF_E bit of the FAULT CONTROL register is set, the output of the channels in which the event occurs is turned off. This bit is auto-cleared after readout but set again as long as the event is not cleared.
3 | OPEN | The OPEN bit indicates whether the OPEN event happens. The event can be detected in case some channel’s headroom goes below 0.25V and its channel’s PWM out is OFF status. If the O_OFF_E bit of the FAULT CONTROL register is set, the output of the channels in which the event occurs is turned off. This bit is auto-cleared after readout but set again as long as the event is not cleared.
2:0 | FB1/2/3 | The FB bit indicates whether the output channels’ headroom voltage is below the value set by FB_LEVEL of the FAULT LEVEL register due to insufficient VLED. This bit is set whenever the FB event occurs in even one of the activated channels and will be auto-cleared after readout this register. This bit will be set again after readout as long as the FB condition is still valid. If the O_FB_E of FAULT CONTROL register is set, the FB event will happen in case the OPEN event is not asserted. FB1 : FB signal for LED1 FB2 : FB signal for LED2 FB3 : FB signal for LED3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
RO | 0x09 | 0x000 | TIMEOUT_ERR | x | x | x | x | x | THERMAL | SHORT | OPEN | FB3 | FB2 | FB1
FAULT STATUS

## Slide 24
XD12R
Bits | Fields | Descriptions
11:0 | MAX_CURR_VREF1/2/3 | The MAX_CURR_VREF1/2/3 determines the maximum current value of a frame to be dimmed. If the max current level is set to 8mA, then the MAX_CURR_VREF value is proportional to the max current level, and so this value decides the max current reference of all blocks being dimmed for a frame. The setting value will come into effect at the next vsync assertion even if the value is set during current dimming frame earlier than the next vsync. MAX_CURR_VREF1 : MAX_CURR_VREF for LED1 MAX_CURR_VREF2 : MAX_CURR_VREF for LED2 MAX_CURR_VREF3 : MAX_CURR_VREF for LED3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0B | 0x000 | MAX_CURR_VREF1[11:0] | x | x | x | x | x | x | x | x | x | RST2 | RST1
MAX CURRENT VREF
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0C | 0x000 | MAX_CURR_VREF2[11:0] | x | x | x | x | x | x | x | x | x | RST2 | RST1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0D | 0x000 | MAX_CURR_VREF3[11:0] | x | x | x | x | x | x | x | x | x | RST2 | RST1
DELAY CH
Bits | Fields | Descriptions
9:0 | DELAY_CHx | The DELAY_CHx determines from which PWM position the dimming out starts. If this is set to n, then the dimming out starts at (n+1)th PWM position. Normally, the setting value can not exceed the max PWM resolution.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0E | 0x000 | x | x | DELAY_CH2 [4:0] |  |  |  |  | DELAY_CH1 [4:0] |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0F | 0x000 | x | x | DELAY_CH4 [4:0] |  |  |  |  | DELAY_CH3 [4:0] |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x10 | 0x000 | x | x | DELAY_CH6 [4:0] |  |  |  |  | DELAY_CH5 [4:0] |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x11 | 0x000 | x | x | DELAY_CH8 [4:0] |  |  |  |  | DELAY_CH7 [4:0] |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x12 | 0x000 | x | x | DELAY_CH10 [4:0] |  |  |  |  | DELAY_CH9 [4:0] |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x13 | 0x000 | x | x | DELAY_CH12 [4:0] |  |  |  |  | DELAY_CH11 [4:0] |  |  |  | 

## Slide 25
XD12R
SERIALIZER OUTPUT BAUDRATE
Bits | Fields | Descriptions
11:6 | SERIAL_CLK_LOW | These bits determine the number of MCLK of VDD level in logic low value ‘0’ or the number of MCLK of 0 level in logic high value ‘1’ when the XD12R is driving the DIO pin on read-back. For more details, refer to Table. 4, Logic low time. (unit MCLK/2)
5:0 | SERIAL_CLK_HIGH | These bits determine the number of MCLK of VDD level in logic high value ‘1’ or the number of MCLK of 0 level in logic low value ‘0’ when the XD12R is driving the DIO pin on read-back. For more details, refer to Table. 4, Logic high time. (unit MCLK/2)
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x14 | 0x318 | SERIAL_CLK_LOW [5:0] |  |  |  |  |  | SERIAL_CLK_HIGH [5:0] |  |  | x | x | x
SERIAL LATENCY
Bits | Fields | Descriptions
7:0 | SERIAL_LAT | This determines the interval time between the successive data packets incoming from the XC24R. That means the interval time between the last bit of nth XD12R device’s data packet and the first bit of (n+1)th XD12R device’s data packet incoming from the XC. The setting value should be larger than the 1-bit serial data length time at which the XC24R is sending to the daisied XD12R s. So, the proper value depends on the serial baudrate of the XC24R and can be set between (1-bit time + 3 MCLKs) and (1-bit time + 5 MCLKs). If the proper value will be set, then the serial data value will be broken. It is careful that this register value should be changed to the proper value firstly in case that the Serializer Output Baudrate of XC24R is changed to slow down.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x15 | 0x080 | x | x | x | x | SERIAL_LATENCY [7:0] |  |  |  |  |  |  | 

## Slide 26
XD12R
V_MASK
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x16 | 0x000 | x | x | V_MASK [9:0] |  |  |  |  |  |  |  |  | 
Bits | Fields | Descriptions
9:0 | V_MASK | The V_MASK determines internal VSYNC position. This register is only valid under (syncmode = 1). Refer the picture Figure 12 below. (unit MCLK/2)
SV_MASK
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x17 | 0x000 | SV_MASK_EN | x | SV_MASK [9:0] |  |  |  |  |  |  |  |  | 
Bits | Fields | Descriptions
0 | SV_MASK_EN | The SV_MASK_EN determines SV_MASK function enable or disable. 0 disable, 1 enable
9:0 | SV_MASK | The SV_MASK determines internal SVSYNC rising / falling position. (unit MCLK/2)
RSTCNT
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x18 | 0x000 | x | RSTCNT[10:0] |  |  |  |  |  |  |  |  |  | 
Bits | Fields | Descriptions
10:0 | RSTCNT | The RSTCNT determines RESET position for interface (decoder/encoder) The RSTCNT is counted by a MCLK/64 from a last svsync, reset at every vsync. (unit MCLK/64)
TIMEOUT
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x19 | 0x3FF | x | x | TIMEOUT[9:0] |  |  |  |  |  |  |  |  | 
Bits | Fields | Descriptions
9:0 | TIMEOUT | The TIMEOUT is the READOUT output waiting time. If no readout is input for more than TIMEOUT, the read operation is stopped. (unit MCLK/64)
Figure 12. Timing Diagram for VSYNC / SVSYNC generation ( @SYNC_MODE = 1)

## Slide 27
FLL CONTROL
Bits | Fields | Descriptions
11:0 8:0 | FLLCNT | This determines the FLL target frequency value. The FLLCNT is counted by an MCLK/64
11 | FLL_EN | This bit enables the FLL function. The FLL continues to calibrate the MCLK frequency to exactly match the PWM frequency with the time of one frame. 1 Enable FLL function (= The MCLK is unlocking, so calibrated to the target frequency) 0 Disable FLL function (= The MCLK is locking at the current frequency) It is needed that this bit should be set to 0 just before the first vsync starts to be entered to the XD12R and set to 1 just before the vsync is not asserted if the vsync will be not supplied any more to the XD12R .
10:9 | FLL_RANGE | It is recommended to use the default value.
XD12R
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1B | 0x864 | FLL_EN | FLL_RANGE[1:0] |  | FLLCNT[20:12] |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1A | 0x000 | FLLCNT [11:0] |  |  |  |  |  |  |  |  |  |  | 
WR_PROTECT
Bits | Fields | Descriptions
11:0 | WR_PROTECT | These bits are used REGISTER write enable. The purpose of WR_PROTECT is to prevent registers from being unintentionally written. 1. write-protect1 = 0xAAA : PWMCLK_DIV1/2/3, MAX_CURR_VREF1/2/3 writable 2. write-protect2 = 0xCCC : MAX_CURR_VREF1/2/3 writable 3. Other values : writable
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1C | 0x555 | WR_PROTECT[11:0] |  |  |  |  |  |  |  |  |  |  | 

## Slide 28
XD12R
NF_CONTROL
Bits | Fields | Descriptions
11:6 | BBKN_TH | The BBKN_TH is a register for detecting short DIN pulses. It is recommended to set BBKN_TH to the max. DIN that should be filtered. The BBKN_TH DIN pulses shorter than this register are not recognized as DIN pulses internally, and the corresponding command is ignored.
5 | EMI_REJ_EN | The EMI_REJ_EN determinant EMI rejection enable. This register is used to improve EMI by spreading the SVSYNC signal in 1-mclk unit. 0 disable 1 enable
4 | SGRJT_EN2 | The SGRJT_EN2 determinant SVI glitch within 4-MCLK rejection enable. 0 disable 1 enable
3 | SGRJT_EN1 | The SGRJT_EN1 determinant SVI glitch within 3-MCLK rejection enable. 0 disable 1 enable
2 | BBKN_EN | The BBKN_TH determinant BBKN_EN function enable. 0 disable 1 enable
1 | DGRJT_EN2 | The DGRJT_EN2 determinant DIN glitch within 4-MCLK rejection enable. 0 disable 1 enable
0 | DGRJT_EN1 | The DGRJT_EN1 determinant DIN glitch within 3-MCLK rejection enable. 0 disable 1 enable
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1D | 0x000 | BBKN_TH[5:0] |  |  |  |  |  | EMI_REJ_EN | SGRJT_EN2 | SGRJT_EN1 | BBKN_EN | DGRJT_EN2 | DGRJT_EN1
CHOP_EN
Bits | Fields | Descriptions
5 | CHOP_DRV_EN | The CHOP_DRV_EN is determinant DRIVER CHOPPING function. 0 disable 1 enable
4 | CHOP_OSCLDO_EN | The CHOP_OSCLDO_EN is determinant OSC LDO CHOPPING function. 0 disable 1 enable
4 | CHOP_OSC_EN | The CHOP_OSC_EN determinant OSC CHOPPING enable. 0 disable 1 enable
3 | CHOP_IREF_EN | The CHOP_IREF_EN determinant IREF CHOPPING enable. 0 disable 1 enable
2 | CHOP_DAC_EN | The CHOP_DAC_EN determinant DAC CHOPPING enable. 0 disable 1 enable
1 | CHOP_BGR_EN | The CHOP_BGR_EN determinant BGR CHOPPING enable. 0 disable 1 enable
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x20 | 0x000 | x | x | x | x | x | x | CHOP_DRV_EN | CHOP_OSCLDO_EN | CHOP_OSC_EN | CHOP_IREF_EN | CHOP_DAC_EN | CHOP_BGR_EN

## Slide 29
XD12R
TEMP
Bits | Fields | Descriptions
11:8 | OFS_TEMP | This determines the temperature level at which the thermal event occurs. The thermal threshold temperature may vary slightly from the set value. The thermal event threshold temperature according to the OFS_TEMP value is mapped as follows. 93/ 99/ 103/ 109/ 113/ 117/ 123/ 127/ 133(default) / 137/ 143/ 147/ 151/ 157/ 161/ 165℃
7 | VDD_SEL | It is recommended to use the default value.
6 | DAC_RNG | It is recommended to use the default value.
5:4 | FLT_CTL | It is recommended to set to 1.
1:0 | FLT_GAIN | It is recommended to use the default value.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x21 | 0x890 | OFS_TEMP [3:0] |  |  |  | VDD_SEL | DAC_RNG | FLT_CTL [1:0] |  | x | x | FLT_GAIN [1:0] | 
OSC FLL MANUAL
Bits | Fields | Descriptions
11 | OSC_MAN_E | Enable the manual mode of the FLL module. It is careful that this bit must be cleared during the initialization after POR.
11:0 3:0 | OSC_FLL_MAN | This determines the FLL target frequency value in manual mode.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x22 | 0x000 | OSC_FLL_MAN [11:0] |  |  |  |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x23 | 0x808 | OSC_MAN_E | x | x | x | x | x | x | x | OSC_FLL_MAN [15:12] |  |  | 
SPREAD
Bits | Fields | Descriptions
11 | SPRD_EN | This determines SPREAD function enable. 0 disable 1 enable
6:4 | SPRD_SPD | This determines SPREAD step. ('000' :128 clock, '001' :64 clock, '010' : 32 clock, '011' : 16 clock '100’ : 8 clock, '101’ : 4 clock, '110’ : 2 clock, '111’ : 1 clock)
2:0 | SPRD_GAIN | This determines SPREAD gain. (‘000' : calculated value/8, ‘001' : calculated value/4, ‘010’ : calculated value/2, ‘011' : calculated value, ‘100’ : calculated value*2, ‘101’ : calculated value*4, ‘110’ : calculated value*8, ‘111’ : calculated value*16)
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x24 | 0x000 | SPRD_EN | x | x | x | x | SPRD_SPD[2:0] |  |  | x | SPRD_GAIN[2:0] |  | 

## Slide 30
Bits | Fields |  | Descriptions
11 | TEST_EN | 0 1 | NOP It is used to test the device for trimming. To use the PWM_FULL_O, MCLK_O and VREF_O function, this bit should be set firstly and cleared lastly after these functions are used.
10:8 | TEST_ANA_EN | 000 | Should be “000”
5 | PWM_FULL_O | 0 1 | NOP Under TEST_EN =1, the enabled channels’ PWM out keeps active state regardless of the vsync.
4 | MCLK64_O | 0 1 | NOP Under TEST_EN =1, the clock obtained by dividing MCLK by 64 is output to DDIO pin.
2 | OFS_RNG |  | It is recommended to use the default value.
1 | EXT_CLKIN |  | This EXT_CLKIN is used under TEST_EN = 1. Should be “0”
0 | ADDR_EXT | 0 1 | This bit is used to select which register groups, the general registers or the OTP mirror registers, will be accessed. The OTP control registers address, 0x3E ~ 0x3F, can be commonly accessed regardless of this bit. The general registers can be accessed except for the OTP mirror registers. The OTP mirror registers can be accessed except for the general registers.
XD12R
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3F | 0x000 | TEST_EN | TEST_ANA_EN[2:0] |  |  | x | x | PWM_FULL_O | MCLK64_O | x | OFS_RNG | EXT_CLKIN | ADDR_EXT
OTP ACCESS
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3C | 0x004 | x | x | x | x | x | x | OTP_RD [1:0] |  | OTP_WSEL [3:0] | SHORT | OPEN | FB
OTP WRITE
OTP RD/PROG
OTP PROTECT
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3E | 0x5A5 | PROTECT_EN/DIS [11:0] ※ enable (0x5A5), disable (0xA5A), need to disable for writing | x | x | x | x | x | x | ID [4:0] | x | x | RST2 | RST1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3B | 0x3FF | OTP_PG_ACCESS_CYCLE [11:0] | x | x | x | x | x | x | ID [4:0] | x | x | RST2 | RST1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3A | 0x000 | x | x | x | x | x | x | x | x | OTP_PG_ACCESS_CYCLE [15:12] | x | x | 
These registers can not go outside the Global Technologies.
OP MODE
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3D | 0x000 | OTP_PG_DONE | x | x | x | x | x | x | x | x | x | OTP_RD_START | OTP_PG_START

## Slide 31
These registers can not go outside the Global Technologies.
XD12R
LDO_DAC_CTL / OSC_RCTL / LDO_OSC_CTL / LOD_CTL
OTP CRC
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x03 | 0x808 | LDO_DAC_CTL[4] | x | x | x | x | x | x | x | OSC_RCTL[3:0] | x |  | 
DAC OFFSET / IREF_CTL / BGR_CTL
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x01 | 0x000 | DACB_OFS[4:0] |  |  |  |  | DACA_OFS[6:0] |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x00 | 0x000 | x | x | x | x | OTP_CRC_CHECKSUM [7:0] | x | x | x | x | x | x | x
These registers are the OTP Mirror registers.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x02 | 0x210 | DACB_OFS[6:5] |  | IREF_CTL[4:0] |  |  |  |  | BGR_TC[4:0] |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x04 | 0x080 | LDO_DAC_CTL[3:0] |  |  |  | LDO_OSC_CTL[3:0] |  |  |  | LDO_CTL[3:0] | x |  | 

## Slide 32
XD12R
OFS_CH 1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x06 | 0x080 | x | x | x | x | x | OFS_CH2 [7:0] | x | x | x | x |  | 
OFS_CH 2
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x07 | 0x080 | x | x | x | x | x | OFS_CH3 [7:0] | x | x | x | x |  | 
OFS_CH 3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x08 | 0x080 | x | x | x | x | x | OFS_CH4 [7:0] | x | x | x | x |  | 
OFS_CH 4
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x09 | 0x080 | x | x | x | x | x | OFS_CH5 [7:0] | x | x | x | x |  | 
OFS_CH 5
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0A | 0x080 | x | x | x | x | x | OFS_CH6 [7:0] | x | x | x | x |  | 
OFS_CH 6
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0B | 0x080 | x | x | x | x | x | OFS_CH7 [7:0] | x | x | x | x |  | 
OFS_CH 7
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0C | 0x080 | x | x | x | x | x | OFS_CH8 [7:0] | x | x | x | x |  | 
OFS_CH 8
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0D | 0x080 | x | x | x | x | x | OFS_CH9 [7:0] | x | x | x | x |  | 
OFS_CH 9
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0E | 0x080 | x | x | x | x | x | OFS_CH10 [7:0] | x | x | x | x |  | 
OFS_CH 10
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x05 | 0x080 | x | x | x | x | x | OFS_CH1 [7:0] | x | x | x | x |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x10 | 0x080 | x | x | x | x | x | OFS_CH12 [7:0] | x | x | x | x |  | 
OFS_CH 12
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0F | 0x080 | x | x | x | x | x | OFS_CH11 [7:0] | x | x | x | x |  | 
OFS_CH 11
These registers can not go outside the Global Technologies.

## Slide 33
XD12R
GAIN_CH 1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x12 | 0x020 | x | x | x | x | x | x | GAIN_CH2 [6:0] | x | x | x |  | 
GAIN_CH 2
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x13 | 0x020 | x | x | x | x | x | x | GAIN_CH3 [6:0] | x | x | x |  | 
GAIN_CH 3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x14 | 0x020 | x | x | x | x | x | x | GAIN_CH4 [6:0] | x | x | x |  | 
GAIN_CH 4
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x15 | 0x020 | x | x | x | x | x | x | GAIN_CH5 [6:0] | x | x | x |  | 
GAIN_CH 5
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x16 | 0x020 | x | x | x | x | x | x | GAIN_CH6 [6:0] | x | x | x |  | 
GAIN_CH 6
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x17 | 0x020 | x | x | x | x | x | x | GAIN_CH7 [6:0] | x | x | x |  | 
GAIN_CH 7
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x18 | 0x020 | x | x | x | x | x | x | GAIN_CH8 [6:0] | x | x | x |  | 
GAIN_CH 8
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x19 | 0x020 | x | x | x | x | x | x | GAIN_CH9 [6:0] | x | x | x |  | 
GAIN_CH 9
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1A | 0x020 | x | x | x | x | x | x | GAIN_CH10 [6:0] | x | x | x |  | 
GAIN_CH 10
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x11 | 0x020 | x | x | x | x | x | x | GAIN_CH1 [6:0] | x | x | x |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1C | 0x020 | x | x | x | x | x | x | GAIN_CH12 [6:0] | x | x | x |  | 
GAIN_CH 12
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1B | 0x020 | x | x | x | x | x | x | GAIN_CH11 [6:0] | x | x | x |  | 
GAIN_CH 11
These registers can not go outside the Global Technologies.

## Slide 34
Soldering Temperature Reflow Profile
XD12R
Important statement
Global Technologies reserves the right to change the above-mentioned information without prior notice.
Figure 13. Reflow Soldering information
Parameter | Pb-free soldering conditions
Average ramp-up rate (217 ℃ to Peak) | 3℃/second max.
Time of Preheat temp (from 150 ℃ to 200 ℃) | 60 ~ 120 second
Time to be maintained above 217 ℃ | 60 ~ 150 second
Peak temperature | 260 ℃
Time within 5 ℃ of actual peak temp | 30 second
Ramp-down rate | 6 ℃/second max.
Time from 25℃ to peak temp | 8 minutes max.
Table 8. Reflow Soldering Parameter
Note:
1. The reflow peak soldering temperature is peak 260°C and it is specified based on IPC/JEDEC J-STD- 020 “
Moisture/Reflow Sensitivity Classification for Non-Hermetic Solid State Surface Mount Devices”
2. Tolerance for peak proﬁle temperature (Tp) is deﬁned as a supplier minimum and a user maximum.
3. This document should serve as recommendation only. Other parameters may also affect soldering, so these profiles
do not guarantee absolute success.
4. Soldering profiles should be determined by reference to the solder and solder paste manufacturer's specifications, unless they conflict with the recommendations in this document.
5. The soldering profile and footprint information specified in this datasheet are general recommendations and are provided for reference only. The design, control, and quality assurance of the actual soldering process are the sole responsibility of the customer. The supplier assumes no responsibility for the soldering process or its results.

## Slide 35
XD12R
XXXXX
abc
YWCD@
        ※ Example code :2025. 07. 07
        wafer Lot #1-5
TOP VIEW
< JSICAT marking >
Fix. Code IC Part Name: XD12R
TOP VIEW
< SEMTECH marking >
Package Drawings Markings
Assembly production Code : CBA2J, CBA2S
        ** Font Type : Arial
        Marking text tolerance : ±0.05mm
Y → Year code
W → Week code , A=W1, B=W2,….
C → Wafer lot, Each wafer Lot is represented by a character (Ex: A, B, C, …).
These character cycle once a week.
D → Traceability Code Wafer lot NO. :
A big assembly Lot consists of three wafers. Each big assembly Lot.
Lot is represented by a character (Ex: 1,2,3,…)
@ → Assembly plant code
CBA2J
XD12R
AAA
CBA2S
XD12R
AAA
Body TOP Marking

## Slide 36
1) JSICAT
Embossed tape and reel data
XD12R
Figure 14. Tape and reel specification
W | 12.00±0.10 | T | 0.20±0.05 | D1 | 1.55±0.10 | 单位 | Mm
E | 1.75±0.10 | F | 5.50±0.10 | D0 | 1.55±0.10 | 材质 | ABS
P0 | 4.00±0.10 | P1 | 8.00±0.10 | P2 | 2.00±0.10 | 品名 | QFN3*3-0.75
A0 | 3.18±0.10 | B0 | 3.22±0.10 | K0 | 0.75±0.10 | 制造商 | 新创源

## Slide 37
2) SEMTECH
XD12R
Figure 15. Tape and reel specification
Note : 1. Metric dimensions govern-English are in parentheses for reference only. 2. The clearance between the components and the cavity must be within 0.05 mm min. to 0.5 mm max.
3. The component cannot rotate more than 10︒ within the determined cavity.
Package | Tape Size | D | D1 | E | F | P | P0 | P2
QFN3030-24L | 12mm | 1.55±0.1mm (0.061±0.004”) | 1.55±0.1mm (0.061±0.004”) | 1.75±0.1mm (0.069±0.004”) | 5.5±0.1mm (0.217±0.004”) | 8±0.1mm (0.315±0.004”) | 4±0.1mm (0.157±0.004”) | 2±0.1mm (0.079±0.004”)
Package | R Min. | T | W | A0 | B0 | K0
QFN3030 -24L | 25mm (0.98”) | 0.20±0.05mm (0.008±0.002”) | 12mm±0.1mm (0.472±0.004”) | 3.22±0.1 mm (0.127±0.004”) | 3.22±0.1mm (0.127±0.004”) | 0.75±0.1mm (0.03±0.004”)

## Slide 38
XD12R
Package specification
QFN 3030-24L Package Outline
TOP VIEW
BOTTOM VIEW
SIDE VIEW
Figure 16. Package Outline
Symbol | Dimensions in mm |  | 
 | Min | Typ | Max
A | 0.50 | 0.55 | 0.60
A1 | 0.00 | - | 0.05
A2 | 0.45 REF |  | 
A3 | 0.152 REF |  | 
b | 0.15 | 0.20 | 0.25
D | 2.90 | 3.00 | 3.10
D1 | 1.75 | 1.80 | 1.85
E | 2.90 | 3.00 | 3.10
E1 | 1.75 | 1.80 | 1.85
e | 0.40 BSC |  | 
K | 0.25 | 0.30 | 0.35
L | 0.25 | 0.30 | 0.35
Note
All Dimensions Do Not Include mold flash or Protrusions.

## Slide 39
Recommended Footprint
XD12R
is the trademark of Global Technologies Co., Ltd. or its subsidiaries in the Republic of Korea and/or other countries. The products of Global Technologies reserve the right to make changes without further notice to any products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Global Technologies does not convey any license under its patent rights nor the rights of others.
is the trademark of Global Technologies Co., Ltd. or its subsidiaries in the Republic of Korea and/or other countries. Global Technologies owns the rights to a number of patents, trademarks, copyrights, trade secrets, and other intellectual property. Global Technologies reserves the right to make changes without further notice to any products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Buyer is responsible for its products and applications using Global Technologies products, including compliance with all laws, regulations and safety requirements or standards, regardless of any support or applications information provided by Global Technologies. “Typical” parameters which may be provided in Global Technologies data sheets and/or specifications can and do vary in different applications and actual performance may vary over time. All operating parameters, including “Typical” must be validated for each customer application by customer’s technical experts. Global Technologies does not convey any license under its patent rights nor the rights of others. Global Technologies products are not designed, intended, or authorized for use as a critical component in life support systems or any FDA Class 3 medical devices or medical devices with a same or similar classification in a foreign jurisdiction or any devices intended for implantation in the human body. Should Buyer purchase or use Global Technologies products for any such unintended or unauthorized application, Buyer shall indemnify and hold Global Technologies and its officers, employees, subsidiaries, affiliates, and distributors harmless against all claims, costs, damages, and expenses, and reasonable attorney fees arising out of, directly or indirectly, any claim of personal injury or death associated with such unintended or unauthorized use, even if such claim alleges that Global Technologies was negligent regarding the design or manufacture of the part. Global Technologies is an Equal Opportunity/Affirmative Action Employer. This literature is subject to all applicable copyright laws and is not for resale in any manner.
Note: The reflow peak soldering temperature is peak 260°C and it is specified based on IPC/JEDEC J-STD- 020
“Moisture/Reflow Sensitivity Classification for Non-Hermetic Solid State Surface Mount Devices”
Recommended Footprint
Figure 17. Recommended Footprint
Symbol | Dimensions in mm | 
 | Value | Margin (Typ+)
X | 0.5 | +0.2
Y | 0.2 | 0
C | 0.4 | 0
X1 | 0.5 | +0.2
Y1 | 0.5 | +0.2
X2 | 1.8 | 0
Y2 | 1.8 | 0
X3 | 1.1 | +0.1
Y3 | 1.6 | +0.1
X4 | 3.4 | +0.2
Y4 | 3.4 | +0.2
G | 0.2 | 0
G1 | 0.3 | 0
G2 | 0.1 | 0
G3 | 0.1 | 0
G4 | 0.1 | 0
X2
Y2
X3
Y3