## Slide 1
XD04
The LED High-Current Sink Driver IC
General Description
The XD04 is a 4-channel constant high-current sink driver for mini-LED Backlight display applications in AM direct driving methodology. It supports max 128mA and 80V at each channel output pin rating. This device can support max 14-bit PWM dimming resolution and a 12-bit DAC global brightness resolution.
The self-protections features, LED open/short detection and thermal shutdown, are embedded. In addition, a Feedback indication signal for adjusting a VLED power is included.
It is used with a XC24 controller as a companion chip. A lot of the XD04 can be daisied to a XC24 channels and controlled through a serial interface by a XC24 controller.
4 Channels
Application
LED back-lighting with local dimming
Global Technologies

## Slide 2
XD04
Features
Bi-directional 1-wire interface and configurable transmit rate
Daisied connection between devices and pin layout suitable for single layer PCB
4 independent channels in a package
Maximum 80V headroom voltage
Configurable max current level (8/16/24/32/48/64/92/128mA)
12-bit DAC global brightness control
14-bit PWM dimming
Configurable dimming directions, Head shift lighting and Tail shift lighting
Sync controllability between daisied devices
Sink current accuracy ±1% (@ configured max current * 1)
Configurable LED short detection level and open detection
Configurable feedback generating level
Configurable over-temperature shutdown @ Typical 135℃ (TJ = 150℃)
Supply voltage 4.5 ~ 5.5V
24-PIN QFN 3030 package
Latch-up Immunity, ILATCH (JEDEC JESD78D Nov 2011) : ±100mA
ESD protection, ESDHBM (Norm: MIL 883 E Method 3015 Human Body Model) : ±2kV

## Slide 3
Application Circuit
Block Diagram
XD04
Figure 1. Block Diagram
Figure 2. Application scheme
XC24

## Slide 4
Pin diagram (Top View)
XD04
Pin description
Figure. 3 Pin diagram
Table 1. Pin Description
Pin Name | Pin No. | I/O | Type | Description | Remark
VDD | 1 | - | Power | Supply voltage | 
VSS | 2 | - | GND | Ground | 
VSS | 3 | - | GND | Ground | 
DIO | 4 | I/O | Digital | Data In/Out | Internal PD, 48KΩ
VSI 1) | 5 | I | Digital | VSYNC Input | If unused, connect to GND
FBO 1) | 6 | O | Digital | FB Open-drain output | Required an external PU If unused, connect to GND
O2 | 7 | O | Current Load | Current Sink 2 | If unused, connect to GND
O2 | 8 | O | Current Load | Current Sink 2 | If unused, connect to GND
VSS | 9 | - | GND | Ground | 
VSS | 10 | - | GND | Ground | 
O4 | 11 | O | Current Load | Current Sink 4 | 
O4 | 12 | O | Current Load | Current Sink 4 | 
FBI 1) | 13 | I | Digital | FB Daisied input (with an internal PU) | If unused, connect to GND
VSYNCO 1) | 14 | O | Digital | VSYNC daisied output | If unused, connect to GND
17
16
15
14
T-Pad
VDD
VSS
VSI
O4
O4
VSS
O2
O1
O1
VSS
O3
VDD
VSO
DDIO
VSS
O3
VSS
VSS
O2
VSS
DIO
2
3
4
5
1
6
8
9
10
11
7
12
20
21
22
23
19
24
18
13
FBI
FBO
VSS

## Slide 5
XD04
Pin Name | Pin No. | I/O | Type | Description | Remark
DDIO | 15 | I/O | Digital | Daisied Data In/Out | Internal PD, 48KΩ
VSS | 16 | - | GND | Ground | 
VSS | 17 | - | GND | Ground | 
VDD | 18 | - | Power | Supply Voltage | 
O3 | 19 | O | Current Load | Current Sink 3 | If unused, connect to GND
O3 | 20 | O | Current Load | Current Sink 3 | If unused, connect to GND
VSS | 21 | - | GND | Ground | 
VSS | 22 | - | GND | Ground | 
O1 | 23 | O | Current Load | Current Sink 1 | If unused, connect to GND
O1 | 24 | O | Current Load | Current Sink 1 | If unused, connect to GND
Pin description
Equivalent Circuits of individual pins
Pad Name | I/O | Internal Circuit | Description
VDD | - |  | Supply voltage
DIO | I/O |  | Data In/Out
DDIO | I/O |  | Daisied Data In/Out
Note : 1) In case of using FB and VSYNC function, it needs to set the FBO_E and EXT_VS_E bit. If not used, it is
recommended to connect to GND. The FBO pin is an open-drain port.

## Slide 6
XD04
Equivalent Circuits of individual pins
VDD
Figure. 4 Equivalent Circuits of individual pins
Pad Name | I/O | Internal Circuit | Description
O1 ~ O4 | Current Sink |  | Current Load
VSS | - |  | Ground
VSYNCI | Input |  | VSYNC Input (if not used, connect to GND)
VSYNCO | Output |  | VSYNC daisied Output (if not used, connect to GND)
FBI | Input |  | FB daisied Input (if not used, connect to GND)
FBO | Output |  | FB Output (if not used, connect to GND)

## Slide 7
XD04
Maximum Absolute ratings (Ta = 25℃ unless otherwise noted)
Stresses beyond the Maximum Absolute ratings may cause permanent damage to the device
Note : 1) Surface mounted on FR-4 substrate PC Board 1” x 1” inch 2-oz copper plate
Parameter | Symbol | Value | Unit
Supply voltage | VDD | -0.3 ~ 6.5 | V
Sink output pin voltage | VO | 80 | V
Sink output current | IO | 128 | mA
DIO to GND | VDIO | -0.3 ~ VDD+0.3 | V
DDIO to GND | VDDIO | -0.3 ~ VDD+0.3 | V
Thermal Resistance |  |  | 
Junction to Ambient | RθJA | TBD 1) | ℃/W
Junction to Case | RθJC | TBD 1) | ℃/W
Power Dissipation on package | PTOT | TBD 1) | W
Junction temperature | TJ | -20 ~ 150 | ℃
Storage temperature | TSTG | -45 ~ 150 | ℃
Relative Humidity (non-condensing) | RHNC | 5 ~ 85 | %
Moisture Sensitivity | MSL | Maximum Floor Life-time | 3
Parameter | Symbol | Value | Unit | Remark
Electrostatic Discharge HBM ; Contact | ESDHBM | ±2K | V | C=100 pF, R=1.5 kΩ
Electrostatic Discharge CDM ; Contact | ESDCDM | ±500 | V | R=1 Ω
Electrostatic Discharge
Table 3. Electrostatic Discharge
Table 2. Maximum Absolute ratings

## Slide 8
XD04
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
Supply voltage |  |  |  |  |  | 
Operating voltage | VDD1) |  | 4.5 | 5.0 | 5.5 | V
Supply current |  |  |  |  |  | 
Quiescent Current | Is | Standby state, No LED current | - | - | TBD | mA
Operating Current 1 | IDD1 | All output sink current = 8mA | - | - | TBD | mA
Operating Current 2 | IDD2 | All output sink current = 16mA | - | - | TBD | mA
Operating Current 3 | IDD3 | All output sink current = 24mA | - | - | TBD | mA
Operating Current 4 | IDD4 | All output sink current = 32mA | - | - | TBD | mA
Operating Current 5 | IDD5 | All output sink current = 48mA | - | - | TBD | mA
Operating Current 6 | IDD6 | All output sink current = 64mA | - | - | TBD | mA
Operating Current 7 | IDD7 | All output sink current = 92mA | - | - | TBD | mA
Operating Current 8 | IDD8 | All output sink current = 128mA | - | - | TBD | mA
Oscillator |  |  |  |  |  | 
Internal MCLK | fOSC |  |  | 40 |  | MHz
In/Out |  |  |  |  |  | 
DIO, DDIO | VIL VIH | Input logic low level | - | - | 0.8 | V
 |  | Input logic high level | 2.7 | - | VDD | 
 | VOL VOH | Output logic low level | - | - | 0.8 | V
 |  | Output logic high level | VDD * 0.8 | - | VDD | 
 | RPD | Internal pull-down resistance | - | 48 | - | KΩ
Logic high time 2) | T1H, T0L | as a receiver | 6 | - | 63 | MCLK
Logic low time 2) | T1L, T0H | as a receiver | 3 | - | 32 | MCLK
Propagation delay | TD_DS | Downstream (DIO to DDIO) | - | 9.0 | 14 | ns
Propagation output skew3) | TDSKEW_DS | DDDIO T1H=T1H-TDSKEW_DS @downstrm | - | 1.5 | 2.6 | ns
Propagation delay | TD_US | Upstream (DDIO to DIO) | - | 9.5 | 14.5 | ns
Propagation output skew3) | TDSKEW_US | DDIO T1H=T1H-TDSKEW_US @upstream | - | 1.4 | 2.3 | ns
Electrical Characteristic (VDD =5.0V, Ta=25.0℃ unless otherwise noted)
Note : 1) The operation below VDD, 5V will limit a maximum LED sinking current and affect a current variation.
2) The conditions, ①T1H ≥ T0H* 2 ② T0L ≥ T1L* 2 ③ (T1H +T0H) = (T0L+T1L) ≤ 95, are recommended.
3) On downstreaming (or upstreaming), the T1H of DDDIO (or T1H of DDIO) is shorted as many as TDSKEW_DS (or
TDSKEW_US), but the total of 1 bit cycle will remain the same. So, the proper value for T1H and T0L must be
carefully determined based on the daisy size.
Logic ‘1’
T1H
T0H
T1L
T0L
Logic ‘0’
Table 4. Electrical Characteristic

## Slide 9
XD04
Electrical Characteristic (VDD =5.0V, Ta=25.0℃ unless otherwise noted)
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
Output |  |  |  |  |  | 
Driving voltage | VO | Headroom voltage VHD : 0.55V@ IO 8mA, 0.60V@ IO 16mA 0.65V@ IO 24mA, 0.70V@ IO 32mA 0.75V@ IO 48mA, 0.80V@ IO 64mA 0.85V@ IO 92mA, 0.90V@ IO128mA | VHD | - | 80 | V
Short detection voltage 4) | VSD | Short detection level VSD : 3b’000= 3V, 3b’001= 4V 3b’010= 6V, 3b’011= 8V 3b’100=12V, 3b’101=16V 3b’110=24V, 3b’111=36V | VSD | - | - | V
Open detection voltage 4) | VOD |  | - | - | 0.25 | V
Sink current | IO | Device max current level : IO 3’b000 = 8mA, 3’b001 = 6mA 3’b010 = 24mA, 3’b011 = 32mA 3’b100 = 48mA, 3’b101 = 64mA 3’b110 = 92mA, 3’b111 = 128mA | - | - | 128 | mA
Current accuracy 5) | % | @ IO =Imax(64mA)*0.03 | -2.0 | - | +2.0 | %
 |  | @ IO =Imax(64mA)*0.1 | -1.5 | - | +1.5 | %
 |  | @ IO = Imax(64mA)*1 | -1 | - | +1 | %
LED off current | IOFF | Vo = 80V | - | - | 300 | nA
Feedback |  |  |  |  |  | 
FB threshold voltage (Logically ORed for 12-ch) | VFBA | FB level VFBA : 3’b000 = 0.40V, 3’b001 = 0.50V 3’b010 = 0.60V, 3’b011 = 0.70V 3’b100 = 0.85V, 3’b101 = 1.00V 3’b110 = 1.15V, 3’b111 = 1.30V | - | VFBA | - | V
FB hysteresis voltage | VFBH |  | 40 | 60 | 110 | mV
Thermal protection |  |  |  |  |  | 
Thermal cut off @TJ | TCUT | OFS_TEMP [3:0] = 0x8 | - | 135 | - | ℃
Thermal cut off hysteresis @TJ | THYS |  | 10 | 20 | 30 | ℃
Note : 4) If LED open or short event is happened, the corresponding channel will be turned-off under the function
enabled. If the thermal is happened, all channels output will be turned-off under the function enabled.
5) Under satisfying the power dissipation specification.
Table 4. Electrical Characteristic

## Slide 10
XD04
Electrical Characteristic (VDD =5.0V, Ta=25.0℃ unless otherwise noted)
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
VDD Ramp up and VLED Start |  |  |  |  |  | 
VDD Ramp up time | TVDD | from 0 to stable 5V | - | - | 1.2 | ms
VLED Start time | TSU_DIM | after TSU_DIM is completed | 6) | - | - | ms
Initialization after VDD, 5V stable |  |  |  |  |  | 
Internal Initial time | TINIT | from stable 5V | 10 | - | - | ms
Allowed 1st command | TFCMD | after TINIT is completed | 5 | - | - | ms
Timeout : Internal timer starts after completing to receive a read-back command and stops after first response bit from a last daisied device. This depends on the frequency of MCLK. |  |  |  |  |  | 
Internal Timeout 7) | TTIMEOUT |  | - | 32,768 | - | MCLK
VSYNC daisy out @ EXT_VS_E = 1 |  |  |  |  |  | 
VSYNCO delay | TVSOD | from VSYNCI to VSYNCO | - | 5.0 | 9.0 | ns
Note : 6) The time depends on the system configuration, the daisied XD number and Baud-rate.
7) If the timeout will be expired, the internal communication logic will go to an initial state, so new command
transaction will be possible. The timeout function is configurable.
Power Sequence
Important statement
Global Technologies reserves the right to change the above-mentioned information without prior notice.
Table 4. Electrical Characteristic
Figure. 5 Power up sequence and Ramp-up time
5V stable
VDD
accessible
TVDD
VLED
TINIT
1st Command to XD
TSU_DIM
Set-up for dimming
XD setup for dimming
TFCMD

## Slide 11
XD04
Functional Description
The XD can be controlled with several commands through a XC controller or directly by a Micom. The access protocol and frame format are as follows and if several XD is connected in daisy, the commands should be repeated successively as many as the XD number in daisy chain.
Serial Communication Protocol
Table 5. Serial communication protocol
The serial communication protocol and the packet formats are shown in below for more details.

## Slide 12
XD04
Functional Description
PWM Configuration
PWM_RES | SCAN_NO [2:0] | sub- frame # | LD Data [15:0] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | step # /sub-frame | pwm freq hz@120
 |  |  | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  | 
0 (12-bit) | 0 | 1 | x | x | x | x | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 4,095 | 120
 | 1 | 2 | x | x | x | x | x | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 2,047 | 240
 | 2 | 4 | x | x | x | x | x | x | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 1,023 | 480
 | 3 | 8 | x | x | x | x | x | x | x | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 511 | 960
 | 4 | 16 | x | x | x | x | x | x | x | x | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 255 | 1,920
 | 5 | 32 | x | x | x | x | x | x | x | x | x | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 127 | 3,840
1 (14-bit) | 0 | 1 | x | x | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 16,383 | 120
 | 1 | 2 | x | x | x | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 8,191 | 240
 | 2 | 4 | x | x | x | x | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 4,095 | 480
 | 3 | 8 | x | x | x | x | x | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 2,047 | 960
 | 4 | 16 | x | x | x | x | x | x | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 1,023 | 1,920
 | 5 | 32 | x | x | x | x | x | x | x | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 511 | 3,840
Table 6. PWM Configuration
The PWM behavior depends on the PWM configuration set to the PWM_RES and SCAN_NO [2:0] as shown in the Table 6.
don’t care
x
valid bit

## Slide 13
XD04
Functional Description
Figure. 6 Head Shift Lighting @ PWM_RES=0, SCAN_NO[2:0]=0
Figure. 7 Head Shift Lighting @ PWM_RES=0, SCAN_NO[2:0]=3
Figure. 8 Tail Shift Lighting @ PWM_RES=0, SCAN_NO[2:0]=0
Figure. 9 Tail Shift Lighting @ PWM_RES=0, SCAN_NO[2:0]=3
The Local dimming sequences according to the PWM configuration are shown as follows below, and has two dimming out directions, Head Shift Lighting and Tail Shift Lighting. The set of PWM frequency (pwmclk) according to the Frame frequency can be shown in the Table 7.
Local dimming

## Slide 14
XD04
Figure 10. External VSYNC In and Out Scheme
Functional Description
Figure 11. FBI and FBO Scheme
5
14
EXT_VS_E
5
14
EXT_VS_E
Dev (n)
Dev (n+1)
(n) VSYNCI
(n+1) VSYNCO
internal FB
6
13
internal FB
6
13
Dev (n)
Dev (n+1)
FBO_E
FBO_E
(n) FBO
(n+1) FBI
The XD has two external signal modes, VSYNC and FB, and if each external mode is enabled, each function is operated using its external signal instead of using the information obtained from the serial communication. These functions are helpful for the single PCB layout and the connection scheme is shown as follows.
Optional an external VSYNC and FB

## Slide 15
XD04
Functional Description
Switching a frame frequency without a flicker
Figure 13. PWM 12-bit
Figure 14. PWM 14-bit

## Slide 16
Register Map
XD04
Bits | Fields |  | Descriptions
0 | RST | 0 1 | NOP All internal logics are initialized to a default state and this bit will be auto-cleared after internal initialization.
4:0 | ID |  | These bits are read only. If the XD04 will receive the ID-Gen command from the XC24 controller, then the ID value is automatically generated. The ID value is needed for proper reading, so, the ID-Gen command must be firstly executed by the XC24 controller before executing any commands. If all XD04 drivers daisied will receive the ID-Gen command, the last-located device will have the first number of ID, and the first located device will have the last number of ID, that is, the number of daisied devices. The ID value can not be written by a Host.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x00 | 0x000 | RST | x | x | x | x | x | x | ID [4:0] |  |  |  | 
RESET / ID

## Slide 17
XD04
Bits | Fields | Descriptions
 |  | This register determines the dimming sequence. Even if the LD_DIR, PWM_RES, OVER_TO_E and SCAN_NO value will be changed in the middle of the current frame, the value will affect the dimming sequence from the next frame after completing the current frame process.
11:8 | CH_SIZE | This value determines how many LD data will be transmitted for one time. This value is not needed to match with the number of enabled channels in the CHANNEL ENABLE register. The LD data to be transmitted will be mapped sequentially from channel 1 to channel n regardless of the corresponded CHx_EN bit activation.
7 | EXT_VS_E | This bit determines whether the device activates external VSYNC input or internal VSYNC as the frame sync signal. 0 Internal VSYNC (The internal VSYNC can be generated from the SYNC Command) 1 External VSYNC (The TEST_EN bit should be not activated)
6 | EXT_VS_POL | This bit determines the polarity of the external VSYNC input. 0 High active 1 Low active
5:3 | SCAN_NO | This value determines the number of scanning within a frame. The scanning number is one if the value is zero. In case the value is greater than 0, the larger the value, the smaller the PWM depth. The available value is from 0 to 5, and the relationship between the set value vs the scanning number and the PWM depth can be showed in below Table 5.
2 | OVER_TO_E | Over Turn-On Enable. This bit is an optional and recommended to decide the set according to the dimming performance from internal PWM clock. It is useful in case the PWM clock is faster than ideal frequency under full PWM data.
1 | PWM_RES | This bit determines the PWM resolution. 0 12-bit PWM resolution (max steps 4,095) 1 14-bit PWM resolution (max steps 16,383)
0 | LD_DIR | This bit determines the direction of modulated edge with increasing on time from a vsync. 0 Head Shift Lighting 1 Tail Shift Lighting
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x01 | 0x000 | CH_SIZE [3:0] |  |  |  | EXT_VS_E | EXT_VS_POL | SCAN_NO [2:0] |  |  | OVER_TO_E | PWM_RES | LD_DIR
LD CONTROL

## Slide 18
Bits | Fields | Descriptions
6:0 | FPWM_DIV | This register determines the PWM reference clock. The PWM reference clock can be created by dividing the MCLK frequency by the setting value + 1. Even if the setting value will be changed in the middle of the frame, the value will be applied immediately from the next vsync assertion. The setting value according to the frame frequency is guided as shown Table 7 below.
FPWM DIVIDER
Bits | Fields | Descriptions
3:0 | CHx_EN | The CHx_EN determines which channel will be activated. The set value is independent of the value of the CH_SIZE. If the CHx_EN is not set, then the corresponding channel sink output including the its faults, OPENx, SHORTx, FBx, will be deactivated. The CHx_EN bits should be set consecutively, such as CH1_EN, CH2_EN, CH3_EN, and so on, and the number of enabled channels does not need to match the CH_SIZE value.
CHANNEL ENABLE
XD04
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x02 | 0x000 | x | x | x | x | x | FPWM_DIV [6:0] |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x03 | 0x000 | x | x | x | x | x | x | x | x | CH4_EN | CH3_EN | CH2_EN | CH1_EN
PWM_RES | Register | 100Hz | 120Hz | 144Hz | 165Hz | 240Hz
0 | FPWM_DIV | 95 | 79 | 67 | 59 | 39
 | MCLK_LOCK_CNT | 393,120 | 327,600 | 278,460 | 245,700 | 163,800
1 | FPWM_DIV | 23 | 19 | 16 | 14 | 9
 | MCLK_LOCK_CNT | 393,192 | 327,660 | 278,511 | 245,745 | 163,830
Table 7. FPWM Configuration

## Slide 19
Bits | Fields | Descriptions
10:8 | DEV_MAX_CURR_ LEVEL | The DEV_MAX_CURR_LEVEL determines the physical maximum current level of the device. The max dimming sink-current set by the MAX_CURR_VREF can not be beyond the DEV_MAX_CURR_LEVEL. 3b’000 : max 8mA 3b’001 : max 16mA 3b’010 : max 24mA 3b’011 : max 32mA 3b’100 : max 48mA 3b’101 : max 64mA 3b’110 : max 92mA 3b’111 : max 128mA
6:4 | SHORT_LEVEL | The SHORT_LEVEL determines the level at which a SHORT event occurs. 3b’000 : > 3V 3b’001 : > 4V 3b’010 : > 6V 3b’011 : > 8V 3b’100 : > 12V 3b’101 : > 16V 3b’110 : > 24V 3b’111 : > 36V
2:0 | FB_LEVEL | The FB_LEVEL determines the level at which a FB event occurs. 3b’000 : < 0.40V 3b’001 : < 0.50V 3b’010 : < 0.60V 3b’011 : < 0.70V 3b’100 : < 0.85V 3b’101 : < 1.00V 3b’110 : < 1.15V 3b’111 : < 1.30V
FAULT LEVEL
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x06 | 0x000 | x | DEV_MAX_CURR_LEVEL [2:0] | x | x | x | SHORT_LEVEL [2:0] | x | x | x | FB_LEVEL [2:0] | FB_LEVEL [1:0] | 
XD04
Bits | Fields | Descriptions
11 | MISS_VS | The MISS_VS bit indicates whether the vsync missing event happens, and auto-cleared after readout this register.
3 | THERMAL | The THERMAL bit indicates whether the THERMAL event due to overheating happens, and this bit will keep asserted as long as the THERMAL event is not cleared. The event threshold can be set by the OFS_TEMP in the TEMP register. If the T_OFF_E bit of the FAULT CONTROL register is set, all output sink drivers will be turned-off as long as the event is asserted, and turned-on again after internal temperature goes down below the set level of the OFS_TEMP.
2 | SHORT | The SHORT bit indicates whether the SHORT event happens. The event can be detected in case some channel’s headroom goes above the set value in the SHORT_LEVEL of FAULT LEVEL register and its channel’s PWM out is ON status. If the S_OFF_E bit of the FAULT CONTROL register is set, the output of the channels in which the event occurs is turned off. This bit is auto-cleared after readout but set again as long as the event is not cleared.
1 | OPEN | The OPEN bit indicates whether the OPEN event happens. The event can be detected in case some channel’s headroom goes below 0.25V and its channel’s PWM out is OFF status. If the O_OFF_E bit of the FAULT CONTROL register is set, the output of the channels in which the event occurs is turned off. This bit is auto-cleared after readout but set again as long as the event is not cleared.
0 | FB | The FB bit indicates whether the output channels’ headroom voltage is below the value set by FB_LEVEL of the FAULT LEVEL register due to insufficient VLED. This bit is set whenever the FB event occurs in even one of the activated channels and will be auto-cleared after readout this register. This bit will be set again after readout as long as the FB condition is still valid. If the O_FB_E of FAULT CONTROL register is set, the FB event will happen in case the OPEN event is not asserted.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
RO | 0x05 | 0x000 | MISS_VS | x | x | x | x | x | x | x | THERMAL | SHORT | OPEN | FB
FAULT STATUS

## Slide 20
XD04
Bits | Fields | Descriptions
11 | TIMEOUT_E | If this bit is set, the internal timeout timer starts counting from receiving some read-back command and stops after receiving the first response bit from daisied devices. If the timer will be expired due to any no response, internal communication logics will be recovered to the standby state. The timeout counter expires at approximately 800us upon receiving the read command. Recommended to be set.
10 | FBO_E | If this bit is set, the FB In/Out function is enabled. The internal FB status will be driven out active-low directly to the FBO open-drain pin #6 after being ORed with the FBI input pin #13 which is active-low with internally pull-up resistor. This function makes the FB status possible to be supplied in real-time unlike the FB value in the FAULT STATUS register. In case this bit is set and the FBI input pin #13 is unused, then the pin should be open or pull-up.
8 | MS_VS_LOCK | Under the MS_VS_LOCK = 1 and the MS_VS_DET_E = 1, if the vsync missing event happens, then the MCLK_LOCK_CNT function will be halted until receiving a vsync.
7 | MS_VS_DIMM | Under the MS_VS_DIMM = 1 and the MS_VS_DET_E = 1, if the vsync missing event happens, then the dimming out will be automatically fixed to the middle level brightness until receiving a vsync.
6 | MS_VS_DET_E | This bit enables to detect whether the vsync input is missed or not. If the vsync is not supplied within about 26ms, then the vsync missing event is asserted internally. This event assertion can be readout through the FALUT STATUS register.
5 | O_FB_E | This bit setting makes the FB possible to be asserted in only case the corresponding channel’s OPEN event is not happen. If this bit is 0, then the FB can be asserted owing to the OPEN event.
4 | O_DET_E | This bit setting enables to detect the OPEN event, and the event can be detected in only case the corresponding channel’s PWM output is OFF status and its channel’s headroom is below 0.25V.
3 | S_DET_E | This bit setting enables to detect the SHORT event, and the event can be detected in only case the corresponding channel’s PWM output is ON status and its channel’s headroom is above the set value in the SHORT_LEVEL register.
2 | T_OFF_E | This bit setting makes all channels’ output be off in case the THERMAL event happens, and all channels will be activated again after the THERMAL event is cleared.
1 | S_OFF_E | This bit setting makes the SHORTed channel’s output be off in case the SHORT event happens.
0 | O_OFF_E | This bit setting makes the OPENed channel’s output be off in case the OPEN event happens.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x07 | 0x800 | TIMEOUT_E | FBO_E | x | MS_VS_LOCK | MS_VS_DIMM | MS_VS_DET_E | O_FB_E | O_DET_E | S_DET_E | T_OFF_E | S_OFF_E | O_OFF_E
FAULT CONTROL

## Slide 21
Bits | Fields | Descriptions
11:0 | DELAY_CHx [13:12] | This register includes the MSB 2 bits of each channel’s DELAY_CHx [13:0] value. The DELAY_CHx determines from which PWM position the dimming out starts. If this is set to n, then the dimming out starts at (n+1)th PWM position. Normally, the setting value can not exceed the max PWM resolution.
DELAY CH EXTEND
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x09 | 0x000 | x | x | x | x | DELAY_CH4 [13:12] |  | DELAY_CH3 [13:12] |  | DELAY_CH2 [13:12] |  | DELAY_CH1 [13:12] | 
XD04
Bits | Fields | Descriptions
11:0 | MAX_CURR_VREF | The MAX_CURR_VREF determines the maximum current value of a frame to be dimmed. If the max current level is set to 8mA, then the MAX_CURR_VREF value is proportional to the max current level, and so this value decides the max current reference of all blocks being dimmed for a frame. The setting value will come into effect at the next vsync assertion even if the value is set during current dimming frame earlier than the next vsync.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x08 | 0x000 | MAX_CURR_VREF [11:0] | x | x | x | x | x | x | x | x | x | RST2 | RST1
MAX CURRENT VREF

## Slide 22
DELAY CH1
DELAY CH2
DELAY CH3
DELAY CH4
XD04
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0C | 0x000 | DELAY_CH2 [11:0] |  |  |  |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0D | 0x000 | DELAY_CH3 [11:0] |  |  |  |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0E | 0x000 | DELAY_CH4 [11:0] |  |  |  |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0B | 0x000 | DELAY_CH1 [11:0] |  |  |  |  |  |  |  |  |  |  | 
SERIAL CLOCK GEN
SERIAL LATENCY
Bits | Fields | Descriptions
11:6 | SERIAL_CLK_LOW | These bits determine the number of MCLK of VDD level in logic low value ‘0’ or the number of MCLK of zero level in logic high value ‘1’ when the XD04 is driving the DIO pin on read-back. For more details, refer to Table. 4, Logic low time.
5:0 | SERIAL_CLK_HIGH | These bits determine the number of MCLK of VDD level in logic high value ‘1’ or the number of MCLK of zero level in logic low value ‘0’ when the XD04 is driving the DIO pin on read-back. For more details, refer to Table. 4, Logic high time.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x25 | 0x318 | SERIAL_CLK_LOW [5:0] |  |  |  |  |  | SERIAL_CLK_HIGH [5:0] |  |  | x | x | x
Bits | Fields | Descriptions
6:0 | SERIAL_LAT | This determines the interval time between the last bit time of the current command and the first bit time of the next command. The setting value should be larger than the 1-bit serial data time. If not so, the serial data value will be broken.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x26 | 0x078 | x | x | x | x | x | SERIAL_LATENCY [6:0] |  |  |  |  |  | 

## Slide 23
MCLK LOCK
Bits | Fields | Descriptions
19:0 | MCLK_LOCK_CNT | This determines the FLL target frequency value. The proper value according to the frame frequency is showed in the Table 7.
11 | MCLK_LOCK_E | This bit enables the FLL function. The FLL continues to calibrate the MCLK frequency to exactly match the PWM frequency with the time of one frame. 0 Enable FLL function (= The MCLK is unlocking, so calibrated to the target frequency) 1 Disable FLL function (= The MCLK is locking at the current frequency)
XD04
TEMP
Bits | Fields | Descriptions
11:8 | OFS_TEMP | It is recommended to use the default value.
1:0 | FLT_GAIN | It is recommended to use the default value.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x27 | 0xFB0 | MCLK_LOCK_CNT [11:0] |  |  |  |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x28 | 0x84F | MCLK_LOCK_CNT_E | x | x | x | MCLK_LOCK_CNT [19:12] |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x29 | 0x800 | OFS_TEMP ]3:0] |  |  |  | x | x | x | x | x | x | FLT_GAIN [1:0] | 
OSC FLL MANUAL
Bits | Fields | Descriptions
11 | OSC_MAN_E | Enable the manual mode of the FLL module.
15:0 | OSC_FLL_MAN | This determines the FLL target frequency value in manual mode.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x2A | 0x000 | OSC_FLL_MAN [11:0] |  |  |  |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x2B | 0x008 | OSC_MAN_E |  |  |  |  |  |  |  | OSC_FLL_MAN [15:12] |  |  | 

## Slide 24
Bits | Fields |  | Descriptions
11 | TEST_EN | 0 1 | Normal operation It is used to test the device for trimming. To use the PWM_FULL_O, MCLK_O and VREF_O function, this bit should be set firstly and cleared lastly after these functions are used.
6 | PWM_FULL_O | 0 1 | Normal operation Under TEST_EN =1, the enabled channels’ PWM out keeps active state regardless of the vsync.
5 | MCLK_O | 0 1 | Normal operation Under TEST_EN =1, the clock obtained by dividing MCLK by 32 is output to DDIO pin.
4 | VREF_O | 0 1 | Normal operation Under TEST_EN =1, the MAX_CURR_VREF register value is continuously output to all internal current control logics regardless of the vsync.
0 | ADDR_EXT | 0 1 | This bit is used to select which register groups, the general registers or the OTP mirror registers, will be accessed. The OTP control registers address, 0x3A ~ 0x3F, can be commonly accessed regardless of this bit. The general registers can be accessed except for the OTP mirror registers. The OTP mirror registers can be accessed except for the general registers.
XD04
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3F | 0x000 | TEST_EN | x | x | x | x | PWM_FULL_O | MCLK_O | VREF_O | x | x | x | ADDR_EXT
OTP ACCESS
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3C | 0x04 | x | x | x | x | x | x | x | x | OTP_WSEL [3:0] | SHORT | OPEN | FB
OTP WRITE
OTP RD/PROG
OTP PROTECT
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3E | 0x5A5 | PROTECT_EN/DIS [11:0] ※ enable (0x5A5), disable (0xA5A), need to disable for writing | x | x | x | x | x | x | ID [4:0] | x | x | RST2 | RST1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3B | 0x3FF | OTP_PG_ACCESS_CYCLE [11:0] | x | x | x | x | x | x | ID [4:0] | x | x | RST2 | RST1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3A | 0x000 | x | x | x | x | x | x | x | x | OTP_PG_ACCESS_CYCLE [15:12] | x | x | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3D | 0x000 | x | x | x | x | x | x | x | x | x | x | OTP_RD_START | OTP_PG_START
These registers can not go outside the Global Technologies.
OP MODE

## Slide 25
These registers can not go outside the Global Technologies.
XD04
VREF CTL
OTP CRC
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x02 | 0x20 | x | x | x | x | x | x | VREF_CTL [5:0] |  | x | x |  | 
OSC
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x01 | 0x020 | x | x | x | x | x | x | OSC [5:0] |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x00 | 0x000 | x | x | x | x | OTP_CRC_CHECKSUM [7:0] | x | x | x | x | x | x | x
These registers are the OTP Mirror registers.

## Slide 26
XD04
ICTL_L_CH 1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x04 | 0x40 | x | x | x | x | x | ICTL_L_CH2 [6:0] | x | x | x | x |  | 
ICTL_L_CH 2
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x05 | 0x40 | x | x | x | x | x | ICTL_L_CH3 [6:0] | x | x | x | x |  | 
ICTL_L_CH 3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x06 | 0x40 | x | x | x | x | x | ICTL_L_CH4 [6:0] | x | x | x | x |  | 
ICTL_L_CH 4
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x03 | 0x40 | x | x | x | x | x | ICTL_L_CH1 [6:0] | x | x | x | x |  | 
These registers can not go outside the Global Technologies.
ICTL_H_CH 1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1C | 0x40 | x | x | x | x | x | ICTL_H_CH2 [6:0] | x | x | x | x |  | 
ICTL_H_CH 2
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1D | 0x40 | x | x | x | x | x | ICTL_H_CH3 [6:0] | x | x | x | x |  | 
ICTL_H_CH 3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1E | 0x40 | x | x | x | x | x | ICTL_H_CH4 [6:0] | x | x | x | x |  | 
ICTL_H_CH 4
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1B | 0x40 | x | x | x | x | x | ICTL_H_CH1 [6:0] | x | x | x | x |  | 

## Slide 27
XD04
Soldering Temperature Reflow Profile
Important statement
Global Technologies reserves the right to change the above-mentioned information without prior notice.
Figure 12. Reflow Soldering information
Parameter | Pb-free soldering conditions
Average ramp-up rate (217 ℃ to Peak) | 3℃/second max.
Time of Preheat temp (from 150 ℃ to 200 ℃) | 60 ~ 120 second
Time to be maintained above 217 ℃ | 60 ~ 150 second
Peak temperature | 260 ℃
Time within 5 ℃ of actual peak temp | 30 second
Ramp-down rate | 6 ℃/second max.
Time from 25℃ to peak temp | 8 minutes max.
Table 8. Reflow Soldering Parameter
Note:
1. The reflow peak soldering temperature is peak 260°C and it is specified based on IPC/JEDEC J-STD- 020 “
Moisture/Reflow Sensitivity Classification for Non-Hermetic Solid State Surface Mount Devices”
2. Tolerance for peak proﬁle temperature (Tp) is deﬁned as a supplier minimum and a user maximum.
3. This document should serve as recommendation only. Other parameters may also affect soldering, so these profiles
do not guarantee absolute success.
4. Soldering profile should be determined by the manufacturer of the solder paste, providing there is no contradiction
with the recommendations in this document.

## Slide 28
Package specification
XD04
QFN 3030-24L Package Outline
TOP VIEW
BOTTOM VIEW
Unit :mm
SIDE VIEW
Fig 10. Package Outline
Symbol | Dimensions in mm |  | 
 | Min | Nom | Max
A | 0.50 | 0.55 | 0.60
A1 | 0.00 | - | 0.05
A2 | 0.45 REF |  | 
A3 | 0.152 REF |  | 
b | 0.15 | 0.20 | 0.25
b1 | 0.08 | 0.13 | 0.18
D | 2.90 | 3.00 | 3.10
D1 | 1.75 | 1.80 | 1.85
E | 2.90 | 3.00 | 3.10
E1 | 1.75 | 1.80 | 1.85
e | 0.40 BSC |  | 
K | 0.25 | 0.30 | 0.35
L | 0.25 | 0.30 | 0.35

## Slide 29
Recommended Footprint
XD04
Note: The reflow peak soldering temperature is peak 260°C and it is specified based on IPC/JEDEC J-STD- 020 “Moisture/Reflow Sensitivity Classification for Non-Hermetic Solid State Surface Mount Devices”
is the trademark of Global Technologies Co., Ltd. or its subsidiaries in the Republic of Korea and/or other countries. The products of Global Technologies reserve the right to make changes without further notice to any products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Global Technologies does not convey any license under its patent rights nor the rights of others.
is the trademark of Global Technologies Co., Ltd. or its subsidiaries in the Republic of Korea and/or other countries. Global Technologies owns the rights to a number of patents, trademarks, copyrights, trade secrets, and other intellectual property. Global Technologies reserves the right to make changes without further notice to any products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Buyer is responsible for its products and applications using Global Technologies products, including compliance with all laws, regulations and safety requirements or standards, regardless of any support or applications information provided by Global Technologies. “Typical” parameters which may be provided in Global Technologies data sheets and/or specifications can and do vary in different applications and actual performance may vary over time. All operating parameters, including “Typical” must be validated for each customer application by customer’s technical experts. Global Technologies does not convey any license under its patent rights nor the rights of others. Global Technologies products are not designed, intended, or authorized for use as a critical component in life support systems or any FDA Class 3 medical devices or medical devices with a same or similar classification in a foreign jurisdiction or any devices intended for implantation in the human body. Should Buyer purchase or use Global Technologies products for any such unintended or unauthorized application, Buyer shall indemnify and hold Global Technologies and its officers, employees, subsidiaries, affiliates, and distributors harmless against all claims, costs, damages, and expenses, and reasonable attorney fees arising out of, directly or indirectly, any claim of personal injury or death associated with such unintended or unauthorized use, even if such claim alleges that Global Technologies was negligent regarding the design or manufacture of the part. Global Technologies is an Equal Opportunity/Affirmative Action Employer. This literature is subject to all applicable copyright laws and is not for resale in any manner.
Fig 14. Recommended Footprint
Symbol | Dimensions in mm | 
 | Value(mm) | Margin(Typ+)
X | 0.5 | +0.2
Y | 0.2 | 0
C | 0.4 | 0
X1 | 0.5 | +0.2
Y1 | 0.5 | +0.2
X2 | 1.9 | +0.1
Y2 | 1.9 | +0.1
X3 | 1.1 | +0.1
Y3 | 1.6 | +0.1
X4 | 3.4 | +0.2
Y4 | 3.4 | +0.2
G | 0.2 | 0
G1 | 0.3 | 0
G2 | 0.1 | 0
G3 | 0.1 | 0
G4 | 0.1 | 0
X2
Y2
X3
Y3