## Slide 1
2026.09.18
ID601 TEST Plan 통합
-

## Slide 2
Test Definition
Register Set | Applicable Test | Register Configuration ( REG_NAME( ADDR ) = DATA ) |  |  |  |  | 
 |  | REG NAME | ADDR | DATA | REG NAME | ADDR | DATA
Analog Test Mode | Trimming, Fault, Verify | RESET | 0x00 | 0x800 | FAULT_CONTROL | 0x06 | 0x0FF
 |  | FLLCNT1 | 0x22 | 0xDCD | CHOP_EN | 0x26 | 0x03F
 |  | OP_MODE | 0x3F | 0x864 |  |  | 
FLL Test Mode | FLL | RESET | 0x00 | 0x800 | CHOP_EN | 0x26 | 0x03F
 |  | OSC_FLL_MAN2 | 0x29 | 0x008 | OP_MODE | 0x3F | 0x874
Register Set Definition
Pin Group Definition
Pin Group | PIN NAME |  |  |  | 
SIGPINS | TEST | DIO | DDIO | SVI | SVO
IOUTPINS | IOUT_CH 1~12 |  |  |  | 
VSSPINS | VSS1~5 |  |  |  | 
VDDPINS | VDD1~2 |  |  |  | 

## Slide 3
Pin Description
Pin No | Pin Name | I/O | Description | Pin No | Pin Name | I/O | Description
1 | VDD | - | Supply voltage | 13 | SVO | O | External sync. Output. External svsync (+vsync).
2 | VSS | - | Ground | 14 | DDIO | I/O | Daisied Data In/Out. Internal PD, 48KΩ.
3 | VSS | - | Ground | 15 | VSS | - | Ground
4 | VSS | - | Ground | 16 | VSS | - | Ground
5 | DIO | I/O | Data In/Out. Internal PD, 48KΩ. | 17 | VSS | - | Ground
6 | SVI | I | External sync. Input. External svsync (+vsync). | 18 | VDD | - | Supply voltage
7 | O12 | O | Current Sink 12. If unused, connect to GND. | 19 | O6 | O | Current Sink 6. If unused, connect to GND.
8 | O11 | O | Current Sink 11. If unused, connect to GND. | 20 | O5 | O | Current Sink 5. If unused, connect to GND.
9 | O10 | O | Current Sink 10. If unused, connect to GND. | 21 | O4 | O | Current Sink 4. If unused, connect to GND.
10 | O9 | O | Current Sink 9. If unused, connect to GND. | 22 | O3 | O | Current Sink 3. If unused, connect to GND.
11 | O8 | O | Current Sink 8. If unused, connect to GND. | 23 | O2 | O | Current Sink 2. If unused, connect to GND.
12 | O7 | O | Current Sink 7. If unused, connect to GND. | 24 | O1 | O | Current Sink 1. If unused, connect to GND.

## Slide 4
Open/Short Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : All pins except pin under test = 0V. Current setting : VSSPINS = 100uA (Source). OS_VSS : Measure VSSPINS voltage.
Expected Results. | OS_VSS MIN / TYP / MAX = -0.2 / 0 / 0.25 V
Verification Method | Simulation
Preconditions(TEST Condition) | Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : All pins except pin under test = 0V. Current setting : SIGPINS, IOUTPINS = -100uA (Sink). OSN : Measure SIGPINS, IOUTPINS voltage.
Expected Results. | OSN MIN / TYP / MAX = -0.9 / -0.6 / -0.3 V
OS_VSS
OSN

## Slide 5
Open/Short Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : All pins except pin under test = 0V. Current setting : SIGPINS = 100uA (Source). OSP : Measure SIGPINS voltage.
Expected Results. | OSP MIN / TYP / MAX = 0.3 / 0.6 / 0.9 V
Verification Method | Simulation
Preconditions(TEST Condition) | Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : All pins except pin under test = 0V. Current setting : VDDPINS = -100uA (Sink). OS_VDD : Measure VDDPINS voltage.
Expected Results. | OS_VDD MIN / TYP / MAX = -0.8 / -0.5 / -0.2 V
OSP
OS_VDD

## Slide 6
Leakage Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : SIGPINS under test = 0V / Other input pins = 3.6V. IIL1 : Measure SIGPINS under test current.
Expected Results. | IIL1 MIN / TYP / MAX = -500 / 0 / 500 nA
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : SIGPINS under test = 3.6V / Other input pins = 0V. IIH1 : Measure SIGPINS under test current.
Expected Results. | IIH1 (TEST) MIN / TYP / MAX = -500 / 0 / 500 nA IIH1 (DIO, DDIO, SVI, SVO) MIN / TYP / MAX = 150 / 180 / 210 uA
IIL1
IIH1

## Slide 7
Leakage Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : IOUTPINS = 0V. IOZL1 : Measure IOUTPINS current in parallel.
Expected Results. | IOZL1 MIN / TYP / MAX = -2 / 0 / 10 nA
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : IOUTPINS = 3.6V. IOZH1 : Measure IOUTPINS current in parallel.
Expected Results. | IOZH1 MIN / TYP / MAX = -2 / 0 / 10 nA
IOZL1
IOZH1

## Slide 8
IDD Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : SIGPINS = 0V / All other signal pins = Open. IDDS1 : Measure VDD current after 10~100ms.
Expected Results. | IDDS1 MIN / TYP / MAX = / /
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : SIGPINS ( except DIO ) = 0V. Pattern : DIO Dynamic condition pattern looping. IDDD1 : Measure VDD current after 10~100ms.
Expected Results. | IDDD1 MIN / TYP / MAX = / /
IDDS1
IDDD1

## Slide 9
IDDQ Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | SCAN Mode condition : VDD1P5 = 1.5V / STEST = VDD / SRSTN = 0V → VDD. Pin setting : SIGPINS ( except DIO ) = 0V / All other signal pins = Open. Pattern : SCAN Mode through DIO. IDDQ_A1 : Measure VDD current after 10~100ms.
Expected Results. | IDDQ_A1 MIN / TYP / MAX = / / mA
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.6V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | SCAN Mode condition : VDD1P5 = 1.5V / STEST = VDD / SRSTN = 0V → VDD. Pin setting : SIGPINS ( except DIO ) = 0V. Pattern : SCAN Mode through DIO / Dynamic condition pattern looping. IDDQ_D1 : Measure VDD1P5 current after 10~100ms.
Expected Results. | IDDQ_D1 MIN / TYP / MAX = / / mA
IDDQ_A1
IDDQ_D1

## Slide 10
SCAN Function Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 5V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Pin setting : DIN VIH = 5V / VIL = 0V. SCAN : Run SCAN pattern and check result.
Expected Results. | SCAN = Pass ( SCAN FUNCTION Test )

## Slide 11
OTP_INIT_CHECK (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V ( 2ms sloped power-up ), DIO VIH = 3.3V / VIL = 0V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Wait 5~10ms for internal logic initialization. Normal register initial check setting (DIO). - RESET(0x00) = 0x800 - ID GEN : cmd = 4b'1000 OTP_INIT : Read register 0x01~0x3F and compare with default.
Expected Results. | OTP_INIT = Pass ( 0x01~0x3F data[11:0] = default )

## Slide 12
OTP_INIT_CHECK (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V ( 2ms sloped power-up ), DIO VIH = 3.3V / VIL = 0V, Temp(TA) = -40℃ / 27℃ / 125℃
Simulation Procedure | Mirror register initial check setting (DIO). - ID GEN : cmd = 4b'1000 - OP_MODE(0x3F) = 0x801 OTP_INIT_M : Read register 0x00~0x1E and compare with default.
Expected Results. | OTP_INIT_M = Pass ( 0x00~0x1E data[11:0] = default )

## Slide 13
OTP_INIT_CHECK (3)
Register | Address | default
LD CONTROL | 0x01 | 0x000
LD SIZE | 0x02 | 0x000
PWMCLK_DIV1/2 | 0x03 | 0x000
PWMCLK_DIV2/3 | 0x04 | 0x000
CHANNEL ENABLE | 0x05 | 0x000
FAULT CONTROL0 | 0x06 | 0x03F
FB LEVEL | 0x07 | 0x000
SHORT LEVEL | 0x08 | 0x000
FAULT STATUS0 | 0x09 | 0x000
FAULT STATUS1 | 0x0A | 0x000
FAULT STATUS2 | 0x0B | 0x000
FAULT STATUS3 | 0x0C | 0x000
MAX CURRENT LEVEL | 0x0D | 0x000
MAX CURRENT VREF1 | 0x0E | 0x000
MAX CURRENT VREF2 | 0x0F | 0x000
MAX CURRENT VREF3 | 0x10 | 0x000
CHx_LD_TYPE | 0x11 | 0x000
DELAY CH1/2 | 0x12 | 0x000
DELAY CH3/4 | 0x13 | 0x000
DELAY CH5/6 | 0x14 | 0x000
DELAY CH7/8 | 0x15 | 0x000
DELAY CH9/10 | 0x16 | 0x000
DELAY CH11/12 | 0x17 | 0x000
FAULT CONFIGURATION | 0x18 | 0x31F
BIST | 0x19 | 0x000
TEST_MODE0 | 0x1A | 0x000
TEST_MODE1 | 0x1B | 0x000
Register | Address | default
SERIAL CLK GEN | 0x1C | 0x318
SERIAL LATENCY | 0x1D | 0x080
V_MASK | 0x1E | 0x000
SV_MASK | 0x1F | 0x000
RSTCNT | 0x20 | 0x000
TIMEOUT | 0x21 | 0x3FF
FLLCNT1 (FLLCNT[11:0]) | 0x22 | 0x000
FLLCNT2 (FLL_EN/FLL_RANGE/FLLCNT[19:12]) | 0x23 | 0xC32
WR_PROTECT | 0x24 | 0x555
NF_CONTROL | 0x25 | 0x000
CHOP_EN | 0x26 | 0x000
TEMP | 0x27 | 0x029
OSC FLL MANUAL1 | 0x28 | 0x000
OSC FLL MANUAL2 | 0x29 | 0x000
OSC SPREAD | 0x2A | 0x000
CLOCK GATE EN | 0x2B | 0x017
VREF FIX1 | 0x2C | 0x000
VREF FIX2 | 0x2D | 0x000
VREF FIX3 | 0x2E | 0x000
TEST_ANA_EN | 0x39 | 0x000
OTP ACCESS1 | 0x3A | 0x000
OTP ACCESS2 | 0x3B | 0x3FF
OTP WRITE | 0x3C | 0x004
OTP RD/PROG | 0x3D | 0x000
OTP PROTECT | 0x3E | 0x555
OP MODE | 0x3F | 0x004
Normal Register
Register | Address | default
OTP_MIRROR1 | 0x00 | 0x000
OTP_MIRROR2 | 0x01 | 0x210
OTP_MIRROR3 | 0x02 | 0x210
OTP_MIRROR4 | 0x03 | 0x810
OTP_MIRROR5 | 0x04 | 0x810
OTP_MIRROR6 | 0x05 | 0x000
OTP_MIRROR7 | 0x06 | 0x000
OTP_MIRROR8 | 0x07 | 0x000
OTP_MIRROR9 | 0x08 | 0x000
OTP_MIRROR10 | 0x09 | 0x000
OTP_MIRROR11 | 0x0A | 0x000
OTP_MIRROR12 | 0x0B | 0x000
OTP_MIRROR13 | 0x0C | 0x000
OTP_MIRROR14 | 0x0D | 0x000
OTP_MIRROR15 | 0x0E | 0x000
OTP_MIRROR16 | 0x0F | 0x000
OTP_MIRROR17 | 0x10 | 0x000
OTP_MIRROR18 | 0x11 | 0x000
OTP_MIRROR19 | 0x12 | 0x040
OTP_MIRROR20 | 0x13 | 0x040
OTP_MIRROR21 | 0x14 | 0x040
OTP_MIRROR22 | 0x15 | 0x040
OTP_MIRROR23 | 0x16 | 0x040
OTP_MIRROR24 | 0x17 | 0x040
OTP_MIRROR25 | 0x18 | 0x040
OTP_MIRROR26 | 0x19 | 0x040
OTP_MIRROR27 | 0x1A | 0x040
OTP_MIRROR28 | 0x1B | 0x040
OTP_MIRROR29 | 0x1C | 0x040
OTP_MIRROR30 | 0x1D | 0x040
OTP_MIRROR31 | 0x1E | 0x000
Mirror Register

## Slide 14
Trim : IREF Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | IREF1 trim register setting (DIO). - TEST_ANA_EN(0x39) = 0x000 - IREF1_CTL(mirror)(0x01)[9:5] = 5-bit trim code IREF1_TRIM : Measure TEST pin current. Trim sweep : Until IREF1_TRIM meets target. Final code save : IREF1_CTL(mirror)(0x01)[9:5].
Expected Results. | IREF1_TRIM MIN / TYP / MAX = 9.7 / 10 / 10.3 uA
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | IREF2 trim register setting (DIO). - TEST_ANA_EN(0x39) = 0x001 - IREF2_CTL(mirror)(0x02)[9:5] = 5-bit trim code IREF2_TRIM : Measure TEST pin current. Trim sweep : Until IREF2_TRIM meets target. Final code save : IREF2_CTL(mirror)(0x02)[9:5].
Expected Results. | IREF2_TRIM MIN / TYP / MAX = 9.7 / 10 / 10.3 uA
IREF1
IREF2

## Slide 15
Trim : LDO Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(DET) trim register setting (DIO). - TEST_ANA_EN(0x39) = 0x002 - LDO_BGR2_CTL(mirror)(0x03)[4:0] = 5-bit trim code LDO_DET_TRIM : Measure TEST pin voltage. Trim sweep : Until LDO_DET_TRIM meets target. Final code save : LDO_BGR2_CTL(mirror)(0x03)[4:0].
Expected Results. | LDO_DET_TRIM MIN / TYP / MAX = 1.425 / 1.5 / 1.575 V
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(DIG) trim register setting (DIO). - TEST_ANA_EN(0x39) = 0x003 - LDO_CTL(mirror)(0x05)[3:0] = 4-bit trim code LDO_DIG_TRIM : Measure TEST pin voltage. Trim sweep : Until LDO_DIG_TRIM meets target. Final code save : LDO_CTL(mirror)(0x05)[3:0].
Expected Results. | LDO_DIG_TRIM MIN / TYP / MAX = 1.425 / 1.5 / 1.575 V
LDO_DET
LDO_DIG

## Slide 16
Trim : LDO Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(DAC) trim register setting (DIO). - TEST_ANA_EN(0x39) = 0x004 - LDO_DAC_CTL(mirror)(0x04)[11:7] = 5-bit trim code LDO_DAC_TRIM : Measure TEST pin voltage. Trim sweep : Until LDO_DAC_TRIM meets target. Final code save : LDO_DAC_CTL(mirror)(0x04)[11:7].
Expected Results. | LDO_DAC_TRIM MIN / TYP / MAX = 1.425 / 1.5 / 1.575 V
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(FLL) trim register setting (DIO). - TEST_ANA_EN(0x39) = 0x005 - LDO_OSC_CTL(mirror)(0x05)[7:4] = 4-bit trim code LDO_FLL_TRIM : Measure TEST pin voltage. Trim sweep : Until LDO_FLL_TRIM meets target. Final code save : LDO_OSC_CTL(mirror)(0x05)[7:4].
Expected Results. | LDO_FLL_TRIM MIN / TYP / MAX = 1.425 / 1.5 / 1.575 V
LDO_DAC
LDO_FLL

## Slide 17
Trim : OVER TEMP Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | OVER TEMP trim register setting (DIO). - OFS_TEMP(mirror)(0x03)[11:8] = 4-bit trim code O1(MEAS). - TEST_ANA_EN(0x39) = 0x008 - Measure Test pin voltage O2(MEAS). - TEST_ANA_EN(0x39) = 0x009 - Measure Test pin voltage OV TEMP TRIM : O2(MEAS) − O1(MEAS). Trim sweep : Until OV TEMP TRIM meets target. Final code save : OFS_TEMP(mirror)(0x03)[11:8].
Expected Results. | OV TEMP TRIM MIN / TYP / MAX = - / 209.4 / - mV

## Slide 18
Trim : OSC Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | OSC trim register setting (DIO). - TEST_ANA_EN(0x39) = 0x000 - OSC_FLL_MAN2(0x29) = 0x808 - OSC_RCTL(mirror)(0x04)[4:0] = 5-bit trim code OSC_TRIM : Measure DDIO pin frequency. Trim sweep : Until OSC_TRIM meets target. Final code save : OSC_RCTL(mirror)(0x04)[4:0].
Expected Results. | OSC_TRIM MIN / TYP / MAX = 0.757 / 0.797 / 0.837 MHz

## Slide 19
Trim : GAIN Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 1V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | GAIN trim register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - MAX_CURRENT_LEVEL(0x0D) = 0x111 - MAX_CURR_VREF1(0x0E) : P1 = 0x12C / P2 = 0x514 - MAX_CURR_VREF2(0x0F) : P1 = 0x12C / P2 = 0x514 - MAX_CURR_VREF3(0x10) : P1 = 0x12C / P2 = 0x514 - GAIN_CH(N)(mirror)(0x12 ~ 0x1D)[6:0] = 7-bit trim code P1 current : Measure IOUT sink current. P2 current : Measure IOUT sink current. GAIN_TRIM : Calculate ( P2 – P1 ). Trim sweep : Until GAIN_TRIM meets target. Final code save : GAIN_CH(N)(mirror)(0x12 ~ 0x1D)[6:0]. Channel repeat : IOUT_CH1~12, one channel at a time.
Expected Results. | GAIN_TRIM MIN / TYP / MAX = 1.856 / 1.954 / 2.052 mA

## Slide 20
Trim : OFFSET Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 1V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | OFFSET trim register setting (DIO) - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - MAX_CURRENT_LEVEL(0x0D) = 0x111 - MAX_CURR_VREF1(0x0E) : P3 = 0x0C8 / P4 = 0x12C - MAX_CURR_VREF2(0x0F) : P3 = 0x0C8 / P4 = 0x12C - MAX_CURR_VREF3(0x10) : P3 = 0x0C8 / P4 = 0x12C - OFS_CH(N)(mirror)(0x06 ~ 0x11)[8:0] = 9-bit trim code P3 current : Measure IOUT sink current. P4 current : Measure IOUT sink current. OFFSET_TRIM : Calculate ( P3 + P4 ) / 2 Trim sweep : Until OFFSET_TRIM meets target. Final code save : OFS_CH(N)(mirror)(0x06 ~ 0x11)[8:0]. Channel repeat : IOUT_CH1~12, one channel at a time.
Expected Results. | OFFSET_TRIM MIN / TYP / MAX = 0.464 / 0.488 / 0.512 mA

## Slide 21
EFUSE
Verification Method | Simulation
Preconditions(TEST Condition) | All trim tests completed, Power up, VDD Voltage 3.3V, VDD rising time : 300us, Temp = 27℃
Simulation Procedure | ※ OTP writing is allowed only once. Voltage setting : VDD 3.3V → 5.5V / I/O = 5.5V (No Power OFF). - DIO VIH = 5.5V / VIL = 0V. eFuse register setting (DIN). - OP_MODE(0x3F) = 0x800 - OTP_RD/PROG(0x3D) = 0x001 (otp_pg_start) eFuse write : Copy final trim codes to eFuse. Power cycle : Power OFF → ON (VDD = 5V). Code download : eFuse codes to register. Code compare : before eFuse vs. after eFuse. EFUSE : Target value maintained.
Expected Results. | EFUSE = Pass

## Slide 22
Verify : IREF Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | IREF1 verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x000 IREF1_VFY : Measure TEST pin current.
Expected Results. | IREF1_VFY MIN / TYP / MAX = 9.7 / 10 / 10.3 uA
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | IREF2 verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x001 IREF2_VFY : Measure TEST pin current.
Expected Results. | IREF2_VFY MIN / TYP / MAX = 9.7 / 10 / 10.3 uA
IREF1_VFY
IREF2_VFY

## Slide 23
Verify : LDO Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(DET) verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x002 LDO_DET_VFY : Measure TEST pin voltage.
Expected Results. | LDO_DET_VFY MIN / TYP / MAX = 1.455 / 1.5 / 1.545 V
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(DIG) verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x003 LDO_DIG_VFY : Measure TEST pin voltage.
Expected Results. | LDO_DIG_VFY MIN / TYP / MAX = 1.455 / 1.5 / 1.545 V
LDO_DET_VFY
LDO_DIG_VFY

## Slide 24
Verify : LDO Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(DAC) verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x004 LDO_DAC_VFY : Measure TEST pin voltage.
Expected Results. | LDO_DAC_VFY MIN / TYP / MAX = 1.455 / 1.5 / 1.545 V
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | LDO(FLL) verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x005 LDO_FLL_VFY : Measure TEST pin voltage.
Expected Results. | LDO_FLL_VFY MIN / TYP / MAX = 1.455 / 1.5 / 1.545 V
LDO_DAC_VFY
LDO_FLL_VFY

## Slide 25
Verify : BGR Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | BGR1 verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x006 BGR1_VFY : Measure TEST pin voltage.
Expected Results. | BGR1_VFY MIN / TYP / MAX = 1.197 / 1.234 / 1.271 V
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | BGR2 verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x007 BGR2_VFY : Measure TEST pin voltage.
Expected Results. | BGR2_VFY MIN / TYP / MAX = 1.220 / 1.258 / 1.295 V
BGR1_VFY
BGR2_VFY

## Slide 26
Verify : OSC Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | OSC verify register setting (DIO). - TEST_ANA_EN(0x39) = 0x000 - OSC_FLL_MAN2(0x29) = 0x808 OSC_VFY : Measure SVO pin frequency (/64).
Expected Results. | OSC_VFY MIN / TYP / MAX = 0.757 / 0.797 / 0.837 MHz (51/64)

## Slide 27
Verify : FLL_LOCK_P1_TEST
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , FLL Test Mode
Simulation Procedure | FLL mode register setting (DIO). - FLLCNT1(0x22) = P1 : 0xB0B / P2 : 0xDCD / P3 : 0x090 - FLLCNT2(0x23) = P1 : 0xC28 / P2 : 0xC32 / P3 : 0xC3D Pattern : Input DIN Pin Vsync Command (1011), Vsync 120Hz input. FLL_P# : Measure SVO pin frequency after 200ms (1/64 divided).
Expected Results. | FLL_P# MIN / TYP / MAX - FLLCNT1 / FLLCNT2 = 0xB0B / 0xC28 : FLL_P1 = 0.622 / 0.625 / 0.628 MHz (40M) - FLLCNT1 / FLLCNT2 = 0xDCD / 0xC32 : FLL_P2 = 0.777 / 0.781 / 0.785 MHz (50M) - FLLCNT1 / FLLCNT2 = 0x090 / 0xC3D : FLL_P3 = 0.933 / 0.938 / 0.942 MHz (60M)

## Slide 28
Verify : IOUT_3Point Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 1V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | IOUT 3Point register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - MAX_CURRENT_LEVEL(0x0D) = 0x111 - MAX_CURR_VREF1(0x0E) = P1 : 0x12C / P2 : 0x2BC / P3 : 0xBB8 - MAX_CURR_VREF2(0x0F) = P1 : 0x12C / P2 : 0x2BC / P3 : 0xBB8 - MAX_CURR_VREF3(0x10) = P1 : 0x12C / P2 : 0x2BC / P3 : 0xBB8 IOUT_3P_P#_VFY1 : Measure IOUT sink current. Channel repeat : IOUT_CH1~12, one channel at a time.
Expected Results. | IOUT_3P_P#_VFY1 MIN / TYP / MAX - MAX_CURR_VREF# = 0x12C : IOUT_3P_P1_VFY1 = 0.577 / 0.586 / 0.595 mA (300) - MAX_CURR_VREF# = 0x2BC : IOUT_3P_P2_VFY1 = 1.347 / 1.368 / 1.389 mA (700) - MAX_CURR_VREF# = 0xBB8 : IOUT_3P_P3_VFY1 = 5.773 / 5.861 / 5.949 mA (3000)

## Slide 29
Verify : IOUT_Sweep Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 1V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | IOUT Sweep register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - MAX_CURRENT_LEVEL(0x0D) = 0x000, 0x111, 0x222, … , 0xDDD, 0xEEE, 0xFFF (16 Level) - MAX_CURR_VREF1(0x0E) = 0x12C - MAX_CURR_VREF2(0x0F) = 0x12C - MAX_CURR_VREF3(0x10) = 0x12C IOUT_1P_P# : Measure IOUT sink current. Channel repeat : IOUT_CH1~12, one channel at a time.
Expected Results. | IOUT_1P_P# MIN / TYP / MAX - MAX_CURRENT_LEVEL = 0x000 : IOUT_1P_P1 = 0.289 / 0.293 / 0.297 mA - MAX_CURRENT_LEVEL = 0x111 : IOUT_1P_P2 = 0.577 / 0.586 / 0.595 mA - MAX_CURRENT_LEVEL = 0x222 : IOUT_1P_P3 = 0.866 / 0.879 / 0.892 mA - MAX_CURRENT_LEVEL = 0x333 : IOUT_1P_P4 = 1.154 / 1.172 / 1.19 mA - MAX_CURRENT_LEVEL = 0x444 : IOUT_1P_P5 = 1.443 / 1.465 / 1.487 mA - MAX_CURRENT_LEVEL = 0x555 : IOUT_1P_P6 = 1.732 / 1.758 / 1.784 mA - MAX_CURRENT_LEVEL = 0x666 : IOUT_1P_P7 = 2.02 / 2.051 / 2.082 mA - MAX_CURRENT_LEVEL = 0x777 : IOUT_1P_P8 = 2.309 / 2.344 / 2.379 mA - MAX_CURRENT_LEVEL = 0x888 : IOUT_1P_P9 = 2.597 / 2.637 / 2.677 mA - MAX_CURRENT_LEVEL = 0x999 : IOUT_1P_P10 = 2.886 / 2.93 / 2.974 mA - MAX_CURRENT_LEVEL = 0xAAA : IOUT_1P_P11 = 3.175 / 3.223 / 3.271 mA - MAX_CURRENT_LEVEL = 0xBBB : IOUT_1P_P12 = 3.463 / 3.516 / 3.569 mA - MAX_CURRENT_LEVEL = 0xCCC : IOUT_1P_P13 = 3.753 / 3.81 / 3.867 mA - MAX_CURRENT_LEVEL = 0xDDD : IOUT_1P_P14 = 4.041 / 4.103 / 4.165 mA - MAX_CURRENT_LEVEL = 0xEEE : IOUT_1P_P15 = 4.33 / 4.396 / 4.462 mA - MAX_CURRENT_LEVEL = 0xFFF : IOUT_1P_P16 = 4.619 / 4.689 / 4.759 mA

## Slide 30
DRIVING VOLTAGE
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp = 27℃ , Analog Test Mode
Simulation Procedure | Driving voltage register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - MAX_CURRENT_LEVEL(0x0D) = 0x111 - MAX_CURR_VREF1(0x0E) = 0xFFF - MAX_CURR_VREF2(0x0F) = 0xFFF - MAX_CURR_VREF3(0x10) = 0xFFF P1 current : Measure IOUT sink current at VLED = 0.5V. P2 current : Measure IOUT sink current at VLED = 1.5V. DRV_VOL : Calculate ( P2 − P1 ) / P2. Channel repeat : IOUT_CH1~12, one channel at a time.
Expected Results. | DRV_VOL MIN / TYP / MAX = - / - / 1 % ( @ IOUT : 8mA )

## Slide 31
UV Voltage VDD Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 2.4V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV VDD register setting (DIO). - TEST_ANA_EN(0x39) = 0x00A VDD sweep : 2.4V → 2.8V. UV_VDD_R_LV : Record VDD at TEST pin 'L' → 'H' transition.
Expected Results. | UV_VDD_R_LV MIN / TYP / MAX = 2.5 / 2.6 / 2.7 V
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.0V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV VDD register setting (DIO). - TEST_ANA_EN(0x39) = 0x00A VDD sweep : 3.0V → 2.4V. UV_VDD_F_LV : Record VDD at TEST pin ‘H' → ‘L' transition.
Expected Results. | UV_VDD_F_LV MIN / TYP / MAX = 2.2 / 2.6 / 3.0 V
UV_VDD_R_LV
UV_VDD_F_LV

## Slide 32
UV/OV Voltage LDO Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO register setting (DIO). - TEST_ANA_EN(0x39) = 0x00D TEST pin setting : 1.5V. INIT_LDO : Read flag 0x0A[2:1].
Expected Results. | INIT_LDO = 00 (Pass)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO register setting (DIO). - TEST_ANA_EN(0x39) = 0x00D - TEST_MODE0(0x1A) = 0x00A TEST pin sweep : 1.5V → 1.0V. LDOOSC_UV Level : TEST voltage when SVO pin is from ‘L’ to v ‘H’. UV_LDO : Read flag 0x0A[2:1].
Expected Results. | LDODIG_UV MIN / TYP / MAX = 1.25 / 1.35 / 1.45 V UV_LDO = 01 (Pass)
INIT_LDO
UV_LDO

## Slide 33
UV/OV Voltage LDO Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO register setting (DIO). - TEST_ANA_EN(0x39) = 0x00D - TEST_MODE0(0x1A) = 0x009 TEST pin sweep : 1.5V → 1.8V. LDODIG_OV Level : TEST voltage when SVO pin is from ‘L’ to ‘H’ OV_LDO : Read flag 0x0A[2:1].
Expected Results. | LDODIG_OV MIN / TYP / MAX = 1.55 / 1.65 / 1.75 V OV_LDO = 10 (Pass)

## Slide 34
UV/OV Voltage LDO_DAC Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO_DAC register setting (DIO). - TEST_ANA_EN(0x39) = 0x00E TEST pin setting : 1.5V. INIT_LDO_DAC : Read flag 0x0A[6:5].
Expected Results. | INIT_LDO_DAC = 00 (Pass)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO_DAC register setting (DIO). - TEST_ANA_EN(0x39) = 0x00E - TEST_MODE0(0x1A) = 0x00E TEST pin sweep : 1.5V → 1.0V. VREF_UV Level : TEST voltage when SVO pin is from ‘L’ to ‘H’ UV_LDO_DAC : Read flag 0x0A[6:5].
Expected Results. | VREF_UV MIN / TYP / MAX = 1.25 / 1.35 / 1.45 V UV_LDO_DAC = 01 (Pass)
INIT_LDO_DAC
UV_LDO_DAC

## Slide 35
UV/OV Voltage LDO_DAC Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO_DAC register setting (DIO). - TEST_ANA_EN(0x39) = 0x00E - TEST_MODE0(0x1A) = 0x00D TEST pin sweep : 1.5V → 1.8V. VREF_OV Level : TEST voltage when SVO pin is from ‘L’ to ‘H’ OV_LDO_DAC : Read flag 0x0A[6:5].
Expected Results. | VREF_OV MIN / TYP / MAX = 1.55 / 1.65 / 1.75 V OV_LDO_DAC = 10 (Pass)

## Slide 36
UV/OV Voltage LDO_OSC Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO_OSC register setting (DIO). - TEST_ANA_EN(0x39) = 0x00F TEST pin setting : 1.5V. INIT_LDO_OSC : Read flag 0x0A[4:3].
Expected Results. | INIT_LDO_OSC = 00 (Pass)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO_OSC register setting (DIO). - TEST_ANA_EN(0x39) = 0x00F - TEST_MODE0(0x1A) = 0x00C TEST pin sweep : 1.5V → 1.0V. LDOOSC_UV Level : TEST voltage when SVO pin is from ‘L’ to ‘H’ UV_LDO_OSC : Read flag 0x0A[4:3].
Expected Results. | LDOOSC_UV MIN / TYP / MAX = 1.25 / 1.35 / 1.45 V UV_LDO_OSC = 01 (Pass)
INIT_LDO_OSC
UV_LDO_OSC

## Slide 37
UV/OV Voltage LDO_OSC Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | UV/OV LDO_OSC register setting (DIO). - TEST_ANA_EN(0x39) = 0x00F - TEST_MODE0(0x1A) = 0x00B TEST pin sweep : 1.5V → 1.8V. LDOOSC_OV Level : TEST voltage when SVO pin is from ‘L’ to ‘H’ OV_LDO_OSC : Read flag 0x0A[4:3].
Expected Results. | LDOOSC_OV MIN / TYP / MAX = 1.55 / 1.65 / 1.75 V OV_LDO_OSC = 10 (Pass)

## Slide 38
Open Detection Level Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | Open detection register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - FAULT_CTRL(0x06) = 0x03C - TEST_ANA_EN(0x39) = 0x019 OPEN VREF : Measure TEST pin voltage. Channel repeat : O1~O12, one channel at a time.
Expected Results. | OPEN VREF MIN / TYP / MAX = - / 0.25 / - V
VREF

## Slide 39
Open Detection Level Test
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test mode
Simulation Procedure | Open detection register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - FAULT_CTRL(0x06) = 0x03C - TEST_ANA_EN(0x39) = 0x019 OPEN_FALL : Sweep O1 0.5V → 0V. Record voltage at OPEN_FLAG(0x09[3]) 'L' → 'H' transition. OPEN_RISE : Sweep O1 0V → 0.5V. Record voltage at OPEN_FLAG(0x09[3]) 'H' → 'L' transition. OPEN HYS : Calculate OPEN_RISE − OPEN_FALL. Channel repeat : O1~O12, one channel at a time.
Expected Results. | OPEN HYS MIN / TYP / MAX = - / 0.075 / - V
HYS
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, O1~12 Voltage 1.5V, Temp(TA) = -40 / 27 / 125℃, Normal operation.
Simulation Procedure | Follow Fault_OPEN Level item from 1 to 3. I_O# : Measure O# pin current. Read OPEN register setting(DIO) : - FAULT_STATUS0(0x09) I_O# : Measure O# pin current. Channel repeat : O1~O12, one channel at a time.
Expected Results. | O# current is 0A FAULT_STATUS0 = 0x000 O# current is set-up current.
Function

## Slide 40
FB Detection Level Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test mode
Simulation Procedure | FB detection register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - FAULT_CTRL(0x06) = 0x03C - FB_LEVEL(0x07) = 0x000, 0x049, 0x092, 0x0DB, 0x124, 0x16D, 0x1B6, 0x1FF - TEST_ANA_EN(0x39) = FB1 : 0x016 / FB2 : 0x017 / FB3 : 0x018 FB# VREF : Measure TEST pin voltage. Channel repeat : O1~O12, one channel at a time.
Expected Results. | FB# VREF MIN / TYP / MAX - FB_LEVEL = 0x000 : FB# VREF = - / 0.45 / - V - FB_LEVEL = 0x049 : FB# VREF = - / 0.55 / - V - FB_LEVEL = 0x092 : FB# VREF = - / 0.65 / - V - FB_LEVEL = 0x0DB : FB# VREF = - / 0.75 / - V - FB_LEVEL = 0x124 : FB# VREF = - / 0.90 / - V - FB_LEVEL = 0x16D : FB# VREF = - / 1.05 / - V - FB_LEVEL = 0x1B6 : FB# VREF = - / 1.20 / - V - FB_LEVEL = 0x1FF : FB# VREF = - / 1.35 / - V
Level

## Slide 41
FB Detection Level Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | FB detection register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - FAULT_CTRL(0x06) = 0x03C - FB_LEVEL(0x07) = 0x000, 0x049, 0x092, 0x0DB, 0x124, 0x16D, 0x1B6, 0x1FF - TEST_ANA_EN(0x39) = FB1 : 0x016 / FB2 : 0x017 / FB3 : 0x018 - OP_MODE(0x3F) = FB1 : 0x864 / FB2 : 0x8A4 / FB3 : 0x8E4 FB#_FALL : Sweep O1 1.5V → 0V. Record voltage at FB_FLAG(0x09[#]) 'L' → 'H' transition. ( FB_FLAG 0x09 = FB1 : [0] / FB2 : [1] / FB3 : [2] ) FB#_RISE : Sweep O1 0V → 1.5V. Record voltage at FB_FLAG(0x09[#]) 'H' → 'L' transition. FB# HYS : Calculate FB#_RISE − FB#_FALL. Channel repeat : O1~O12, one channel at a time.
Expected Results. | FB# HYS MIN / TYP / MAX = - / 0.025 / - V
HYS

## Slide 42
SHORT Detection Level Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | SHORT detection register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - FAULT_CTRL(0x06) = 0x03C - SHORT_LEVEL(0x08) = 0x000, 0x049, 0x092, 0x0DB, 0x124, 0x16D, 0x1B6, 0x1FF - TEST_ANA_EN(0x39) = SHORT1 : 0x01A / SHORT2 : 0x01B / SHORT3 : 0x01C SHORT# VREF : Measure TEST pin voltage. Channel repeat : O1~O12, one channel at a time.
Expected Results. | SHORT# VREF MIN / TYP / MAX - SHORT_LEVEL = 0x000 : SHORT# VREF = 2.8 / 3.5 / 4.2 V - SHORT_LEVEL = 0x049 : SHORT# VREF = 5.2 / 6.5 / 7.8 V - SHORT_LEVEL = 0x092 : SHORT# VREF = 7.6 / 9.5 / 11.4 V - SHORT_LEVEL = 0x0DB : SHORT# VREF = 10 / 12.5 / 15 V - SHORT_LEVEL = 0x124 : SHORT# VREF = 13.2 / 16.5 / 19.8 V - SHORT_LEVEL = 0x16D : SHORT# VREF = 13.2 / 16.5 / 19.8 V - SHORT_LEVEL = 0x1B6 : SHORT# VREF = 13.2 / 16.5 / 19.8 V - SHORT_LEVEL = 0x1FF : SHORT# VREF = 13.2 / 16.5 / 19.8 V
Level

## Slide 43
SHORT Detection Level Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test mode
Simulation Procedure | SHORT detection register setting (DIO). - CHANNEL_ENABLE(0x05) = 0x001, 0x002, … , 0x400, 0x800 (12 One hot, 1 Ch Only) - FAULT_CTRL(0x06) = 0x03C - SHORT_LEVEL(0x08) = 0x000, 0x049, 0x092, 0x0DB, 0x124, 0x16D, 0x1B6, 0x1FF - TEST_ANA_EN(0x39) = SHORT1 : 0x01A / SHORT2 : 0x01B / SHORT3 : 0x01C - OP_MODE(0x3F) = SHORT1 : 0x864 / SHORT2 : 0x8A4 / SHORT3 : 0x8E4 SHORT#_FALL : Sweep O1 1.5V → 0V. Record voltage at SHORT_FLAG(0x09[4]) 'L' → 'H' transition. SHORT#_RISE : Sweep O1 0V → 1.5V. Record voltage at SHORT_FLAG(0x09[4]) 'H' → 'L' transition. SHORT# HYS : Calculate SHORT#_RISE − SHORT#_FALL. Channel repeat : O1~O12, one channel at a time.
Expected Results. | SHORT# HYS MIN / TYP / MAX = - / 0.065 / - V
HYS
Function
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, O1~12 Voltage 1.5V, Temp(TA) = -40 / 27 / 125℃, Normal operation.
Simulation Procedure | Follow Fault_SHORT Level item from 1 to 3. I_O# : Measure O# pin current. Read SHORT register setting(DIO) - FAULT_STATUS0(0x09) I_O# : Measure O# pin current. Channel repeat : O1~O12, one channel at a time.
Expected Results. | O# current is 0A FAULT_STATUS0 = 0x000 O# current is set-up current.

## Slide 44
Fault Flag(Initial) Test (1)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 0.05V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | Fault flag register setting (DIO). - CHANNEL_ENABLE(0x05) = 0xFFF - FAULT_CTRL(0x06) = 0x03C - FB_LEVEL(0x07) = 0x16D - OP_MODE(0x3F) = FB1 : 0x864 / FB2 : 0x8A4 / FB3 : 0x8E4 FAULT_INIT : Read flag 0x09[4:0]. FB mode repeat : FB1~FB3, one mode at a time.
Expected Results. | FAULT_INIT (0x09[4:3]) = 01 (Pass) FAULT_INIT (0x09[2:0]) : FB3([2]) / FB2([1]) / FB1([0]) = 1 (Pass)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 0.7V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | Fault flag register setting (DIO). - CHANNEL_ENABLE(0x05) = 0xFFF - FAULT_CTRL(0x06) = 0x03C - FB_LEVEL(0x07) = 0x16D - OP_MODE(0x3F) = FB1 : 0x864 / FB2 : 0x8A4 / FB3 : 0x8E4 FAULT_OPEN : Read flag 0x09[4:0]. FB mode repeat : FB1~FB3, one mode at a time.
Expected Results. | FAULT_OPEN (0x09[4:3]) = 00 (Pass) FAULT_OPEN (0x09[2:0]) : FB3([2]) / FB2([1]) / FB1([0]) = 1 (Pass)
FAULT_INIT
FAULT_OPEN

## Slide 45
Fault Flag(Initial) Test (2)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 2V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | Fault flag register setting (DIO). - CHANNEL_ENABLE(0x05) = 0xFFF - FAULT_CTRL(0x06) = 0x03C - FB_LEVEL(0x07) = 0x16D - OP_MODE(0x3F) = FB1 : 0x864 / FB2 : 0x8A4 / FB3 : 0x8E4 FAULT_FB : Read flag 0x09[4:0]. FB mode repeat : FB1~FB3, one mode at a time.
Expected Results. | FAULT_FB (0x09[4:3]) = 00 (Pass) FAULT_FB (0x09[2:0]) : FB3([2]) / FB2([1]) / FB1([0]) = 0 (Pass)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, VLED Voltage 5V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | Fault flag register setting (DIO). - CHANNEL_ENABLE(0x05) = 0xFFF - FAULT_CTRL(0x06) = 0x03C - FB_LEVEL(0x07) = 0x16D - OP_MODE(0x3F) = FB1 : 0x864 / FB2 : 0x8A4 / FB3 : 0x8E4 FAULT_SHORT : Read flag 0x09[4:0]. FB mode repeat : FB1~FB3, one mode at a time.
Expected Results. | FAULT_SHORT (0x09[4:3]) = 10 (Pass) FAULT_SHORT (0x09[2:0]) : FB3([2]) / FB2([1]) / FB1([0]) = 0 (Pass)
FAULT_FB
FAULT_SHORT

## Slide 46
BIST (Build in Self TEST)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V, Temp(TA) = -40 / 27 / 125℃ , Analog Test Mode
Simulation Procedure | BIST register setting (DIO). - BIST(0x19) = 0x800 BIST : Read flag 0x19 after 50μs.
Expected Results. | BIST(0x19) = 0x002. it is passed. (Fail : BIST(0x19) = 0x003)

## Slide 47
HVS
Verification Method | Simulation
Preconditions(TEST Condition) | Temp(TA) = -40 / 27 / 125℃
Simulation Procedure | HVS : Force VDD = 6.2V for 0.5s. Re-Check TEST item : IIL, IIH, IOZL, IOZH, IDDS, IDDD, IDDQ_A, IDDQ_D, IOUT_3P_P1_VFY, IOUT_3P_P2_VFY, IOUT_3P_P3_VFY Name the result : (ITEM)2 Δ_(ITEM) : Calculate ( 1ST result − 2ND result ) / 1ST result × 100.
Expected Results. | Δ_(ITEM) MIN / TYP / MAX = -5 / 0 / 5 %

## Slide 48
OTP_Write (e-fuse)
Verification Method | Simulation
Preconditions(TEST Condition) | VDD Voltage 3.3V -> 5.5V Power up Temp(TA) = -40℃/27℃/125℃
Simulation Procedure | Set register for OTP_Write (e-fuse) - TEST CONTROL (0xF0) = 0x0008 - OTP RD/PROG (0xF3) = 0x0001 Keep SCLK more than 2000 cycles Power OFF(Erased date in register area Power ON(3.3V) -> e-fused codes are downloaded to register area
Expected Results. | OTP programming is completed and e-fused codes are downloaded to register area after Power ON.

## Slide 49
PWM Test (TBD)
Verification Method | Simulation
Preconditions(TEST Condition) | 
Simulation Procedure | 
Expected Results. |