## Slide 1
IP805 Test Plan Documentation
2026.01.28
전원구동반도체팀
작성자 : 최지수 연구원

## Slide 2
목 차
Trimming guide
Trimmed Parameters
Datasheet EC Parameters

## Slide 3
목 차
Trimming guide
Trimmed Parameters
Datasheet EC Parameters

## Slide 4
Trim parameter & Trim bit register map
< Trim Parameters >
< Trim bit Register map >

## Slide 5
Trim Mode Register Map
* IP805_Register_ADIF_TOP  Sheet “Testmode Reg.Table” 확인

## Slide 6
Initial Pin Conditions
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V

## Slide 7
ATB_1 MODE
Entry Sequence
Common Test Sequence
<ATB1 Entry>
0xE8 : 0x100 (TM_ANA_TEST_EN)
0xE7 : 0x004 (TM_ATB1_EN)
Test mode Enter (I2C mode)
TM pin : 05V 인가
(100us Delay)
GPIO0 /ADDR2 pin : 0V 인가
20us delay 이후 i2c write(TM Unlock)
0xE1 : 0x800 (TEST_E=1)
RFREQ pin = N.C
VIN/EN pin = 12V
(4ms Delay)
ATB_2 MODE
Entry Sequence
<ATB2 Entry>
0xE8 : 0x100 (TM_ANA_TEST_EN)
0xE7 : 0x001 (TM_ATB2_EN)
RFREQ pin = N.C
VIN/EN pin = 12V
(4ms Delay)
DTB MODE
Entry Sequence
<DTB1/2 Entry>
0xE5 : 0x040 (DTB1_MUX_EN)
0xE6 : 0x040 (DTB2_MUX_EN)
RFREQ pin = N.C
VIN/EN pin = 12V
(4ms Delay)
<GPIO1/2 Output Mode>
0x08 : 0x113 (GPIO1/2 Output Mode)
기본 Test Set은 아래와 같고, 추가적인 내용이 필요한 경우 따로 각 Item Plan에 내용 명시할 예정 (EX : RFREQ pin : 50kΩ 설치)
I2C 통신 자체는 POWER ON 이후, “4.5ms 이후” 에 모든 I2C Command Sequence 시작 실시
Test mode Enter (I2C mode)
TM pin : 05V 인가
(100us Delay)
GPIO0 /ADDR2 pin : 0V 인가
20us delay 이후 i2c write(TM Unlock)
0xE1 : 0x800 (TEST_E=1)
Test mode Enter (I2C mode)
TM pin : 05V 인가
(100us Delay)
GPIO0 /ADDR2 pin : 0V 인가
20us delay 이후 i2c write(TM Unlock)
0xE1 : 0x800 (TEST_E=1)

## Slide 8
Normal Test Mode
Entry Sequence
Common Test Sequence
VIN/EN pin = 12V
(4ms Delay)
기본 Test Set은 아래와 같고, 추가적인 내용이 필요한 경우 따로 각 Item Plan에 내용 명시할 예정 (EX : RFREQ pin : 50kΩ 설치)
I2C 통신 자체는 POWER ON 이후, “4.5ms 이후” 에 모든 I2C Command Sequence 시작 실시
Test mode Enter (I2C mode)
TM pin : 05V 인가
(100us Delay)
GPIO0 /ADDR2 pin : 0V 인가
20us delay 이후 i2c write(TM Unlock)
0xE1 : 0x800 (TEST_E=1)

## Slide 9
목 차
Trimming guide
Trimmed Parameters
Datasheet EC Parameters

## Slide 10
Trim #. Trim Basic Sequence
초기 데이터 측정 (PRE) - V/I/Hz 등
Target 과의 차이 계산 (PRE_ERR) - %
1차 - LSB 기반의 CODE 산출 / 적용 (MID_CODE) - HEX
1차 CODE값 적용한 데이터 측정 (MID) - V/I/Hz 등
Target 과의 차이 계산 (MID_ERR) - %
2차 - LSB 기반의 CODE 산출 / 적용 (PST_CODE) - HEX
2차 CODE 적용 (PST_CODE_SIGN)
2차 CODE 적용한 데이터 측정 (PST) - V/I/Hz 등
Target 과의 차이 계산 (PST_ERR) - %
(+/- 0.5 LSB 안으로 들어와야 함)
Trim Table Extraction
(초기에만 Sample 별 LSB 측정을 위해 시행필요)

## Slide 11
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #0. ATB1_BUFFER offset check Pin condition

## Slide 12
ATB_1 MODE
Entry Sequence
Trim #0. ATB1_BUFFER offset check
<VREF Monitor>
0xE0 : 0x008 (TM_ATB_BIAS_EN)
0xE0 : 0x00b (VREF_1p2v select)
①GPIO1 pin Voltage 측정 (VREF_1p2v w/o Buffer offset 출력)
<ATB1_BUFFER ON>
0xE7 : 0x00c (TM_ATB1_BUF_EN Enable)
②GPIO1 pin Voltage 측정 (VREF_1p2v w/ Buffer offset 출력)
ATB1_Buffer offset = ② - ①
=ATB_OFST1

## Slide 13
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #1. BGR Trim Pin Condition

## Slide 14
Trim #1. BGR Trim (ZTC Trim)
<BGR Monitor>
0xE0 : 0x008 (TM_ATB_BIAS_EN)
0xE0 : 0x009 (VBG_1p2_lvl select)
READ 0xF2 [4:0] (BGR 1.2vZTC Trim code)
GPIO1 pin Voltage 측정  VBG_pre0 (VBG_1p2v_lvl 출력)
<BGR Trim 실행>
0xF2 : 0x000 ~ 0x01f (1.2V ZTC target / 1LSB: +/-4.5mV)
1ST Turn : WRITE 0xF2 MID CODE (1st try target 1.2V)
2nd Turn : WRITE 0xF2 FINE CODE (should be 1.2V +/-0.5LSB)
ATB_1 MODE
Entry Sequence
BGR Double Trim 실행
(2nd Turn으로 이동)
<ATB1_BUFFER ON>
0xE7 : 0x00c (TM_ATB1_BUF_EN Enable)
<내부 BGR 전압 추정치 계산>
VBG_pre0 – ATB_OFST1 (Trim#0 결과) = VBG_pre1
0xF2 [4:0] TRIM_BG | TRIM RESULT | 0xF2 [4:0] TRIM_BG | TRIM RESULT
0 | 1.2 | 16 | 1.27
1 | 1.196 | 17 | 1.266
2 | 1.191 | 18 | 1.261
3 | 1.187 | 19 | 1.257
4 | 1.183 | 20 | 1.253
5 | 1.178 | 21 | 1.248
6 | 1.174 | 22 | 1.244
7 | 1.169 | 23 | 1.24
8 | 1.165 | 24 | 1.235
9 | 1.161 | 25 | 1.231
10 | 1.156 | 26 | 1.226
11 | 1.152 | 27 | 1.222
12 | 1.148 | 28 | 1.218
13 | 1.143 | 29 | 1.213
14 | 1.139 | 30 | 1.209
15 | 1.134 | 31 | 1.205

## Slide 15
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #2. IREF Trim Pin Condition

## Slide 16
ATB_1 MODE
Entry Sequence
Trim #2. IREF Trim
<IREF Monitor>
0xE0 : 0x008 (TM_ATB_BIAS_EN)
0xE0 : 0x00a (IREF_TEST_3uA select)
READ 0xF3 [7:4] (IREF Trim code)
GPIO1 pin Current 측정( 2V BIAS) (IREF_TEST_3uA sink)
<IREF Trim 실행>
0xF3 : 0x000 ~ 0x0f0 (3uA target / 1LSB: +/-120nA)
1ST Turn : WRITE 0xF3 MID CODE (1st try target 3uA)
2nd Turn : WRITE 0xF3 FINE CODE (should be 3uA +/-0.5LSB)
IREF Double Trim 실행
(2nd Turn으로 이동)
0xF3 [7:4] TRIM_IREF | TRIM RESULT
0 | 3u
1 | 3.12u
2 | 3.25u
3 | 3.39u
4 | 3.55u
5 | 3.72u
6 | 3.91u
7 | 4.12u
8 | 2.29u
9 | 2.36u
10 | 2.43u
11 | 2.51u
12 | 2.59u
13 | 2.68u
14 | 2.78u
15 | 2.88u

## Slide 17
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #3. VREF1P2V Trim Pin Condition

## Slide 18
Trim #3. VREF1P2V Trim
<VREF Monitor>
0xE0 : 0x008 (TM_ATB_BIAS_EN)
0xE0 : 0x00b (VREF_1p2v select)
READ 0xF2 [11:8] (BGR Level Trim code)
GPIO1 pin Voltage 측정 (VREF_1p2v 출력 1.2V target)
ATB_1 MODE
Entry Sequence
<VBG_1p2_lvl코드로 VREF_1p2v Offset TRIM 실행>
0xF2 : 0x0-- ~ 0xf-- (1.2V Level target / 1LSB: +/-5mV)
1ST Turn : WRITE 0xF2 MID CODE (1st try target 1.2V)
2nd Turn : WRITE 0xF2 FINE CODE (should be 1.2V +/-0.5LSB)
BGR Double Trim 실행
(2nd Turn으로 이동)
0xF2 [11:8] TRIM_BG_LVL | TRIM RESULT
0 | 1.2
1 | 1.205
2 | 1.21
3 | 1.215
4 | 1.22
5 | 1.225
6 | 1.23
7 | 1.235
8 | 1.16
9 | 1.165
10 | 1.17
11 | 1.175
12 | 1.18
13 | 1.185
14 | 1.19
15 | 1.195

## Slide 19
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #4. IPTAT Trim Pin Condition

## Slide 20
Trim #4. IPTAT Trim
<IPTAT Monitor>
0xE0 : 0x008 (TM_ATB_BIAS_EN)
0xE0 : 0x00c (IPTAT_TEST_1uA select)
READ 0xF3 [3:0] (IPTAT Trim code)
GPIO1 pin Current 측정 (2V BIAS) (IPTAT_TEST_1uA sink)
<IPTAT Trim 실행>
0xF3 : 0x--0 ~ 0x--f (1uA target / 1LSB: +/-65nA)
1ST Turn : WRITE 0xF3 MID CODE (1st try target 1uA)
2nd Turn : WRITE 0xF3 FINE CODE (should be 1uA +/-0.5LSB)
ATB_1 MODE
Entry Sequence
IPTAT Double Trim 실행
(2nd Turn으로 이동)
0xF3 [3:0] TRIM_IPTAT | TRIM RESULT
0 | 1.01u
1 | 1.08u
2 | 1.16u
3 | 1.25u
4 | 1.37u
5 | 1.50u
6 | 1.67u
7 | 1.88u
8 | 0.67u
9 | 0.70u
10 | 0.73u
11 | 0.76u
12 | 0.80u
13 | 0.85u
14 | 0.89u
15 | 0.95u

## Slide 21
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #5. 1P5V_LDO Trim Pin Condition

## Slide 22
Trim #5. 1P5V_LDO Trim
<1P5V_LDO Monitor>
0xE7 : 0x041 (ATB2_1P5V_SENSE select)
READ 0xF2 [7:5] (1P5V_LDO Trim code)
GPIO2 pin Voltage 측정 (VPD_SENSE 출력)
<1P5V_LDO Trim 실행>
0xF2 : 0x-0- ~ 0x-f- (1.5V target / 1LSB: +/-4mV)
1ST Turn : WRITE 0xF2 MID CODE (1st try target 1.5V)
2nd Turn : WRITE 0xF2 FINE CODE (should be 1.5V +/-0.5LSB)
ATB_2 MODE
Entry Sequence
1P5V_LDO Double Trim 실행
(2nd Turn으로 이동)
0xF2 [7:5] TRIM_VLDO | TRIM RESULT
0 | 1.5
1 | 1.504
2 | 1.508
3 | 1.512
4 | 1.485
5 | 1.489
6 | 1.493
7 | 1.496

## Slide 23
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #6. LP_OSC Trim Pin Condition

## Slide 24
Trim #6. LP_OSC Trim
<LP_OSC Monitor>
0xE5 : 0x056 (DTB_LP_CLK select)
READ 0xF3 [11:8] (LP_OSC Trim code)
GPIO1 pin Frequency 측정 (LP_CLK 출력)
<LP_OSC Trim 실행>
0xF3 : 0x0-- ~ 0xF-- (100kHz target / 1LSB: +/-6kHz)
1ST Turn : WRITE 0xF3 MID CODE (1st try target 100kHz)
2nd Turn : WRITE 0xF2 FINE CODE (should be 100kHz +/-0.5LSB)
DTB MODE
Entry Sequence
LP_OSC Double Trim 실행
(2nd Turn으로 이동)
0xF3 [11:8] TRIM_LP_OSC | TRIM RESULT
0 | 102k
1 | 108k
2 | 114k
3 | 120k
4 | 126k
5 | 132k
6 | 138k
7 | 143k
8 | 55k
9 | 61k
10 | 67k
11 | 73k
12 | 79k
13 | 85k
14 | 91k
15 | 97k

## Slide 25
 |  |  | : Measure point |  |  |  | : Sweep point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MODE | Pin Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | Pin Name | VIN | EN | VDD5 | ADDR0 | ADDR1 | ADDR2 | GPIO0 | GPIO1 | GPIO2 | AGND | CANH | CANL | GND_ IO | SIO_P | SIO_N | TM | RFREQ | VBCK_IO | BOOT | SW2 | SW1 | VIN_ SW2 | VIN_ SW1 | PGND
ATB_1 | Before Trim #0 : ATB_Buffer offest check | 12V | 12V | NC | NC | 5V | 0V | NC | Measure |  | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #1 : BGR ZTC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #2 : IREF Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #3 : VREF1P2V Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #4 : IPTAT Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
ATB_2 | Trim #5 : 1P5VLDO Trim | 12V | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
DTB | Trim #6 : LP_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | Trim #7 : 32M_OSC Trim | 12V | 12V | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
I2C | EC #1 : Current consumption | 12V | Sweep | NC | NC | 5V | 0V | NC | NC | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | 5V | NC | 0V | 0V | 12V(I Meas.) |  | 0V
DTB | EC #2: Over-Voltage monitoring | Sweep | 12V | NC | NC | 5V | 0V | NC | NC | Meas | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #3: Enable Input | 12V | Sweep | NC | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
 | EC #4: VDD5 LDO | 12V | 12V | Sweep& Meas | NC | 5V | 0V | NC | Meas | NC | 0V | NC | NC | 0V | NC | NC | 0V | NC | NC | NC | 0V | 0V | 12V | 12V | 0V
Trim #7. 32M OSC Trim Pin Condition

## Slide 26
Trim #7. 32M_OSC Trim
<32M_OSC Monitor>
0xE5 : 0x05a (DTB_MCLK_DIV_32 select)
READ 0xF4 [7:0] (32M_OSC Trim code)
GPIO1 pin Frequency 측정 (MCLK_DIV_32출력-1MHz)
<32M_OSC Trim 수행)
0xF4 : 0x000 ~ 0x0FF (32MHz target / 1LSB: +/-100KHz)
 32분주 되어 1MHz로 출력 (1MHz target / 1LSB: +/-3.125kHz)
1ST Turn : WRITE 0xF4 MID CODE (1st try target 1MHz)
2nd Turn : WRITE 0xF4 FINE CODE (should be 1MHz +/-0.5LSB)
DTB MODE
Entry Sequence
32M OSC Double Trim 실행
(2nd Turn으로 이동)
0xF4 [7:0] TRIM_32MOSC | Internal OSC Freq. | 32분주 RESULT
0 | 32M | 1000K
1 | 31.9M | 996.87K
… | … | 
127 | 18.7M | 584.37K
128 | 32M | 1000K
… | … | 
254 | 44.4M | 1387.5K
255 | 44.5M | 1390.6K

## Slide 27
Trim #9. BUCK_OSC (OSC_TOP_CLK) Trim
<SSC Function OFF & BUCK_OSC Monitor>
0x07 : 0x0BD (SSC Function OFF)
0xE5 : 0x058 (DTB_OSC_TOP_CLK_DIV_4)
READ 0xF5 [3:0] (OSC_BIAS Trim code, default : 0)
GPIO1 pin Frequency 측정 (OSC_TOP_CLK_DIV_4출력 - 550kHz)
<BUCK_OSC Trim 실행>
0xF5 : 0x--0 ~ 0x--F (2.2MHz target / 1LSB: +/-120kHz)
 4분주 되어 550kHz로 출력 (550kHz target / 1LSB: +/-30kHz)
1ST Turn : WRITE 0xF4 MID CODE (1st try target 550kHz)
2nd Turn : WRITE 0xF4 FINE CODE (should be 550kHz +/-0.5LSB)
BUCK_OSC
Double Trim 실행
(2nd Turn으로 이동)
DTB MODE
Entry Sequence
<DTB1/2 Entry>
0xE5 : 0x040 (DTB1_MUX_EN)
0xE6 : 0x040 (DTB2_MUX_EN)
RFREQ pin = 50kΩ 연결?
VIN/EN pin = 12V
<GPIO1/2 Output Mode>
0x08 : 0x113 (GPIO1/2 Output Mode)
Test mode Enter (I2C mode)
TM pin : 05V 인가
(100us Delay)
GPIO0 /ADDR2 pin : 0V 인가
20us delay 이후 i2c write(TM Unlock)
0xE1 : 0x800 (TEST_E=1)
저항 연결하는 시점 정의 필요

## Slide 28
Trim #9. BUCK_OSC (OSC_TOP_CLK) Trim
0xF5 [3:0] TRIM_OSC_TOP | OSC_FREQ (MHz) | DIV_4 (MHz)
0000 (default) | 2.201 | 0.550
0001 | 2.088 | 0.522
0010 | 1.974 | 0.494
0011 | 1.858 | 0.465
0100 | 1.739 | 0.435
0101 | 1.617 | 0.404
0110 | 1.492 | 0.373
0111 | 1.364 | 0.341
1000 | 3.023 | 0.756
1001 | 2.924 | 0.731
1010 | 2.827 | 0.707
1011 | 2.728 | 0.682
1100 | 2.626 | 0.657
1101 | 2.522 | 0.631
1110 | 2.417 | 0.604
1111 | 2.310 | 0.578
RFREQ@50kohm
0xF5 [3:0] TRIM_OSC_TOP | OSC_FREQ (MHz) | DIV_4 (kHz)
0000 (default) | 458.8 | 114.7
0001 | 432.2 | 108.1
0010 | 405.3 | 101.3
0011 | 378.3 | 94.6
0100 | 351.0 | 87.8
0101 | 323.4 | 80.9
0110 | 295.7 | 73.9
0111 | 267.8 | 66.9
1000 | 665.9 | 166.5
1001 | 640.5 | 160.1
1010 | 615.0 | 153.7
1011 | 589.4 | 147.3
1100 | 563.6 | 140.9
1101 | 537.7 | 134.4
1110 | 511.5 | 127.9
1111 | 485.4 | 121.4
RFREQ@300kohm

## Slide 29
Trim #10. LVDS TX Current Trim
<LVDS TX Current Trim 실행>
0xF7 : 0x--0 ~ 0x--7 (1.5mA target / 1LSB: +/-165uA)
Voltage 를 측정하여 200 ohm 으로 나누어 전류 치 역산 (V = IR)
1ST Turn : WRITE 0xF6 MID CODE (1st try target 1.5mA)
2nd Turn : WRITE 0xF6 FINE CODE (should be 1.5mA +/-0.5LSB)
LVDS_TX_Current
Double Trim 실행
(2nd Turn으로 이동)
< LVDS TX Current Measurement Setting>
0xE3 : 0x090 (Only LVDS TX_High ON)
“SIO_P : High / SIO_N : Low”
Normal I2C Test Mode
Entry Sequence
저항 200ohm 연결 릴레이 ON
(SIO_P ↔ SIO_N)
SIO_P ~ SIO_N 사이 전압 측정
(V=IR, Measure V = I * ideal 200 ohm)
0xF6 [2:0] TRIM_LVDS_TX | TRIM RESULT
000 (default) | 1.493 mA
001 | 1.657 mA
010 | 1.821 mA
011 | 1.985 mA
100 | 0.832 mA
101 | 0.997 mA
110 | 1.163 mA
111 | 1.328 mA

## Slide 30
Trim #11. LVDS RX RES Trim
<LVDS RX Term_res Trim 실행>
0xF7 : 0x-0- ~ 0x-3- (200ohm target / 1LSB: +/-18ohm / 2bit)
SIO_P 전압을 측정하여 역산 (R = Vdiff / Isource )
=> (1.2V - 1.0V) = Measurement Current * Target Res.
=> 200mV / 1mA = 200ohm (target)
WRITE 0xF6 FINE CODE (should be 200ohm +/-0.5LSB)
< LVDS RX RES Measurement Setting>
0xE3 : 0x060 (Only LVDS RX ON)
SIO_N : 1.0V Force (전압 인가)
Normal I2C Test Mode
Entry Sequence
0xF6 [5:4] TRIM_LVDS_RX_RES | TRIM RESULT
0 | 203 ohm
1 | 184 ohm
2 | 221 ohm
3 | 192 ohm
SIO_P : 1mA Sourcing(전류 인가)
(“SIO_P 전압 측정값” – 1V)/1mA = “RX_Term_저항값”

## Slide 31
Trim #12. TMON_OFFSET_TRIM - Pin Conditions

## Slide 32
Trim #12. TMON_OFFSET_TRIM
ATB_2 MODE
Entry Sequence
GPIO2 pin Voltage 측정
(TMON_OFST 1V 출력)
<TMON_OFFSET Trim 실행>
측정값(V) – 1V_target = 오차 측정
오차 / 55mV(1LSB) = (Trim Code 찾기, 소수점 반올림)
0xF5 : 0x000 ~ 0x0f0 (1.0V target / 1LSB: +/-55mV)
 (1V- 0.5*LSB) < 최종값 < (1V+ 0.5*LSB)
<ATB2 SPARE_SEL >
0xE7 : 0x800 (TM_GAIN_TMON_EN)
+ 10us Delay
0xE7 : 0x861 (TM_ATB2_SPARE_SEL<10>)
GPIO2 pin Voltage 측정 (TMON 출력)
ROOM TEMP = 25 Degree
TMON_OFFSET
Double Trim 실행
(2nd Turn으로 이동)
0xF5 [7:4] TRIM_OFST_TMON | TRIM RESULT
0 | 1.005
1 | 0.951
2 | 0.893
3 | 0.839
4 | 0.777
5 | 0.723
6 | 0.665
7 | 0.610
8 | 1.468
9 | 1.414
10 | 1.356
11 | 1.302
12 | 1.240
13 | 1.185
14 | 1.127
15 | 1.073
<ATB2 SPARE_SEL >
0xE7 : 0x071 (TM_ATB2_SPARE_SEL<11>)
0xF5 (Read TMON_OFFSET Trim code)
GPIO2 pin Voltage 측정
(TMON_GAIN 1V 전압) 단순 산포 측정용