## Slide 1
XC24
SPI FAULT STATUS & CONTROL
Bits | Fields | Descriptions
15:8 | ACC_COUNTER | These bits show how many times the access from a Host to a XC has been executed on SPI bus. Therefore, the next access number should be sent as same as (ACC_COUNTER + 1) after sending last data bit. If the value is not same under the SPI_ACC_CNT_ ERR_DET_EN set, then the INT_ACC_CNT_ERR_SRC bit will be set under the INT_ACC_CNT_ERR_EN set. This counter incremented with roll-over and reset to ‘0’ after power on/off.
5 | ACC_CNT_ERR | Read-Only. This bit shows whether the access counter value error has been happened or not. Auto-cleared after a readout.
4 | PARITY_ERR | Read-Only. This bit shows whether the parity error has been happened or not. Auto-cleared after a readout. ( Error check type is odd. Parity bit is ‘1’ if number of ones for each 16 data bit is odd. Parity information should be sent after ACC_COUNTER and additional 5 SCLK )
1 | ACC_CNT_ERR_DET_EN | This bit enables the detection whether the access count value from a Host on SPI transaction is correct.
0 | PARITY_ERR_DET_EN | This bit enables the detection whether the parity value of SPI data stream from a Host is correct. The parity is expressed with Odd parity for SPI data stream.
Bits | Fields | Descriptions
14:12 | SPREAD_RANGE_A | Refer to the Table 9.
11 | LD_B_RD_CLK_SEL | ‘0’ Internal OSC ‘1’ External MCLK
10 | SERIALIZE_CLK_STS | Read-Only. ‘0’ Internal OSC ‘1’ External MCLK
9:8 | SPREAD_RANGE_D | Refer to the Table 9.
7:6 | SPREAD_SPEED | Internal OSC clock spread period. Refer to the Table 9. ‘00’ x1, ‘01’ x2, ‘10’ x4, ‘11’ x8
5:4 | SPREAD_DIR | ‘00’ +%, ‘01’ -%, ‘10’ ±%
3 | SERIALIZE_CLK_SEL | ‘0’ Internal OSC ‘1’ External MCLK Read protection as ‘1’. Status can be read by SERIALIZE_CLK_STS
2 | OSC_SPREAD_EN | Spread of internal OSC clock. (The external MCLK can not be spread) Refer to the Figure 22. for the clock scheme. ‘0’ Not Spread ‘1’ Spread
1 | SERIALIZER_SKEW_EN | ‘0’ Skew disabled between Serializers ‘1’ Skew enabled
0 | MCLK_MODE (Read-Only) | ‘0’ Internal OSC (Default) ‘1’ External MCLK (auto-changed if the ext. MCLK is entered)
CLK CONTROL 1
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6
‘h1A | RO | ACC_COUNTER [7:0] |  |  |  |  |  |  |  | x | x
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8
‘h1B | 0x0000 | x | SPREAD_RANGE_A[2:0] |  |  | LD_B_RD_CLK_SEL | SERIALIZE_CLK_STATUS | SPREAD_RANGE_D[1:0] | 
Addr | Default | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h1B | 0x0000 | SPREAD_SPEED[1:0] |  | SPREAD_DIR[1:0] |  | SERIALIZE_CLK_SEL | OSC_SPREAD_EN | SERIALIZER_SKEW_EN | MCLK_MODE
Addr | Default | B5 | B4 | B3 | B2 | B1 | B0
‘h1A | 0x0 | ACC_CNT_ERR | PARITY_ERR | x | x | ACC_CNT_ERR_DET_EN | PARITY_ERR_DET_EN

## Slide 2
XC24
Bits | Fields | Descriptions
15:7 | DAC_INC_HOLD_ LIMIT | This value determines the number of frames without the FB assertion in which the current DAC stays within the range, (CURR_TGR_DAC – the current DAC) < DAC_INC _HOLD_THRESHOLD. If the counted value is same as this value, then the DAC OUT will be held at the current DAC value so that the DAC OUT will be not increased any more. This function is useful in case that the PWM data are kept to 0 for a lot of frames.
6:0 | DAC_INT4 | This value determines the amount of the DAC OUT increasement in case that the current DAC OUT stays within the range, the current DAC OUT < (CURR_TGT_DAC – SOA_P3) without any FB assertion. The increment value is added whenever the FB is not asserted every frame. Refer to the Figure 28.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h53 | 0x0820 | DAC_INC_HOLD_LIMIT [8:0] |  |  |  |  |  |  |  |  | DAC_INT4 [6:0] |  |  |  |  |  | 
DAC DECREMENT & INC WAIT
Bits | Fields | Descriptions
14:8 | DAC_DEC1 | This value determines the amount of the DAC OUT decrement whenever the FB is asserted. The DAC_DEC1_MODE bit allows two modes choice, one is to decrease by the amount of DAC_DEC1, and the other is to decrease by the amount of arithmetic exponential of DAC_DEC1. Refer to the Figure 28.
6:0 | DAC_INC1_WAIT | This value determines the number of frames that the DAC OUT increment execution will wait with the FB deassertion. In case the value is set to 2, then the DAC OUT will be increased by the DAC_INC1 at the third frame if three successive frames are kept without the FB assertion. If the value is set to 0, then the DAC OUT will be increased immediately whenever the frame is without a FB assertion.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h54 | 0x0400 | x | DAC_DEC1 [6:0] |  |  |  |  |  |  | x | DAC_INC1_WAIT [6:0] |  |  |  |  |  | 
DAC INCREMENT HOLD THRESHOLD
Bits | Fields | Descriptions
9 | SIGNED | The signed bit of the DAC_INC_HOLD_THRESHOLD. Set negative value as ‘1’.
8:0 | DAC_INC_HOLD_ THRESHOLD | This determines the range that the DAC_INC_HOLD_LIMIT counter will work. Refer to the DAC_INC_HOLD_LIMIT and the DAC_HOLD_EN bit in details.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h55 | 0x020A | x | x | x | x | x | x | SIGNED | DAC_INC_HOLD_THRESHOLD [8:0] |  |  |  |  |  |  |  | 
DAC INCREMENT 2 & HOLD_LIMIT

## Slide 3
XC24
DAC FB VALID CNT
Bits | Fields | Descriptions
15:0 | DAC_FB_VAILD_CNT | This is for test only. This value shows the counted value, MCLK x 4, for one frame.
DAC INC HOLD/WAIT CNT
Bits | Fields | Descriptions
15:8 | DAC_INC_HOLD_LIMIT_CNT | This is for test only.
6:0 | DAC_INC1_WAIT_CNT | This is for test only.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h5D | RO | DAC_FB_VAILD_CNT [17:2] |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h5E | RO | DAC_INC_HOLD_LIMT_CNT [7:0] |  |  |  |  |  |  |  | x | DAC_INC1_WAIT_CNT [6:0] |  |  |  |  |  | 
R2
Bits | Fields | Descriptions
12 | SIGNED | The signed bit of the R2 with representing negative as 1. This is for test only.
11:0 | R2 | = (CURR_TGT_DAC – the current DAC)
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h5F | RO | x | x | x | SIGNED | R2 [11:0] |  |  |  |  |  |  |  |  |  |  |