## Slide 1
Protocol Sequence
For
Each Test Items

## Slide 2
 | Protocol Sequence |  |  |  |  | 
 | 1. Test CH Dependency |  |  |  |  | 
 | Sequence | command | data | To Do | Note | 
 | 1 | Test CH Dependency | 0 | 1. Compare the LED brightness between all LEDs on and individual LEDs on. 2. No brightness difference is allowed between the two conditions. |  | 
 | 2. Test SCAN No. |  |  |  |  | 
 | Sequence | command | data | To Do | Note | 
 | 1 | Initial | 0 | 1. The pattern is 1.0s ON → 0.1s OFF, repeated. 2. No brightness difference is allowed between ON-OFF cycles. | 1. There is no history of this type of defect occurring. (26.04.20) 2. After 17s, test is stopped. | 
 | 2 | Bar On Select | 0 |  |  | 
 | 3 | Test SCAN No. | 1 |  |  | 
 | 3. Test Line Delay |  |  |  |  | 
 | Sequence | command | data | To Do | Note | 
 | 1 | Initial | 0 | 1. The brightness must be maintained without any variation. 2. OFF or low brightness for more than 0.5 seconds is considered a defect. | 1. Minor flicker is a transient effect caused by line delay switching. 2. After 7s, test is stopped. | 
 | 2 | Bar On Select | 0 |  |  | 
 | 3 | Test Line Delay | 1 |  |  | 

## Slide 3
Test
CH Dependency

## Slide 4
1. Test CH Dependency |  |  |  |  |  |  |  | 
case) normal |  |  |  |  |  |  |  | 
Sequence | XD #1 |  |  |  | XD #2 |  |  | 
 | LED 1 | LED 2 | LED 3 | LED 4 | LED 5 | LED 6 | LED 7 | LED 8
1 | O | X | X | X | O | X | X | X
2 | O | O | O | O | O | O | O | O
3 | X | O | X | X | X | O | X | X
4 | O | O | O | O | O | O | O | O
5 | X | X | O | X | X | X | O | X
6 | O | O | O | O | O | O | O | O
7 | X | X | X | O | X | X | X | O
8 | O | O | O | O | O | O | O | O
9 | O | X | X | X | O | X | X | X
10 | O | O | O | O | O | O | O | O
11 | X | O | X | X | X | O | X | X
12 | O | O | O | O | O | O | O | O
13 | X | X | O | X | X | X | O | X
14 | O | O | O | O | O | O | O | O
15 | X | X | X | O | X | X | X | O
16 | O | O | O | O | O | O | O | O
Compare
※ Should be no difference between sequence.
1. Compare the LED brightness between all LEDs on and individual LEDs on.
2. No brightness difference is allowed between the two conditions.

## Slide 5
1. Test CH Dependency |  |  |  |  |  |  |  | 
case) defect (High Brightness) |  |  |  |  |  |  |  | 
Sequence | XD #1 |  |  |  | XD #2 |  |  | 
 | LED 1 | LED 2 | LED 3 | LED 4 | LED 5 | LED 6 | LED 7 | LED 8
1 | O | X | X | X | O | X | X | X
2 | O | O | O | O | O | O | O | O
3 | X | O | X | X | X | O | X | X
4 | O | High | O | O | O | O | O | O
5 | X | X | O | X | X | X | O | X
6 | O | O | O | O | O | O | O | O
7 | X | X | X | O | X | X | X | O
8 | O | O | O | High | O | O | O | O
9 | O | X | X | X | O | X | X | X
10 | O | O | O | O | O | O | O | O
11 | X | O | X | X | X | O | X | X
12 | O | O | O | O | O | O | O | O
13 | X | X | O | X | X | X | O | X
14 | O | O | O | O | O | O | High | O
15 | X | X | X | O | X | X | X | O
16 | O | O | O | O | O | O | O | O

## Slide 6
Test
SCAN No.

## Slide 7
 | 2. Test SCAN No. |  |  |  |  |  |  |  |  | 
 | case) normal |  |  |  |  |  |  |  |  | 
 | Sequence | XD #1 |  |  |  | XD #2 |  |  |  | 
 |  | LED 1 | LED 2 | LED 3 | LED 4 | LED 5 | LED 6 | LED 7 | LED 8 | 
 | 1 (scan_no : 0) | O | O | O | O | O | O | O | O | 
 | 2 (mute) | X | X | X | X | X | X | X | X | 
 | 3 (scan_no : 3) | O | O | O | O | O | O | O | O | 
 | 4 (mute) | X | X | X | X | X | X | X | X | 
 | Repeat (8-times) | Repeat Sequence (1 ~ 4, 5-times) |  |  |  |  |  |  |  | 
Compare
※ Should be no difference between sequence.
※ There is no history of this type of defect occurring.
1. The pattern is 1.0s ON → 0.1s OFF, repeated.
2. No brightness difference is allowed between ON-OFF cycles.

## Slide 8
 | 2. Test SCAN No. |  |  |  |  |  |  |  |  | 
 | case) expected defect (flicker or OFF) |  |  |  |  |  |  |  |  | 
 | Sequence | XD #1 |  |  |  | XD #2 |  |  |  | 
 |  | LED 1 | LED 2 | LED 3 | LED 4 | LED 5 | LED 6 | LED 7 | LED 8 | 
 | 1 (scan_no : 0) | O | O | O | O | O | O | O | O | 
 | 2 (mute) | X | X | X | X | X | X | X | X | 
 | 3 (scan_no : 3) | O | Flicker | O | O | O | O | OFF | O | 
 | 4 (mute) | X | X | X | X | X | X | X | X | 
 | Repeat (8-times) | Repeat Sequence (1 ~ 4, 5-times) |  |  |  |  |  |  |  | 

## Slide 9
Test
Line Delay

## Slide 10
 | 3. Test Line Delay |  |  |  |  |  |  |  |  |  | 
 | case) normal |  |  |  |  |  |  |  |  |  | 
 | Sequence | Setting for Line Delay | XD #1 |  |  |  | XD #2 |  |  |  | 
 |  |  | LED 1 | LED 2 | LED 3 | LED 4 | LED 5 | LED 6 | LED 7 | LED 8 | 
 | 1 | 0 | O | O | O | O | O | O | O | O | 
 | 2 | 20 | O | O | O | O | O | O | O | O | 
 | 3 | 21 | O | O | O | O | O | O | O | O | 
 | 4 | 22 | O | O | O | O | O | O | O | O | 
 | 5 | 23 | O | O | O | O | O | O | O | O | 
 | 6 | 24 | O | O | O | O | O | O | O | O | 
 | 7 | 25 | O | O | O | O | O | O | O | O | 
 | 8 | 26 | O | O | O | O | O | O | O | O | 
 | 9 | 27 | O | O | O | O | O | O | O | O | 
 | 10 | 28 | O | O | O | O | O | O | O | O | 
 | 11 | 29 | O | O | O | O | O | O | O | O | 
 | 12 | 210 | O | O | O | O | O | O | O | O | 
 | 13 | 211 | O | O | O | O | O | O | O | O | 
※ Should be no difference between sequence.
※ Minor flicker is a transient effect caused by line delay switching.
1. The brightness must be maintained without any variation.
2. OFF or low brightness for more than 0.5 seconds is considered a defect.

## Slide 11
 | 3. Test Line Delay |  |  |  |  |  |  |  |  |  | 
 | case) defect (OFF or Low Brightness) |  |  |  |  |  |  |  |  |  | 
 | Sequence | Setting for Line Delay | XD #1 |  |  |  | XD #2 |  |  |  | 
 |  |  | LED 1 | LED 2 | LED 3 | LED 4 | LED 5 | LED 6 | LED 7 | LED 8 | 
 | 1 | 0 | O | O | O | O | O | O | O | O | 
 | 2 | 20 | O | O | O | O | O | O | O | O | 
 | 3 | 21 | OFF | O | O | O | O | O | O | O | 
 | 4 | 22 | O | O | O | O | O | O | O | O | 
 | 5 | 23 | O | O | O | O | Low | O | O | O | 
 | 6 | 24 | O | O | O | O | Low | O | O | O | 
 | 7 | 25 | O | O | OFF | O | Low | O | O | O | 
 | 8 | 26 | O | O | OFF | O | O | O | O | O | 
 | 9 | 27 | O | O | OFF | O | O | O | O | O | 
 | 10 | 28 | O | O | OFF | O | O | O | O | OFF | 
 | 11 | 29 | O | O | OFF | O | O | O | O | OFF | 
 | 12 | 210 | O | O | OFF | O | O | O | O | OFF | 
 | 13 | 211 | O | O | OFF | O | O | O | O | OFF | 

## Slide 12
Appendix

## Slide 13
Inch | IC1 |  |  |  | IC2 |  |  | 
50 | ch1 | ch3 | ch4 | ch2 | x | x | x | x
55 | ch1 | ch3 | ch4 | ch2 | x | x | x | x
65 | ch1 | x | ch4 | x | x | ch3 | ch4 | ch2
75 | ch1 | ch3 | ch4 | x | x | ch3 | ch4 | ch2
85 | ch1 | ch3 | ch4 | ch2 | x | ch3 | ch4 | ch2
Channel Mapping