## Slide 1
ID804 I2C
Consol manual
Aug. 31, 2026
Global Technologies

## Slide 2
Board Connection
Power Supply
- 12V, 1A
- YH396-02V
USB Cable
- MCU <-> PC
- MICRO-B to USB-B

## Slide 3
Board Connection
Switch Lever:
DOWN ↓
Switch Lever:
RIGHT →
Switch Lever:
DOWN ↓
Switch Lever:
DOWN ↓
Switch Lever:
DOWN ↓
ID804
Switch Lever:
LEFT ←

## Slide 4
Command Interface

## Slide 5
Serial Terminal Program
TeraTerm: https://github.com/TeraTermProject/teraterm/releases#release-v5.2

## Slide 6
Command Interface
Follow the steps below, then check the terminal program screen.
1. Install the IC. (Ensure the IC is oriented correctly.)
2. Connect the PC to the MCU using a USB cable.
3. Apply 12 V power to the JIG board.

## Slide 7
Command Interface
To see possible command, enter “help”

## Slide 8
Command Interface
Serial – “804_i2c_init”
- Supply VDD & VLED
- Read all register & Dump

## Slide 9
Command Interface
Serial – “804_w [hex] [hex]”
addr
value
Serial – “804_r [hex]”
addr
※ ID804 I2C Error
If an I2C Error occurs:
- The following message log will be displayed.
The written value can be read back successfully.

## Slide 10
F/W Download

## Slide 11
F/W Download
Run STM32CubeProgrammer
Turn on Jig Power
Press “Connect” BTN

## Slide 12
F/W Download
3) Click “Open file” & open released “sal_es0_xxxxxx.hex”

## Slide 13
F/W Download
4) Click “Download” -> “OK” -> “Disconnect” & turn off Jig Power