## Slide 1
SAL – CAN 호환성 검토
이준영
주식회사 글로벌 테크놀로지
2024. 11. 04.

## Slide 2
실험) CAN Bus의 (1)Load 저항(R103, R104) & SPLIT 단자의 (2)병렬 커패시터(C81) 유무에 따른 특성 확인
(1)
(2)

## Slide 3
1) GCV1043; No CAP at SPLIT; 110Ω at CAN_H/CAN_L
CAN_H
CAN_L
Vo(dom); CANH; Spec : 2.75 ~ 4.5V
Vo(dom); CANL; Spec : 0.5 ~ 2.25V
Vo(rec); Spec : 2 ~ 3V, NG!!
- dominant에서 recessive로 전환될 때
CANH/CANL의 상태 전환에 대한
timing issue에 의해 발생하는 현상

## Slide 4
Vo(dom); CANH; Spec : 2.75 ~ 4.5V
Vo(dom); CANL; Spec : 0.5 ~ 2.25V
CAN_H
CAN_L
Vo(rec); Spec : 2 ~ 3V
- SPLIT에 CAP을 장착
- CANH/CANL의 중간지점 (약 2.2V)으로 맞아짐
1) GCV1043; 4.7nF at SPLIT; 110Ω at CAN_H/CAN_L

## Slide 5
CAN_H
CAN_L
3) GCV1043; No CAP at SPLIT; No RES at CAN_H/CAN_L
2.5V (0.5vcc) (정상)
CAN_H
SPLIT

## Slide 6
참고) TJA1043; No CAP at SPLIT; 110Ω at CAN_H/CAN_L
CAN_H
CAN_L
Vo(dom); CANH; Spec : 2.75 ~ 4.5V
Vo(dom); CANL; Spec : 0.5 ~ 2.25V
Vo(rec); Spec : 2 ~ 3V, OK

## Slide 7
CAN_H
CAN_L
Vo(dom); CANH; Spec : 2.75 ~ 4.5V
Vo(dom); CANL; Spec : 0.5 ~ 2.25V
Vo(rec); Spec : 2 ~ 3V, OK
참고) TJA1043; 4.7nF at SPLIT; 110Ω at CAN_H/CAN_L