## Slide 1
Dated July/21/23 Rev. 0.0
XC-24
The local dimming controller for current drivers
Global Technologies
http://www.glbltech.com/
General Description
The XC-24 is a local dimming controller featuring 24 channels to drive its companion chips, XD-12 LED drivers that act as the voltage-based low side current sink for White LED back-lighting solution. This controller interfaces with XD-12 drivers through one serial line to send and receive the data to be needed for local dimming.
The XC-24 supports the SPI interface to communicate with the host, and the SPI interface can be daisy-chained, so it is effective to expand to support a large number of dimming areas.
For raising up dimming controllability, XC-24 supports the FB signal to efficiently control the LED power supply voltage and two interrupt pins, nINT_FAULT to indicate the fault events like as the thermal status, the open detection, the short detection and the feedback status, and nINT_LD to indicate the room of internal buffers for dimming data.
The XC-24 can support BIST functionality to ensure Back Light Unit is
properly assembled.
Confidential
24 Channels
Application
LED back-lighting with local dimming control

## Slide 2
XC-24
http://www.glbltech.com/
Confidential
Global Technologies
Feature
24 channels local dimming controller for the XD-12 LED drivers
Flexible sizing for each channel
up to 31 daisied drivers per channel
up to 127 blocks per channel
SPI interface
up to 30MHz
support daisy-chain connection
Flexible the baud-rate speed
Frame synchronization support : VSYNC 50 ~ 144Hz
Fault events support of drivers
Over temperature event
Open detection
Short detection
FB status
TTL-level input range
Supply voltage 4.5V ~ 5.5V
48-pin QFN 6060 Package
Latch-up Immunity ILATCH: JEDEC JESD78D Nov 2011: ±100mA
ESD, HBM protection (Norm: MIL 883 E Method 3015 Human Body Model): ±2kV

## Slide 3
http://www.glbltech.com/
Confidential
Application Circuit
Block Diagram
Global Technologies
XC-24

## Slide 4
http://www.glbltech.com/
Dated April/12/23 Rev. 0.0
Confidential
Pin diagram (Top View)
Global Technologies
XC-24
Pin Name | Pin No. | I/O | Type | Description | Remark
D12 | 1 | I/O | Digital | Data in/out | 
VDD1 | 2 | I | Power | Digital VDD | 
nSCS | 3 | I | Digital | SPI Chip Select | 
SCLK | 4 | I | Digital | SPI SCLK | 
MISO | 5 | O | Digital | SPI MISO | 
MOSI | 6 | I | Digital | SPI MOSI | 
VSS1 | 7 | I | GND | Digital GND | 
MCLK | 8 | I | Digital | Master Clock | 
Pin description

## Slide 5
http://www.glbltech.com/
Confidential
Pin description
Pin Name | Pin No. | I/O | Type | Description | Remark
VSS2 | 9 | I | GND | Digital GND | 
VSYNC | 10 | I | Digital | Frame synchronization | 
VDD2 | 11 | I | Power | Digital VDD | 
D24 | 12 | I/O | Digital | Data in/out | 
D23 | 13 | I/O | Digital | Data in/out | 
D22 | 14 | I/O | Digital | Data in/out | 
D21 | 15 | I/O | Digital | Data in/out | 
VDD3 | 16 | I | Power | Digital VDD | 
D20 | 17 | I/O | Digital | Data in/out | 
D19 | 18 | I/O | Digital | Data in/out | 
D18 | 19 | I/O | Digital | Data in/out | 
D17 | 20 | I/O | Digital | Data in/out | 
VSS3 | 21 | I | GND | Digital GND | 
D16 | 22 | I/O | Digital | Data in/out | 
D15 | 23 | I/O | Digital | Data in/out | 
D14 | 24 | I/O | Digital | Data in/out | 
D13 | 25 | I/O | Digital | Data in/out | 
LDOIN | 26 | I | Power | LDO feedback from LDOOUT | Attach 1uF
LDOOUT | 27 | O | Power | Internal LDO out to LDOIN | Connect to LDOIN
FB | 28 | O | Digital | Feedback for LED power supply | Open-drain, 10kΩ PU
VSS4 | 29 | I | GND | Digital GND | 
nINT_FT | 30 | O | Digital | Interrupt for fault events | Open-drain, 10kΩ PU
nINT_LD | 31 | O | Digital | Interrupt for dimming data room | Open-drain, 10kΩ PU
SDO | 32 | O | Digital | SPI MOSI daisied out | Unused : 10kΩ PD
VDD4 | 33 | I | Power | Digital VDD | 
SCLKO | 34 | O | Digital | SPI SCLK daisied out | Unused : 10kΩ PD
Global Technologies
XC-24

## Slide 6
http://www.glbltech.com/
Confidential
Pin description
Global Technologies
XC-24
Pin Name | Pin No. | I/O | Type | Description | Remark
TEST | 35 | I | Digital | TEST mode pin | 10Ω PD
D1 | 36 | I/O | Digital | Data in/out | 
D2 | 37 | I/O | Digital | Data in/out | 
D3 | 38 | I/O | Digital | Data in/out | 
D4 | 39 | I/O | Digital | Data in/out | 
VDD5 | 40 | I | Power | Digital VDD | 
D5 | 41 | I/O | Digital | Data in/out | 
D6 | 42 | I/O | Digital | Data in/out | 
D7 | 43 | I/O | Digital | Data in/out | 
D8 | 44 | I/O | Digital | Data in/out | 
VSS5 | 45 | I | GND | Digital GND | 
D9 | 46 | I/O | Digital | Data in/out | 
D10 | 47 | I/O | Digital | Data in/out | 
D11 | 48 | I/O | Digital | Data in/out | 

## Slide 7
http://www.glbltech.com/
Confidential
Equivalent Circuits of individual pins
Pad Name | I/O | Internal Circuit | Description
nSCS | I |  | SPI Chip Select
SCLK | I |  | SPI Clock Input
MOSI | I |  | SPI MOSI
MISO | O |  | Frame Sync.
SCLKO | O |  | SCLK Daisy Out
SDO | O |  | MOSI Daisy Out
MCLK | I |  | Mater Clock
Global Technologies
XC-24

## Slide 8
http://www.glbltech.com/
Confidential
Equivalent Circuits of individual pins
Global Technologies
XC-24
Pad Name | I/O | Internal Circuit | Description
VSYNC | I |  | Frame Sync.
nINT_FB | O |  | SPI Chip Select
nINT_LD | O |  | SPI Clock Input
FB | O |  | SPI MOSI
D | I/O |  | Data In/Out
VDD | - |  | Digital Power
VSS | - |  | Digital GND

## Slide 9
Maximum Absolute ratings (Ta = 25℃ unless otherwise noted)
http://www.glbltech.com/
Notes : Stresses beyond those listed under Absolute Maximum Ratings may cause permanent damage to the device
Confidential
Parameter | Symbol | Value | Unit
Supply voltage | VDD | -0.3 ~ 6.0 | V
MCLK to GND voltage | VMCLK | -0.3 ~ VDD+0.5 | V
VSYNC to GND voltage | VVSYNC | -0.3 ~ VDD+0.5 | V
nSCS to GND voltage | VSCS | -0.3 ~ VDD+0.5 | V
SCLK to GND voltage | VSCLK | -0.3 ~ VDD+0.5 | V
MOSI to GND voltage | VMOSI | -0.3 ~ VDD+0.5 | V
MISO to GND voltage | VMISO | -0.3 ~ VDD+0.5 | V
SCLKO to GND voltage | VSCLK | -0.3 ~ VDD+0.5 | V
SDO to GND voltage | VSDO | -0.3 ~ VDD+0.5 | V
D voltage | VDIO | -0.3 ~ VDD+0.5 | V
Ambient temperature | TA | -20 ~ 85 | ℃
Junction temperature | TJ | -20 ~ 125 | ℃
Storage temperature | TSTG | -45 ~ 150 | ℃
Relative Humidity(non-condensing) | RHNC | 5 ~ 85 | %
Moisture Sensitivity | MSL | Maximum Floor Life-time | 3
Parameter | Symbol | Value | Unit | Remark
Electrostatic Discharge HBM ; Contact | ESDHBM | ±2K | V | C=100 pF, R=1.5 kΩ
Electrostatic Discharge CDM ; Contact | ESDCDM | ±500 | V | R=1 Ω
Electrostatic Discharge
Global Technologies
XC-24

## Slide 10
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
Supply |  |  |  |  |  | 
Operating voltage | VDD |  | 4.5 | - | 5.5 | V
Operating Current | IDD |  | - | - |  | mA
Quiescent current | IDDD |  | - |  | - | mA
Input |  |  |  |  |  | 
nSCS Input Voltage | VSCSL | Chip Select, low level | - | - | 0.8 | V
 | VSCSH | Chip Select, high level | 2.0 | - | VDD | V
SCLK Input Voltage | VSCLKL | SPI Clock, low level | - | - | 0.8 | V
 | VSCLKH | SPI Clock, high level | 2.0 | - | VDD | V
MOSI Input Voltage | VMOSIL | MOSI, low level | - | - | 0.8 | V
 | VMOSIH | MOSI, high level | 2.0 | - | VDD | V
VSYNC Input Voltage | VVSYNCL | VSYNC low level | - | - | 0.8 | V
 | VVSYNCH | VSYNC high level | 2.0 | - | VDD | V
Output |  |  |  |  |  | 
MISO Output voltage | VMISOL | MISO, low level | - | - | 0.8 | V
 | VMISOH | MISO, high level | 2.0 | - | VDD | V
SCLKO Output voltage | VSCLKOL | SCLKO, low level | - | - | 0.8 | V
 | VSCLKOH | SCLKO, high level | 2.0 | - | VDD | V
SDO Output voltage | VSDOL | SDO, low level | - | - | 0.8 | V
 | VSDOH | SDO, high level | 2.0 | - | VDD | V
Bi-direction |  |  |  |  |  | 
D Inout voltage | VDIOL | D, low level | - | - | 0.8 | V
 | VDIOH | D, high level | 2.0 | - | VDD | V
 | RINT_PD | Internal pull-down resistance | - | 48 | - | KΩ
MCLK |  |  |  |  |  | 
Frequency | FMCLK |  | - | 14.7456 | - | MHz
Duty |  |  | 45 | 50 | 55 | %
Jitter | △FMCLK |  | -1 |  | 1 | %
Electrical Characteristic (VDD =5.0V, Ta=25.0℃ unless otherwise noted)
http://www.glbltech.com/
Confidential
Global Technologies
XC-24

## Slide 11
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Power Sequence
VDD
Command accessible
Stabilizing time > 5ms
Ramp time < 300us
Target Voltage
Operation

## Slide 12
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
SCLK |  |  |  |  |  | 
SCLK frequency | fCLK |  | - | - | 30 | MHz
SCLK duty | tCLK_DUTY |  | 49 | - | 51 | %
SCLK high time | tCH |  | 8 | - | - | ns
SCLK low time | tCL |  | 8 | - | - | ns
SCLKO |  |  |  |  |  | 
SCLK to SCLKO delay | TCO_DELAY |  | - | - | 6 (3) | ns
The skew between SCLKO to SDO | tSKEW |  | - | - | -1 (3) | ns
SCLKO high time | tOCH |  | tCH - 1(3) | - | - | ns
nSCS setup to the first rising SCLK | tCSS |  | 20 | - | - | ns
nSCS hold time from the last falling SCLK | tCSH |  | 3 | - | - | MCLK
nSCS high latency time | tCSHG |  | 3 | - | - | MCLK
MOSI setup time | tDS |  | 7 | - | - | ns
MOSI hold time | tDH |  | 3 | - | - | ns
MISO delay from the rising edge SCLK | tDO |  | - | - | 6 | ns
MISO high-Z from the nSCS de-assertion | tDOZ |  | - | - | 1 | MCLK
AC Characteristics (VDD S=5.0V, Ta=25.0℃ unless otherwise noted)
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Note (3) It should be careful that the tSKEW and tOCH are accumulated by the number of daisy devices if the daisy chain
connection is used. So, for the read and write transaction, the proper timing should be considered in daisy chain.

## Slide 13
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
For the local dimming data transmit a Serial Peripheral Interface is used. The SPI is configurated to work as SPI slave.
A Daisy Chain structure can be used to support large scale blocks array with several devices and operated up to 30MHz.
SPI Daisy Chain Structure
All SPI slaves share the Chip select signal, and these devices in Daisy chain can be treated as one big shift register. The devices can be enumerated as described below.
1. SPI Interface
SPI Protocol
The XQ-24 has 3 types of the SPI Interface protocol, the register-read, the register-write and the LD data-transfer. The SPI protocol’s format consists of a 16-bit command and a 16-bit register data or a series of 24(or 16)-bit LD data following the 16-bit command.
Figure 2. SPI protocol format
[Command format] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Bit15 | Bit14 | Bit14 | Bit13 | Bit12 | Bit11 | Bit10 | Bit9 | Bit8 | Bit7 | Bit6 | Bit5 | Bit4 | Bit3 | Bit2 | Bit1 | Bit0
 | Command code [1:0] |  |  | Address [7:0] |  |  |  |  |  |  |  | Burst size [5:0] |  |  |  |  | 
Register-read | 0 |  | 1 | Start address [7:0] |  |  |  |  |  |  |  | Burst size [5:0] |  |  |  |  | 
Register-write | 1 |  | 0 | Start address [7:0] |  |  |  |  |  |  |  | Burst size [5:0] |  |  |  |  | 
LD-transfer | 1 |  | 1 | don’t care |  |  |  |  |  |  |  | Line size [5:0] |  |  |  |  | 
[Data format] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Bit15 | Bit14 | Bit13 | Bit12 | Bit11 | Bit10 | Bit9 | Bit8 | Bit7 | Bit6 | Bit5 | Bit4 | Bit3 | Bit2 | Bit1 | Bit0
 | Data [15:0] |  | Address [7:0] |  |  |  |  |  |  |  | Burst size [5:0] |  |  |  |  | 
Register-RW | Register data [15:0] |  | Start address [7:0] |  |  |  |  |  |  |  | Burst size [5:0] |  |  |  |  | 
LD1 transfer | LD_WIDTH [1:0] = 2’b00 : 24 bits /block |  | 8’hxx |  |  |  |  |  |  |  | Line size [5:0] |  |  |  |  | 
LD2 transfer | LD_WIDTH [1:0] = 2’b01 : 24 bits /block |  | 8’hxx |  |  |  |  |  |  |  | Line size [5:0] |  |  |  |  | 
LD3 transfer | LD_WIDTH [1:0] = 2’b10 : 24 bits /block |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LD4 transfer | LD_WIDTH [1:0] = 2’b11 : 16 bits /block |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Figure 1. SPI daisy connection

## Slide 14
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
The SPI access sequence is as follows, depending on the type of access. There is no difference between a single and
a burst access except for the number of data due to the burst size.
SPI read/write sequence in burst
Command
Data
Data
a
a+1
Data
a+n
Data
Data
b
b+1
Data
b+m
Command
Data
Data
b
b+1
Data
b+m
Command
nSCS
MOSI
SDO
Start addr = 0xa
Burst size = n+1
SCLK
SCLKO
Command
Command
Data
Data
b
b+1
Data
b+m
nSCS
MOSI
MISO
(dev#2)
Data
Data
a
a+1
Data
a+n
MISO
Start addr = 0xa
Burst size = n+1
SCLK
SCLKO
Command
SDO
Figure 3. The SPI Burst write in daisied 2 devices
Figure 4. The SPI Burst read in daisied 2 devices

## Slide 15
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
Command
nSCS
LD
ch1
MOSI
LD width
SDO
LD
ch2
LD
chx
LD
ch1
LD
ch2
LD
chx
LD
chx
Command
LD
ch1
LD
ch2
Command
LD
ch1
LD
ch2
Burst size 1
Burst size 2
Burst size = n
CH_SIZE = x
1-Line size
The SPI sequence for the LD transfer is as follows. The LD width depends on the LD_WIDTH value of the CHANNEL ENABLE 2 register. If the LD_WIDTH = 2’b00, then the LD data size of one block zone transferred through the SPI becomes 24 bits consisted of PAM 12 bits and PWM 12 bits. Even if the transmitted width is 24 bits, the valid bits are actually 20 bits, PAM 10 bits + PWM 10 bits. Therefore, the data size per block to be transmitted to the daisied devices is 20 bits.
SPI LD transfer sequence
Figure 5. The SPI LD transfer in daisied 2 devices
LD_WIDTH [1:0] | LD width | LD format | Valid bits
2’b00 | 24 bits | PAM 12-bit + PWM 12-bit | PAM 10-bit + PWM 10-bit
2’b01 | 24 bits | PAM 12-bit + PWM 12-bit | PAM 10-bit + PWM 11-bit
2’b10 | 24 bits | PAM 12-bit + PWM 12-bit | PAM 10-bit + PWM 12-bit
2’b11 | 16 bits | LD 16-bit | LD 16-bit
Table 1. LD data size according to LD_WIDTH
The burst size unit means the amount of LD data corresponding to one line and the one line of LD data corresponds to the total LD data of all activated channels, and the number of active channel is determined by the CH_SIZE value of the ENABLE CHANNEL 2 register. Here, the CH_SIZE value should be equal to the number of activated channels by the CHx_EN of the ENABLE CHANNEL 1/2 registers.
Burst size unit = 1-line LD data = CH_SIZE * LD data size

## Slide 16
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
The XC-24 has a total of 24 channels for serial daisy connections with a total of 31 XD-12 devices. Each channel can transmit the data to the XD-12 and receive the data from the XD-12 through one line daisied to the XD-12 devices. The XD-24 has a total of 5 instructions for transferring the data to the XD-12 and 3 instructions for receiving the data from the XD-12.
2. Serial Interface
Instruction | Transaction direction | Data direction | Description
 | Command | Data | 
Global write | XC → XD | XC → XD | Global-write command the same register data between the XD devices
Local write | XC → XD | XC → XD | Local-write command the different register data between the XD devices
LD transfer | XC → XD | XC → XD | Local Dimming data-transfer command to the XD devices
ID gen | XC → XD | - | ID generation command of the XD devices in daisied each channel
Sync gen | XC → XD | - | Sync-generation command to the XD devices
Sync auto-gen | XC → XD | - | Automatically sync-generation command sync on the XD devices
Local read | XC → XD | XD → XC | Local-read command to the XD devices and read-back from the XD devices
Fault read | XC → XD | XD → XC | Fault-read command to the XD devices and read-back from the XD devices
Fault auto-read | XC → XD | XD → XC | Automatically fault-read command to the XD devices and read-back from the XD devices
XC-24
Ch1
Ch24
XD-12
#1
DIO
DDIO
XD-12
#2
DIO
DDIO
XD-12
#31
DIO
DDIO
The commands are listed as shown in the Table 2. and described in more detail below.
Table 2. Instruction list
Figure 6. The daisied scheme

## Slide 17
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
The ID-GEN COMMAND register is used to set a unique ID for each device and each device’s ID helps identifying when
each device should react on a read-back operation. Therefore, after POR this command should be transacted at the first time for proper operation of the XD-12 devices before transacting other commands. If the START bit of ID-GEN COMMAND register is set, then all activated channels begin issuing the command signals to all XD-12 daisied in each channel and the command signal streams repeat continuously for the number of daisied devices.
The number of daisied devices is determined by the DAISY SIZE register of each channel. After the command signal streams are completed, all devices will have their own ID respectively. The ID is numbered in opposite direction of daisied line. It is careful that the writing data is transferred from the first located device, the last number ID, to the last located device, the first number ID, in daisied line but the reading data is received from the last located device to the first located device sequentially.
ID-generation
Functional Description
Figure 7. The sequence of ID-GEN command
nSCS
MOSI
ID-GEN COMMAND
transmit
CH1
CH2
CHx
VDD
Initialization to the XD-12
XC-24
Ch1
Ch24
XD-12
#1
ID=31
DIO
DDIO
XD-12
#2
ID=30
DIO
DDIO
XD-12
#31
ID=1
DIO
DDIO

## Slide 18
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
The Global-write command is used to write the register data to the XD-12 only if all XD-12 devices daisied to a channel of the XC-24 have the same register data. If the register data to be written to the XD-12 are different each other, at that time the Local-write command should be used. For executing the Global-write command properly, the GLOBAL-WRITE DATA register should be firstly written with desired value and then the START bit of the GLOBAL-WRITE COMMAND register should be set with desired address in order to begin transacting this command.
Global-write
The GLOBAL-WRITE COMMAND register consists of 6 bits of ADDRESS field and 1 bit of START. The ADDRESS is the register address of the XD-12 to be accessed. If the START bit is set with the ADDRESS together, the Global writing command begins issuing simultaneously in all activated channels, and the command streams repeat continuously for the number of daisied XD-12. The number of daisied devices can be determined by the DAISY SIZE register of each channel. The max number of daisied devices per channel is 31.
GLOBAL-WRITE DATA
transmit
nSCS
MOSI
GLOBAL-WRITE COMMAND
transmit
CH1
CH2
CHx
Data
Address
Figure 8. The sequence of Global-write command

## Slide 19
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
The Local-write command is used to write the register data to the XD-12 in case that all XD-12 devices daisied to a channel of the XC-24 have the different register data each other. If the register data to be written to the XD-12 are same, at that time the Global-write command is more useful for fast transaction time. For proper execution of the Local-write command, the LOCAL-RW DATA registers should be firstly written with desired value and then, the START bit of the LOCAL-WRITE COMMAND register should be set with desired address for beginning this command. It is careful that the LOCAL-RW POINTER RESET register must be set necessarily to 1 for the next transaction after the current Local -write command execution is completed or before the next Local-write command will start again.
Local-write
The LOCAL-WRITE COMMAND register consists of ADDRESS 6 bits, CH_SEG 2 bits and START 1 bit. The ADDRESS is the register address of the XD-12 to be accessed. If the START bit is set with the ADDRESS together, the Local-write command begins the execution simultaneously in all activated channels, and the command streams repeat continuously for the number of daisied XD-12. The number of daisied devices can be determined by the DAISY SIZE register of each channel. The max number of daisied devices per channel is 31. The channel segment bits, CH_SEG, are used to decide on which channels are activated for this command, because this command can be performed 8 channels at a time.
The LOCAL-RW DATA registers are divided into a total of 8 port group and each port has a total of 16 registers. The first data register in the port is mapped to the first located XD-12 in daisied order and the second data register is mapped to the second located XD-12, and so on. Although the data registers in a port are a total 16, the XC-24 can support over 16 daisied devices in a channel by using the LOCAL-WR TRANSFER POINTER and LOCAL-RW DIFFERENCE POINTER. The LOCAL-WR TRANSFER DIFF POINTER of the LOCAL-RW DIFFERENCE POINTER shows how many data remain in the LOCAL-RW DATA buffers. A value of 0 means that the LOCAL-RW DATA buffers are empty, so you must continue to fill up before they are empty. A value greater than 16 means that the buffer has been overwritten, so you must wait until the pointer value is less than 16.
CH_SEG[1:0] | Channel to be activated | LOCAL-RW DATA 1 ~ 16 |  |  |  |  |  |  | 
 |  | PORT1 | PORT2 | PORT3 | PORT4 | PORT5 | PORT6 | PORT7 | PORT8
2’b00 | Ch 1 ~ Ch 8 | Ch 1 | Ch 2 | Ch 3 | Ch 4 | Ch 5 | Ch 6 | Ch 7 | Ch 8
2’b01 | Ch 9 ~ Ch 16 | Ch 9 | Ch 10 | Ch 11 | Ch 12 | Ch 13 | Ch 14 | Ch 15 | Ch 16
2’b10 | Ch 17 ~ Ch 24 | Ch 17 | Ch 18 | Ch 19 | Ch 20 | Ch 21 | Ch 22 | Ch 23 | Ch 24
Table 3. The LOCAL-RW DATA mapping according to the CH_SEG
Figure 9. The sequence of Local-write command
LOCAL-RW DATA
transmit
nSCS
MOSI
LOCAL-WRITE COMMAND
transmit
CH1
CH2
CHx
LOCAL-RW POINTER RESET
transmit
Data
Address
Local-write Done

## Slide 20
Address |  | PORT 1 |  | PORT 2 |  | PORT 3 |  | PORT 4 |  | PORT 5 |  | PORT 6 |  | PORT 7 |  | PORT 8
0x70~0x77 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1
0x78~0x7F |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2
0x80~0x87 |  | LOCAL RW DATA 3 |  | LOCAL RW DATA 3 |  | LOCAL RW DATA 3 |  | LOCAL RW DATA 3 |  | LOCAL RW DATA 3 |  | LOCAL RW DATA 3 |  | LOCAL RW DATA 3 |  | LOCAL RW DATA 3
0xE8~0xEF |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 16
0x70~0x77 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1 |  | LOCAL RW DATA 1
0x78~0x7F |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2 |  | LOCAL RW DATA 2
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
CH_SEG |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2’b00 |  | Channel 1 |  | Channel 2 |  | Channel 3 |  | Channel 4 |  | Channel 5 |  | Channel 6 |  | Channel 7 |  | Channel 8
2’b01 |  | Channel 9 |  | Channel 10 |  | Channel 11 |  | Channel 12 |  | Channel 13 |  | Channel 14 |  | Channel 15 |  | Channel 16
2’b10 |  | Channel 17 |  | Channel 18 |  | Channel 19 |  | Channel 20 |  | Channel 21 |  | Channel 22 |  | Channel 23 |  | Channel 24
 | XD-12 drivers daisied in each channel |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | # 1 |  |  |  |  |  |  |  |  |  | # 1 |  |  |  | 
 | # 2 |  | # 1 |  |  |  | # 1 |  | # 1 |  | # 2 |  |  |  | 
 | # 3 |  | # 2 |  | # 1 |  | # 2 |  | # 2 |  | # 3 |  |  |  | # 1
 | # 4 |  | # 3 |  | # 2 |  | # 3 |  | # 3 |  | # 4 |  | # 1 |  | # 2
 | # m-1 |  | # n-1 |  | # k-1 |  | # n-1 |  | # n-1 |  | # m-1 |  | # l-1 |  | # k-1
 | # m |  | # n |  | # k |  | # n |  | # n |  | # m |  | # l |  | # k
Physical
size
Functional Description
Local-RW DATA structure for access
Figure 10. LOCAL-RW DATA mapping structure and data flow
 | 20th dev | 19th dev |  | 5th dev |  | 1st dev
XD-12 daisied | ID #1 | ID #2 |  | ID #16 |  | ID #20
PORT1 | LOCAL RW DATA 1 | LOCAL RW DATA 2 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 4
 | 1st dev | 2nd dev |  | 16th dev |  | 20th dev
XD-12 daisied | ID #20 | ID #19 |  | ID #5 |  | ID #1
PORT1 | LOCAL RW DATA 1 | LOCAL RW DATA 2 |  | LOCAL RW DATA 16 |  | LOCAL RW DATA 4
write
read-back

## Slide 21
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
The Sync-generation command is used to synchronize the frame sync time for all daisied devices simultaneously. This command execution can be done by two methods, the one is by setting the START bit of the SYNC-GEN COMMAND register and the other is by setting the SYNC_AUTO_EN bit of the COMMAND AUTO ENABLE register.
If the SYNC_AUTO_EN bit is set, the Sync-generation command is automatically executed at the moment of receiving the VSYNC input. It is recommended to use this function, but it should be careful that The synchronization time of the XD-12 devices may be as late as the number of XD-12 devices than the time the VSYNC was received, so the VSYNC should arrive as soon as it is late. This command streams repeat continuously for the number of daisied devices in each channel.
Sync-generation
The Fault-read command is used to read-out the fault information of all daisied devices simultaneously. This command execution can be done by two methods, the one is by setting the START bit of the FAULT-GEN COMMAND register and the other is by setting the FAULT_AUTO_EN bit of the COMMAND AUTO ENABLE register.
If the FAULT_AUTO_EN bit is set, the Fault-read command is automatically executed after the completion of the Sync auto-gen command at the moment of receiving the VSYNC input. The fault data to be read-back from all XD-12 devices in each channel is stored into the corresponding channel’s GLOBAL FAULT-READ DATA register, respectively.
Fault-read
Figure 12. The sequence of FAULT-READ command
nSCS
MOSI
FAULT-READ COMMAND
transmit
CH1
CH2
CHx
VSYNC
SYNC-AUTO-GEN
FAULT-AUTO-READ
FAULT-READ
Figure 11. The sequence of SYNC-GEN command
nSCS
MOSI
SYNC-GEN COMMAND
transmit
CH1
CH2
CHx
VSYNC
SYNC-AUTO-GEN
SYNC-GEN

## Slide 22
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
The Local-read command is used to read the register data from all XD-12 devices daisied in a channel of the XC-24. Unlike the Local-write or Global-write command, the Local-read command can be used to read the register data of the XD-12 devices regardless of whether the data is the same or different. The data to be read-out from the XD-12 devices are stored into the LOCAL-RW DATA registers sequentially like the Figure 10. The START bit of the LOCAL-READ COMMAND register should be set with desired address to be read-out for beginning this command. It is careful that the LOCAL-RW POINTER RESET register must be set necessarily to 1 for the next transaction after the current Local read command execution is completed or before the next Local-read command will start again.
Local-read
The LOCAL-READ COMMAND register consists of ADDRESS 6 bits, CH_SEG 2 bits and START 1 bit. The ADDRESS is the register address of the XD-12 to be accessed. If the START bit is set with the ADDRESS together, the Local-read command begins the execution simultaneously in all activated channels, and the command streams repeat continuously for the number of daisied XD-12. The number of daisied devices can be determined by the DAISY SIZE register of each channel. The max number of daisied devices per channel is 31. The channel segment bits, CH_SEG, are used to decide on which channels are activated for this command, because this command can be performed 8 channels at a time.
The LOCAL-RW DATA registers are divided into a total of 8 port group and each port has a total of 16 registers. Unlike the Local-write command, the first data register in the port is mapped to the last located XD-12 in daisied order and the second data register is mapped to the second located XD-12 from the back, and so on. Although the data registers in a port are a total 16, the XC-24 can support over 16 daisied devices in a channel by using the LOCAL-READ RECEIVE POINTER and LOCAL-RW DIFFERENCE POINTER. The LOCAL-RD RECEIVE DIFF POINTER of the LOCAL-RW DIFFERENCE POINTER shows how many data are filled up in the LOCAL-RW DATA buffers. A value of 0 means that the LOCAL-RW DATA buffers are empty, so you must wait for the buffers to be refilled, and if the value is greater than 16, it means that the LOCAL-RW DATA buffers have been overwritten, so you must drag out the buffers before they are overflowed. Refer to the Table 3. and the Figure 10. for the mapping scheme.
Figure 13. The sequence of Local-read command
LOCAL-READ COMMAND
transmit
nSCS
MOSI
CH1
CH2
CHx
LOCAL-RW POINTER RESET
transmit
Addr
Data
MISO
LOCAL-READ COMMAND
LOCAL-READ-BACK
Local-Read Done
SPI Read

## Slide 23
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Functional Description
The Local Dimming data of the next frame should be transmitted to the XC-24 through the SPI and the XC-24 should complete to transfer the LD data to the XD-12 devices before assertion of the next frame sync. And then, the LD data will be started to dimming-out by the XC-12 devices at the next frame sync. The LD_WR_POINTER of the LD WR POINTER register will be increased one by one in line unit whenever the LD data are written to the XC-24 LD data buffers through the SPI and see the Figure 5. for the amount of one line LD. The LD_RD_POINTER will be increased one by one whenever the XC-24 transmits the amount of one LD data to the XD-12 devices. The LD_DIFF_POINTER is a value of the LD_WR_POINTER minus the LD_RD_POINTER, so the value is useful to check how many LD data remains in the internal LD buffers.
If the LD_TANS_START_POINTER value becomes equal to the LD_DIFF_POINTER, then the XC-24 starts sending the LD data to the XD-12 devices automatically until the LD_DIFF_POINTER value becomes to 0.
Sequence of Local Dimming data transfer
Figure 14. The sequence of Local dimming Data transfer
LD Data transfer
(frame #1-1)
#1
VSYNC
#2
LD TRANSFER
(frame #1)
DIO #x
SPI I/F
LD Data transfer
(frame #2-1)
Local dimming out
(of XD-12)
Local dimming out
(frame #1)
LD_WR_POINTER=k
LD_TRANS_START_POINTER=k
LD_DIFF_POINTER=m-n
LD Data transfer
(frame #1-2)
LD Data transfer
(frame #1-n)
LD_RD_POINTER=n
LD_WR_POINTER=m

## Slide 24
Channel 1 |  | Channel 2 |  | Channel 3 |  | Channel x
XD-12 drivers daisied in each channel |  |  |  |  |  | 
# m |  |  |  |  |  | 
# m-1 |  | # n |  |  |  | 
# m-2 |  | # n-1 |  |  |  | # l
# m-3 |  | # n-2 |  | # k |  | # l-1
# 2 |  | # 2 |  | # 2 |  | # 2
# 1 |  | # 1 |  | # 1 |  | # 1
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Block 1 | LD buffer 1 |  | LD buffer 1 |  | LD buffer 1 |  | LD buffer 1
Block 2 | LD buffer 2 |  | LD buffer 2 |  | LD buffer 2 |  | LD buffer 2
Block 3 | LD buffer 3 |  | LD buffer 3 |  | LD buffer 3 |  | LD buffer 3
Block 32 | LD buffer 32 |  | LD buffer 32 |  | LD buffer 32 |  | LD buffer 32
Block 33 | LD buffer 33 |  | LD buffer 33 |  | LD buffer 33 |  | LD buffer 33
Block 34 | LD buffer 34 |  | LD buffer 34 |  | LD buffer 34 |  | LD buffer 34
Block 35 | LD buffer 35 |  | LD buffer 35 |  | LD buffer 35 |  | LD buffer 35
Block 127 | LD buffer 127 |  | LD buffer 127 |  | LD buffer 127 |  | LD buffer 127
Physical
size
Functional Description
The total number of Local Dimming data buffers is 32 per channel and 1 buffer can contain one block data which consists of PAM and PWM data. The size of PAM and PWM data depends on the LD_WIDTH of CHANNEL ENABLE 2 register and refer to previous chapter for more details. Even if the physical buffer size is limited to 32, the XC-24 can support to transfer over 256 blocks by using the LD WRITE POINTER, LD READ POINTER and LD DIFFERENCE POINTER. You can continue to send the LD data so that the LD DIFFERENCE POINTER does not become 0. The number of daisied devices of each channel can be different from each other by separately setting the DAISY SIZE register of each channel. The below shows the scheme of LD buffers and the mapping to the daisied device. For more information refer to the example on the next page.
Local Dimming data buffer
Figure 15. The scheme of Local dimming Data buffers

## Slide 25
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Channel 1 |  | Channel 2 |  | Channel 3 |  | Channel x
XD-12 drivers daisied in each channel |  |  |  |  |  | 
# 10 |  |  |  |  |  | # 10
# 9 |  | # 9 |  |  |  | # 9
# 8 |  | # 8 |  |  |  | # 8
# 7 |  | # 7 |  | # 7 |  | # 7
# 2 |  | # 2 |  | # 2 |  | # 2
# 1 |  | # 1 |  | # 1 |  | # 1
Block 1 | LD 1 |  | LD 1 |  | LD 1 |  | LD 1
Block 2 | LD 2 |  | LD 2 |  | LD 2 |  | LD 2
Block 3 | LD 3 |  | LD 3 |  | LD 3 |  | LD 3
Block 4 | LD 4 |  | LD 4 |  | LD 4 |  | LD 4
Block 5 | LD 5 |  | LD 5 |  | LD 5 |  | LD 5
Block 27 | LD 27 |  | LD 27 |  | LD 27 |  | LD 27
Block 28 | LD 28 |  | LD 28 |  | LD 28 |  | LD 28
Block 29 | LD 29 |  | LD 29 |  | 0 |  | LD 29
Block 30 | LD 30 |  | LD 30 |  | 0 |  | LD 30
Block 31 | LD 31 |  | LD 31 |  | 0 |  | LD 31
Block 32 | LD 32 |  | LD 32 |  | 0 |  | LD 32
Block 33 | LD 33 |  | LD 33 |  | 0 |  | LD 33
Block 34 | LD 34 |  | LD 34 |  | 0 |  | LD 34
Block 35 | LD 35 |  | 0 |  | 0 |  | LD 35
Block 36 | LD 36 |  | 0 |  | 0 |  | LD 36
Block 37 | LD 37 |  | 0 |  | 0 |  | LD 37
Block 38 | LD 38 |  | 0 |  | 0 |  | 0
Block 39 | LD 39 |  | 0 |  | 0 |  | 0
Block 40 | 0 |  | 0 |  | 0 |  | 0
①
②
39
Physical
size
DAISIED_DEV_CH_SIZE= 4
BLOCK_SIZE_CHx=37
CH_SIZE= x
Figure 16. The example of Local dimming Data-transfer
Functional Description
The below example shows how to set properly the registers relevant to the Local Dimming data transfer. The CH_SIZE of the CHANNEL ENABLE 2 register determines how many channels among a total of 24 channels of XC-24 will be activated, and if 20 channels will be used, then the CH_SIZE is 0x14 and available channels become from the channel 1 to channel 20, so it should be careful that the order of channels to be selected must be a direction that sequentially increases from 1 to 24. The DAISY_SIZE_CHx of the DAISY SIZE registers determines how many XD-12 devices will be daisied in the channel x, and if 10 XD-12 devices are daisied in a channel x, then the DAISY_ SIZE_CHx should be set to 0xA. The DAISIED_DEV_CH_SIZE determines how many channels of the XD-12 will be used, so if the value is 0x4, the XD-12 devices daisied in a channel x will capture only 4 LD data and then bypass the flowing LD data streams to the next XD-12 devices and the remainder of the multiples of 4 be delivered lastly to a las XD-12 device. It should be careful that all devices except for the last device must have the same value of DAISIED_ DEV_CH_SIZE. The BLOCK_SIZE_CHx determines the total number of LD data to be transferred to a channel x.
Local Dimming data transfer
SPI transfer data sequence and direction
DAISY_SIZE_CHx=10

## Slide 26
http://www.glbltech.com/
Confidential
3. Register Map
The SPI interface protocol consists of two segments, the command 16-bit followed by the register’s data 16-bit or
a series of local dimming data.
Global Technologies
XC-24
Command format
B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
COMMAND CODE |  | START ADDRESS [7:0] |  |  |  |  |  |  |  | BURST SIZE [5:0] |  |  |  |  | 
Bits | Fields | Descriptions
15:14 | COMMAND CODE | 2’b00 : No operation. 2’b01 : Register Read. 2’b10 : Register Write. 2’b11 : Local dimming data transfer.
13:6 | START ADDRESS | The start address of registers to access.
5:0 | BURST SIZE | Amount of data to transfer or receive. In case of accessing the registers, the number 1 means one packet of 16-bit data. In case of transferring the Local dimming data, the number 1 means one packet of (LD size * enabled channel numbers). The LD size and enabled channel numbers depend on the LD_WIDTH[1:0] and its bits of CHANNEL ENABLE 1 and 2 registers.
Data format
Bits | Fields | Descriptions | 
15:0 | DATA [15:0] | In case of COMMAND CODE : | In case of COMMAND CODE :
 |  | 2’b01 2’b10 2’b11 | A register’s data to read. A register’s data to write. A series of local dimming data. Be careful that the data size and width to transfer the local dimming data are different from the register access. Refer to previous chapter 2. SPI protocol
B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
DATA [15:0] |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 27
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Bits | Fields | Descriptions | 
15 | START | ‘0’ | No operation.
 |  | ‘1’ | Start executing the global-write command with the GLOBAL WRITE DATA register, together, and this bit is auto-cleared after completing this execution. For correct operation, It needs to set the GLOBAL WRITE DATA register with desired value before setting this bit. The global-writing can be used in case that the target registers’ values of all XD-12 daisied devices are all the same. If the values are different from each other, then the local-write command should be used instead of the global-write command.
5:0 | ADDRESS [5:0] | The same target address of all XD-12 daisied devices to write. | 
GLOBAL-WRITE COMMAND
Bits | Fields | Descriptions
5 | VS_RST2 | If this bit is set, all de-serializers’ sm are reset at VSYNC rising. Normally, no need to use this bit.
4 | VS_RST1 | If this bit is set, all serializers’ sm are reset at VSYNC rising. Normally, no need to use this bit.
2 | RST3 | Reset to all types of buffer, the frame buffers, the global and local r/w registers and the global fault read registers. Auto-cleared. Normally, no need to use this bit.
1 | RST2 | Reset to all serializers’ and de-serializers’ state machine, Auto-cleared. Normally, no need to use this bit.
0 | RST1 | Reset to all logics, Auto-cleared (No need to clear after set) It need to set this bit after POR to ensure XC-24 reset.
SOFT RESET
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h00 | 0 | x | x | x | x | x | x | x | x | x | x | VS_RST2 | VS_RST1 | x | RST3 | RST2 | RST1
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h01 | 0 | START | x | x | x | x | x | x | x | x | x | ADDR [5:0] |  |  |  |  | 

## Slide 28
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Bits | Fields | Descriptions | 
15 | START | ‘0’ | No operation.
 |  | ‘1’ | Start executing the local-write command with the LOCAL RW DATA registers together, and this bit is auto-cleared after completing this execution. For correct operation, It needs to set the LOCAL RW DATA registers with desired values before setting this bit. The local-write command is used in case that the target registers’ values of all XD-12 daisied devices are different from each other.
9:8 | CH_SEG [1:0] | These bits are used to designate which channels are activated for this command. | These bits are used to designate which channels are activated for this command.
 |  |  | 2’b00 The channel 1 from 8 are activated. 2’b01 The channel 9 from 16 are activated. 2’b10 The channel 17 from 24 are activated. 2’b11 No allocated.
 |  | Refer to previous chapter. how to allocate the LOCAL RW DATA registers according to CH_SEG [1:0]. | 
5:0 | ADDRESS [5:0] | The same target address of all XD-12 daisied devices to write | 
LOCAL-WRITE COMMAND
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h02 | 0 | START | x | x | x | x | x | CH_SEG [1:0] |  | x | x | ADDR [5:0] |  |  |  |  | 
LOCAL-READ COMMAND
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h03 | 0 | START | x | x | x | x | x | CH_SEG [1:0] |  | x | x | ADDR [5:0] |  |  |  |  | 
Bits | Fields | Descriptions | 
15 | START | ‘0’ | No operation.
 |  | ‘1’ | Start executing the local-read command with the LOCAL RW DATA registers together, and this bit is auto-cleared after completing this execution. For correct operation, It needs to set the LOCAL RW DATA registers with desired values before setting this bit. The local-read command is used to read out the target registers’ values of all XD-12 daisied devices.
9:8 | CH_SEG [1:0] | These bits are used to designate which channels are activated for this command | These bits are used to designate which channels are activated for this command.
 |  |  | 2’b00 : The channel 1 from 8 are activated. 2’b01 : The channel 9 from 16 are activated. 2’b10 : The channel 17 from 24 are activated. 2’b11 : No allocated.
 |  | Refer to previous chapter. how to allocate the LOCAL RW DATA registers according to CH_SEG [1:0]. | 
5:0 | ADDRESS [5:0] | The same target address of all XD-12 daisied devices to read out. | 

## Slide 29
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
Bits | Fields | Descriptions | 
15 | START | ‘0’ ‘1’ | No operation. Start executing the id-generating command to all XD-12 daisied devices and this bit is auto-cleared after completing this execution. All XD-12 daisied devices connected in each channel will have their own ID number after completing the id-generating command. This command is needed to read-out the XD-12 drivers’ registers data correctly in sequential, so, this command should be executed before executing the local-reading or the fault-reading command. It is recommended that the id-generating command should be executed firstly on system initialization.
ID-GEN COMMAND
FAULT-READ COMMAND
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h04 | 0 | START | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h05 | 0 | START | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
LD-TRANSFER COMMAND
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h06 | 0 | START | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
Bits | Fields | Descriptions | 
15 | START | ‘0’ ‘1’ | No operation. Start executing the fault-reading command to all XD-12 daisied devices to monitor the fault event like as the thermal occurrence, the short status, the open status and the fb status of the XD-12 devices and this bit is auto-cleared after completing this execution. This command can be also auto-executed at the VSYNC rising edge if the FAULT_ AUTO_EN bit in the COMMAND AUTO ENABLE register is set.
Bits | Fields | Descriptions | 
15 | START | ‘0’ ‘1’ | No operation. Start executing the local dimming data transfer command to all XD-12 daisied devices in order to transfer the LD data in burst from the XC-24 to the XD-12 drivers and this bit is auto-cleared after the completion. This command can be also auto-executed immediately after the amount of LD data to be transferred to the XC-24 through the SPI interface is reached to the value of the LD_RD_START_POINTER of the LD START POINTER/TH register.

## Slide 30
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
SYNC-GEN COMMAND
COMMAND AUTO ENABLE
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h07 | 0 | START | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h08 | 0 | x | x | x | x | x | x | x | x | x | x | x | FAULT_AUTO_EN | x | x | x | SYNC_AUTO_EN
Bits | Fields | Descriptions | 
4 | FAULT_AUTO_EN | ‘0’ ‘1’ | N operation. Start executing the fault-reading command automatically. If this bit is set, the fault-reading command is auto-executed in two conditions. The first is occurred at the time of VSYNC rising edge and the second condition is occurred at the time of expiration of the FAULT AUTO READ TIMER register for the number of occurrence of the FAULT AUTO READ EVENT register.
0 | SYNC_AUTO_EN | ‘0’ ‘1’ | No operation. Start executing the sync-gen command automatically. If this bit is set, the sync-gen command is auto-executed at the time of VSYNC rising edge.
LD-WRITE POINTER
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h0A | RO | x | x | x | x | x | x | x | LD_WR_POINTER [8:0] | x | x | x | x | x | x | x | x
Bits | Fields | Descriptions
8:0 | LD_WR_POINTER | This register value represents the number of times the local dimming data are written into the internal LD buffers through the SPI interface. The number increases one by one whenever the local dimming data corresponding to (the number of enabled channels * one LD data width) are transferred to the internal LD buffers. This pointer value is reset at the VSYNC rising. LD_WIDTH of the CHANNEL ENABLE 2 register : 2’b00 : one block LD data width = 24 bits 2’b01 : one block LD data width = 24 bits 2’b10 : one block LD data width = 24 bits 2’b11 : one block LD data width = 16 bits
Bits | Fields | Descriptions | 
15 | START | ‘0’ ‘1’ | No operation. Start executing the sync-gen command to all XD-12 daisied devices in order to make the frame synchronization to the drivers and this bit is auto-cleared after this execution. This command can be also auto-executed at the VSYNC rising edge, if the SYNC_ AUTO_EN bit in the COMMAND AUTO ENABLE register is set. It is recommended that the SYNC_AUTO_EN bit is set for good local dimming.

## Slide 31
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
LD-READ POINTER
LD-DIFFERENCE POINTER
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h0B | RO | x | x | x | x | x | x | x | LD_RD_POINTER [8:0] | x | x | x | x | x | x | x | x
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h0C | RO | x | x | x | x | x | x | x | x | x | x | LD_DIFF_POINTER [5:0] |  |  |  |  | 
Bits | Fields | Descriptions
5:0 | LD_DIFF_POINTER | This value is useful to monitor how much the LD data remains in the internal LD buffers for checking overrun or underrun. = LD_WR_POINTER – LD_RD_POINTER
LD-TRANSFER START POINTER / THRESHOLD
Bits | Fields | Descriptions
13:8 | LD_TRANS_START_POINTER | The LD_TRANS_START_POINTER determines when the transmit from the internal LD buffers to the XD-12 drivers will begin. If the value is set to 8, then the transmit will begin as soon as the number of times the data through the SPI interface becomes 8. Once the transmit is stated, the transaction will be continued until the number of transmit reaches to the BLOCK_SIZE value of the BLOCK SIZE registers.
7 | INT_LD_SIGN | Don’t set this bit.
5:0 | LD_DIFF_THRESHOLD | The LD_DIFF_THRESHOLD is used to set in which condition the nINT_LD output signal will be issued to the host. Whenever the LD_DIFF_POINTER is equal to or smaller than the LD_DIFF_THRESHOLD, then the nINT_LD signal will be issued. This feature helps to check how much LD data remains in the internal LD buffer for monitoring overruns or underruns of the LD data.
Bits | Fields | Descriptions
8:0 | LD_RD_POINTER | This register value represents the number of times the local dimming data are read-out to transfer the data from the internal LD buffers to the XD-12 drivers. The number increases one by one whenever the local dimming data corresponding to the one block LD data of the XD-12 drivers are read-out. This pointer value is reset at the VSYNC rising.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h0D | 0 | x | x | LD_TRANS_START_POINTER [5:0] | x | x | x | x | x | INT_LD_SIGN | x | LD_DIFF_THRESHOLD [5:0] |  |  |  |  | 

## Slide 32
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
LOCAL-WR TRANSFER POINTER
LOCAL-RD RECEIVE POINTER
Bits | Fields | Descriptions
12:8 | LOCAL_RD_OUT_POINTER | This register value represents the number of times the data transferred from the XD-12 drivers are read out from the LOCAL RW DATA registers for transferring the data through the SPI interface. The number increases one by one whenever the data are read-out from the LOCAL RW DATA registers.
5:0 | LOCAL_RD_REC_POINTER | This register value represents the number of times the data to be transferred through the SPI interface are written from the XD-12 drivers to the LOCAL RW DATA registers. The number increased one by one whenever the data are written to the LOCAL RW DATA registers.
LOCAL-RW DIFFERENCE POINTER
Bits | Fields | Descriptions
12:8 | LOCAL_RD_DIFF_POINTER | This value is useful to monitor how much the data from the XD-12 drivers remains in the LOCAL RW DATA registers for checking overrun or underrun. = LOCAL_RD_REC_POINTER – LOCAL_RD_OUT_POINTER
5:0 | LOCAL_WR_DIFF_POINTER | This value is useful to monitor how much the data to be transferred to the XD-12 remains in the LOCAL RW DATA registers for checking overrun or underrun. = LOCAL_WR_TRANS_POINTER – LOCAL_WR_OUT_POINTER
Bits | Fields | Descriptions
12:8 | LOCAL_WR_OUT_POINTER | This register value represents the number of times the data from the LOCAL RW DATA registers are read-out to write the data to the XD-12 drivers’ registers. The number increases one by one whenever the data are read-out from the LOCAL RW DATA registers.
5:0 | LOCAL_WR_TRANS_POINTER | This register value represents the number of times the data to be transferred to the XD-12 drivers are written to the LOCAL RW DATA registers through the SPI interface. The number increased one by one whenever the data are written to the LOCAL RW DATA registers.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h0E | RO | x | x | LOCAL_WR_OUT_POINTER [5:0] | x | x | x | x | x | x | x | LOCAL_WR_TRANS_POINTER [5:0] |  |  |  |  | 
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h0F | RO | x | x | LOCAL_RD_OUT_POINTER [5:0] | x | x | x | x | x | x | x | LOCAL_RD_REC_POINTER [5:0] |  |  |  |  | 
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h10 | RO | x | x | LOCAL_RD_DIFF_POINTER [5:0] | x | x | x | x | x | x | x | LOCAL_WR_DIFF_POINTER [5:0] |  |  |  |  | 

## Slide 33
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
LOCAL-RW POINTER RESET
FAULT-AUTO-READ TIMER
Bits | Fields | Descriptions
15:0 | FAULT_AUTO_RD_INTERVAL | This register determines the execution interval for the fault auto-read commands. Counted in MCLK units.
FAULT-AUTO-READ EVENT
Bits | Fields | Descriptions
15:8 | FAULT_AUTO_RD_EVENT | This register determines the execution times for the fault auto-read commands. The value is reset at VSYNC rising edge.
0 | FAULT_AUTO_RD_INTERVAL | The last bit of the FAULT_AUTO_RD_TIMER [16:0]
Bits | Fields | Descriptions | 
8 | LOCAL_RD_POINTER_RST | ‘0’ ‘1’ | No operation The LOCAL_RD_OUT_POINTER and the LOCAL_RD_REC_POINTER are reset. This bit is auto-cleared.
0 | LOCAL_WR_POINTER_RST | ‘0’ ‘1’ | No operation The LOCAL_WR_OUT_POINTER and the LOCAL_WR_TRANS_POINTER are reset. This bit is auto-cleared.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h12 | RO | FAULT_AUTO_RD_TIMER [15:0] | x | LOCAL_RD_OUT_POINTER [5:0] | x | x | x | x | x | x | x | LOCAL_RD_REC_POINTER [5:0] |  |  |  |  | 
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h11 | 0 | x | x | x | x | x | x | x | LOCAL_RD_POINTER_RST | x | x | x | x | x | x | x | LOCAL_WR_POINTER_RST
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h13 | 0 | FAULT_AUTO_RD_EVENT [7:0] | x | x | x | x | x | x | x | x | x | x | x | x | x | x | FAULT_AUTO_RD_INTERVAL [16]

## Slide 34
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
SERIALIZER CLOCK GEN
INTERRUPT ENABLE
Bits | Fields | Descriptions | 
7 | INT_FAULT_RD_FAIL_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that any violation happens during the execution for the fault read-back from the XD-12.
6 | INT_FAULT_AUTO_RD_ FAIL_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that any violation happens during the execution for the fault auto-read-back from the XD-12.
5 | INT_RD_REC_FAIL_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that any violation happens during the execution for the local read-back from the XD-12.
4 | INT_LD_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that the LD_DIFF_POINTER is equal to or smaller than the LD_DIFF_THRESOLD during the execution of the LD transfer to the XD-12.
3 | INT_THERMAL_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that the thermal regulation happens among the XD-12 drivers during dimming operation.
2 | INT_SHORT_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that the short condition happens among the XD-12 drivers during dimming operation.
1 | INT_OPEN_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that the open condition happens among the XD-12 drivers during dimming operation.
0 | INT_FB_EN | ‘0’ ‘1’ | No operation This bit enables to issue the interrupt through the nINT_FAULT pin in case that the fb condition happens among the XD-12 drivers during dimming operation.
Bits | Fields | Descriptions
6:4 | SCK_LOW | This register determines the high pulse duration in case the serial data-out drives the low state. Counted in MCLK units.
3:0 | SCK_HIGH | This register determines the high pulse duration in case the serial data-out drives the high state. Counted in MCLK units.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h14 | 0 | x | x | x | x | x | x | x | x | x | SCK_LOW [2:0] | x | x | SCK_HIGH [3:0] | x | x | 
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6
‘h15 | 0 | x | x | x | x | x | x | x | x | INT_FAULT_RD_FAIL_EN | INT_FAULT_AUTO_RD_FAIL_EN
Addr | Default | B5 | B4 | B3 | B2 | B1 | B0
‘h15 | 0 | INT_RD_REC_FAIL_EN | INT_LD_EN | INT_THERMAL_EN | INT_SHORT_EN | INT_OPEN_EN | INT_FB_EN

## Slide 35
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
COMMAND STATUS 1
Bits | Fields | Descriptions
15 | LOCAL_RD_DONE | This bit is set after the execution for the local-reading command is completed.
14 | LOCAL_RD_DOING | This bit is set while the local-reading command is working until it is complete.
13 | LOCAL_WR_DONE | This bit is set after the execution for the local-writing command is completed.
12 | LOCAL_WR_DOING | This bit is set while the local-writing command is working until it is complete.
11 | GLOBAL_WR_DONE | This bit is set after the execution for the global-writing command is completed.
10 | GLOBAL_WR_DOING | This bit is set while the global-writing command is working until it is complete.
9 | LD_TRANS_DONE | This bit is set after the execution for the LD transferring command is completed.
8 | LD_TRANS_DOING | This bit is set while the LD transferring command is working until it is complete.
7 | FAULT_DONE | This bit is set after the execution for the fault-reading command is completed.
6 | FAULT_DOING | This bit is set while the fault-reading command is working until it is complete.
5 | FAULT_AUTO_DONE | This bit is set after the execution for the fault auto-reading command is completed.
4 | FAULT_AUTO_DOING | This bit is set while the fault auto-reading command is working until it is complete.
3 | SYNC_AUTO_DONE | This bit is set after the execution for the sync auto-gen command is completed.
2 | SYNC_AUTO_DOING | This bit is set while the sync auto-gen command is working until it is complete.
1 | SYNC_DONE | This bit is set after the execution for the sync-gen command is completed.
0 | SYNC_DOING | This bit is set while the sync-gen command is working until it is complete.
Addr | Default | B15 | B14 | B13 | B12
‘h16 | 0 | LOCAL_RD_DONE | LOCAL_RD_DOING | LOCAL_WR_DONE | LOCAL_WR_DOING
Addr | Default | B5 | B4 | B3 | B2 | B1 | B0
‘h16 | 0 | FAULT_AUTO_DONE | FAULT_AUTO_DOING | SYNC_AUTO_DONE | SYNC_AUTO_DOING | SYNC_DONE | SYNC_DOING
Addr | Default | B11 | B10 | B9 | B8 | B7 | B6
‘h16 | 0 | GLOBAL_WR_DONE | GOLBAL_WR_DOING | LD_TRANS_DONE | LD_TRANS_DOING | FAULT_DONE | FAULT_DOING

## Slide 36
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
COMMAND STATUS 2
RECEIVE STATUS
Bits | Fields | Descriptions
1 | ID_GEN_DONE | This bit is set after the execution for the id-gen command is completed.
0 | ID_GEN_DOING | This bit is set while the id-gen command is working until it is complete.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h17 | 0 | x | x | x | x | x | x | x | x | x | x | x | x | x | x | ID_GEN_DONE | ID_GEN_DOING
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5
‘h18 | 0 | x | FAULT_REC_FAIL | FAULT_AUTO_REC_FAIL | LOCAL_REC_FAIL | x | x | x | x | x | x | FAULT_REC_DONE
Bits | Fields | Descriptions
14 | FAULT_REC_FAIL | This bit is set if any violation happens while the fault-receiving job is working.
13 | FAULT_AUTO_REC_FAIL | This bit is set if any violation happens while the fault auto-receiving job is working.
12 | LOCAL_REC_FAIL | This bit is set if any violation happens while the local read-receiving job is working.
5 | FAULT_REC_DONE | This bit is set after the fault-receiving job is completed.
4 | FAULT_REC_DOING | This bit is set while the fault-receiving job is working until it is complete.
3 | FAULT_AUTO_REC_DONE | This bit is set after the fault auto-receiving job is completed.
2 | FAULT_AUTO_REC_DOING | This bit is set while the fault auto-receiving job is working until it is complete.
1 | LOCAL_REC_DONE | This bit is set after the local read-receiving job is completed.
0 | LOCAL_REC_DOING | This bit is set while the local read-receiving job is working until it is complete.
Addr | Default | B4 | B3 | B2 | B1 | B0
‘h18 | 0 | FAULT_REC_DOING | FAULT_AUTO_REC_DONE | FAULT_AUTO_REC_DOING | LOCAL_REC_DONE | LOCAL_REC_DOING

## Slide 37
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
INTERRUPT STATUS
Bits | Fields | Descriptions
11 | INT_FAULT_REC_FAIL_SRC | This bit shows whether any violation has been happened or not while the fault- receiving job is working until it is complete. This bit value remains at the level even if this register is read-out.
10 | INT_FAULT_AUTO_REC_ FAIL_SRC | This bit shows whether any violation has been happened or not while the fault auto-receiving job is working until it is complete. This bit value remains at the level even if this register is read-out.
9 | INT_LOCAL_REC_FAIL_SRC | This bit shows whether any violation has been happened or not while the local read-receiving job is working until it is complete. This bit value remains at the level even if this register is read-out.
8 | INT_LD_TRANS_SRC | This bit shows whether the LD interrupt has been asserted or not while transferring the LD data to XD-12 drivers through the XC-24 controller. This bit value remains at the level even if this register is read-out.
7 | INT_TML_SRC | This bit shows the thermal status from all XD-12 daisied to enabled channels after completing the fault (auto-) reading command. This bit value remains at the level even if this register is read-out.
6 | INT_SHORT_SRC | This bit shows the short status from all XD-12 daisied to enabled channels after completing the fault (auto-) reading command. This bit value remains at the level even if this register is read-out.
5 | INT_OPEN_SRC | This bit shows the open status from all XD-12 daisied to enabled channels after completing the fault (auto-) reading command. This bit value remains at the level even if this register is read-out.
4 | INT_FB_SRC | This bit shows the fb status from all XD-12 daisied to enabled channels after completing the fault (auto-) reading command. This bit value remains at the level even if this register is read-out.
1 | INT_LD | This high-active bit indicates the nINT_LD pin has been asserted to the low- active level. The INT_LD represents an interrupt sources, INT_LD_TRAN_SRC, if its interrupt enable bits is set. If the INT_LD_EN bit is set and INT_LD_ TRAN_SRC is asserted, then, this bit will be asserted through nINT_LD pin. This bit is auto-cleared after this INTERRUPT STATUS register is read-out.
0 | INT_FAULT | This high-active bit indicates the nINT_FAULT pin has been asserted to the low-active level. The INT_FAULT represents several interrupt sources, INT_FB_SRC, INT_OPEN_SRC, INT_SHORT_SRC, INT_TML_SRC, INT_LOCAL_REC_FAIL_ SRC, INT_FAULT_AUTO_REC_FAIL_SRC and INT_FAULT_REC_FAIL_SRC, if their own interrupt enable bits are set. If the corresponding interrupt enable bit is set and the interrupt source is asserted, then, this bit will be asserted through nINT_FAULT pin. This bit is auto-cleared after this INTERRUPT STATUS register is read-out.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9
‘h19 | 0 | x | x | x | x | INT_FAULT_REC_FAIL_SRC | INT_FAULT_AUTO_REC_FAIL_SRC | INT_LOCAL_REC_FAIL_SRC
Addr | Default | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h19 | 0 | INT_LD_TRAN_SRC | INT_TML_SRC | INT_SHORT_SRC | INT_OPEN_SRC | INT_FB_SRC | x | x | INT_LD | INT_FAULT

## Slide 38
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
DAISY SIZE 1
Bits | Fields | Descriptions
14:10 | DAISY_SIZE_CHx | This register should be set with a valid number for correct operating. The number means how many XD-12 drivers are daisied in those channel. The maximum 31 XD-12 drivers per channel can be daisied.
9:5 | DAISY_SIZE_CHx | The same as above.
4:0 | DAISY_SIZE_CHx | The same as above.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h30 | 0 | x | DAISY_SIZE_CH3 [4:0] | x | x | x | x | DAISY_SIZE_CH2 [4:0] | x | x | x | x | DAISY_SIZE_CH1 [4:0] | x | x |  | 
DAISY SIZE 2
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h31 | 0 | x | DAISY_SIZE_CH6 [4:0] | x | x | x | x | DAISY_SIZE_CH5 [4:0] | x | x | x | x | DAISY_SIZE_CH4 [4:0] | x | x |  | 
DAISY SIZE 3
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h32 | 0 | x | DAISY_SIZE_CH9 [4:0] | x | x | x | x | DAISY_SIZE_CH8 [4:0] | x | x | x | x | DAISY_SIZE_CH7 [4:0] | x | x |  | 
DAISY SIZE 4
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h33 | 0 | x | DAISY_SIZE_CH12 [4:0] | x | x | x | x | DAISY_SIZE_CH11 [4:0] | x | x | x | x | DAISY_SIZE_CH10 [4:0] | x | x |  | 
DAISY SIZE 5
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h34 | 0 | x | DAISY_SIZE_CH15 [4:0] | x | x | x | x | DAISY_SIZE_CH14 [4:0] | x | x | x | x | DAISY_SIZE_CH13 [4:0] | x | x |  | 
DAISY SIZE 6
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h35 | 0 | x | DAISY_SIZE_CH18 [4:0] | x | x | x | x | DAISY_SIZE_CH17 [4:0] | x | x | x | x | DAISY_SIZE_CH16 [4:0] | x | x |  | 
DAISY SIZE 7
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h36 | 0 | x | DAISY_SIZE_CH21 [4:0] | x | x | x | x | DAISY_SIZE_CH20 [4:0] | x | x | x | x | DAISY_SIZE_CH91 [4:0] | x | x |  | 
DAISY SIZE 8
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h37 | 0 | x | DAISY_SIZE_CH24 [4:0] | x | x | x | x | DAISY_SIZE_CH23 [4:0] | x | x | x | x | DAISY_SIZE_CH22 [4:0] | x | x |  | 

## Slide 39
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
BLOCK SIZE 1
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h38 | 0 | BLOCK_SIZE_CH2 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH1 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 2
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h39 | 0 | BLOCK_SIZE_CH4 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH3 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 3
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h3A | 0 | BLOCK_SIZE_CH6 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH5 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 4
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h3B | 0 | BLOCK_SIZE_CH8 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH7 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 5
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h3C | 0 | BLOCK_SIZE_CH10 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH9[7:0] | x | x | x | x | x | x | x
BLOCK SIZE 6
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h3D | 0 | BLOCK_SIZE_CH12 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH11 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 7
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h3E | 0 | BLOCK_SIZE_CH14 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH13 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 8
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h3F | 0 | BLOCK_SIZE_CH16 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH15 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 9
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h40 | 0 | BLOCK_SIZE_CH18 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH17 [7:0] | x | x | x | x | x | x | x

## Slide 40
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
BLOCK SIZE 10
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h41 | 0 | BLOCK_SIZE_CH20 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH19 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 11
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h42 | 0 | BLOCK_SIZE_CH22 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH21 [7:0] | x | x | x | x | x | x | x
BLOCK SIZE 12
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h43 | 0 | BLOCK_SIZE_CH24 [7:0] | x | x | x | x | x | x | x | BLOCK_SIZE_CH23 [7:0] | x | x | x | x | x | x | x
Bits | Fields | Descriptions
15:8 | BLOCK_SIZE_CHx | This register should be set with a valid number for correct operating. The number means how many block zones are daisied in those channel. The maximum 127 block zones per channel can be daisied.
7:0 | BLOCK_SIZE_CHx | The same as above.
DAISIED DEVICE CHANNEL SIZE
Bits | Fields | Descriptions
4:0 | DAISIED_DEV_ CH_SIZE | This register should be set with a valid number for correct operating. The number means how many channels of the XD-12 drivers are to be activated.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h44 | 0 | x | x | x | x | x | x | x | x | x | x | x | DASIED_DEV_CH_SIZE [4:0] | x | x | x | x

## Slide 41
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
CHANNEL ENABLE 1
Bits | Fields | Descriptions
15:0 | CHx_EN | This bit should be set if each corresponding channel is to be activated for the local dimming operation. If any channel is not used, then don’t set its bit.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8
‘h45 | 0 | CH16_EN | CH15_EN | CH14_EN | CH13_EN | CH12_EN | CH11_EN | CH10_EN | CH9_EN
Addr | Default | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h45 | 0 | CH7_EN | CH6_EN | CH5_EN | CH4_EN | CH3_EN | CH2_EN | CH1_EN | CH0_EN
CHANNEL ENABLE 2/ SIZE/ LD WIDTH
Bits | Fields | Descriptions
15:14 | LD_WIDTH | These bits represent the number of bits contained in one LD data in one block zone. 2’b00 : 24 bits/block even if the 24 bits/block are transferred in SPI interface, the valid bits are PAM 10 bits and PWM 10 bits. 2’b01 : 24 bits/block, PAM 10 bits + PWM 11 bits. 2’b10 : 24 bits/block, PAM 10 bits + PWM 12 bits. 2’b11 : 16 bits/block
12:8 | CH_SIZE | These bits represent how many channels are activated.
7:0 | CHx_EN | The same as above CHANNEL ENABLE 1 register.
Addr | Default | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h46 | 0 | CH24_EN | CH23_EN | CH22_EN | CH21_EN | CH20_EN | CH19_EN | CH18_EN | CH17_EN
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8
‘h46 | 0 | LD_WIDTH [1:0] | CH15_EN | x | CH_SIZE [4:0] | CH12_EN | CH11_EN | CH10_EN | CH9_EN
GLOBAL-WRITE DATA
Bits | Fields | Descriptions
11:0 | GLOBAL_WR_ DATA | This register represents the data to be written to the XD-12 drivers daisied. This register should be written with desired value before the global-writing command is executed.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h60 | 0 | x | x | x | x | GLOBAL_WR_DATA [11:0] |  |  |  |  |  |  |  |  |  |  | 

## Slide 42
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
GLOBAL FAULT-READ DATA 1
Bits | Fields | Descriptions
15:12 11:8 7:4 3:0 | FAULT_CHx | These bits represent the fault status from all XD-12 drivers daisied in each channel. FAULT_CHx [3] : The thermal status, all bits from each channel are OR-ed. FAULT_CHx [2] : The short status, all bits from each channel are OR-ed. FAULT_CHx [1] : The open status, all bits from each channel are OR-ed. FAULT_CHx [0] : The fb status, all bits from each channel are OR-ed. The FAULT_CHx [3:1] are auto-cleared after reading the INTERRUPT register, but the FAULT_CHx [0] remains at the level even if the INTERRUPT register is read-out. And the FAULT_CHx [0] value is driven directly to the FB pin.
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h61 | 0 | FAULT_CH4 [3:0] | x | x | x | FAULT_CH3 [3:0] | x | x | x | FAULT_CH2 [3:0] | x | x |  | FAULT_CH1 [3:0] | x | x | x
GLOBAL FAULT-READ DATA 2
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h62 | 0 | FAULT_CH8 [3:0] | x | x | x | FAULT_CH7 [3:0] | x | x | x | FAULT_CH6 [3:0] | x | x |  | FAULT_CH5 [3:0] | x | x | x
GLOBAL FAULT-READ DATA 3
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h63 | 0 | FAULT_CH12 [3:0] | x | x | x | FAULT_CH11 [3:0] | x | x | x | FAULT_CH10 [3:0] | x | x |  | FAULT_CH9 [3:0] | x | x | x
GLOBAL FAULT-READ DATA 4
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h64 | 0 | FAULT_CH16 [3:0] | x | x | x | FAULT_CH15 [3:0] | x | x | x | FAULT_CH14 [3:0] | x | x |  | FAULT_CH13 [3:0] | x | x | x
GLOBAL FAULT-READ DATA 5
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h65 | 0 | FAULT_CH20 [3:0] | x | x | x | FAULT_CH19 [3:0] | x | x | x | FAULT_CH18 [3:0] | x | x |  | FAULT_CH17 [3:0] | x | x | x
GLOBAL FAULT-READ DATA 6
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h66 | 0 | FAULT_CH24 [3:0] | x | x | x | FAULT_CH23 [3:0] | x | x | x | FAULT_CH22 [3:0] | x | x |  | FAULT_CH21 [3:0] | x | x | x

## Slide 43
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
PORT1 LOCAL-RW DATA 1 ~ PORT8 LOCAL RW DATA 1
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h70~’h77 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 1 [11:0] ~ PORT8_LOCAL_RW_DATA 1 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 2 ~ PORT8 LOCAL RW DATA 2
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h78~’h7F | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 2 [11:0] ~ PORT8_LOCAL_RW_DATA 2 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 3 ~ PORT8 LOCAL RW DATA 3
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h80~’h87 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 3 [11:0] ~ PORT8_LOCAL_RW_DATA 3 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 4 ~ PORT8 LOCAL RW DATA 4
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h88~’h8F | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 4 [11:0] ~ PORT8_LOCAL_RW_DATA 4 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 5 ~ PORT8 LOCAL RW DATA 5
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h90~’h97 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 5 [11:0] ~ PORT8_LOCAL_RW_DATA 5 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 6 ~ PORT8 LOCAL RW DATA 6
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘h98~’h9F | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 6 [11:0] ~ PORT8_LOCAL_RW_DATA 6 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 7 ~ PORT8 LOCAL RW DATA 7
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hA0~’hA7 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 7 [11:0] ~ PORT8_LOCAL_RW_DATA 7 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 8 ~ PORT8 LOCAL RW DATA 8
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hA8~’hAF | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 8 [11:0] ~ PORT8_LOCAL_RW_DATA 8 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 9 ~ PORT8 LOCAL RW DATA 9
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hB0~’hB7 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 9 [11:0] ~ PORT8_LOCAL_RW_DATA 9 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 10 ~ PORT8 LOCAL RW DATA 10
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hB8~’hBF | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 10 [11:0] ~ PORT8_LOCAL_RW_DATA 10 [11:0] |  | x | x |  | x | x |  |  | x | x | x

## Slide 44
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
PORT1 LOCAL-RW DATA 12 ~ PORT8 LOCAL RW DATA 12
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hC8~’hCF | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 12 [11:0] ~ PORT8_LOCAL_RW_DATA 12 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 13 ~ PORT8 LOCAL RW DATA 13
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hD0~’hD7 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 13 [11:0] ~ PORT8_LOCAL_RW_DATA 13 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 14 ~ PORT8 LOCAL RW DATA 14
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hD8~’hDF | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 14 [11:0] ~ PORT8_LOCAL_RW_DATA 14 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 15 ~ PORT8 LOCAL RW DATA 15
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hE0~’hE7 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 15 [11:0] ~ PORT8_LOCAL_RW_DATA 15 [11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 16 ~ PORT8 LOCAL RW DATA 16
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hE8~’hEF | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 16 [11:0] ~ PORT8_LOCAL_RW_DATA 16[11:0] |  | x | x |  | x | x |  |  | x | x | x
PORT1 LOCAL-RW DATA 11 ~ PORT8 LOCAL RW DATA 11
Addr | Default | B15 | B14 | B13 | B12 | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
‘hC0~’hC7 | 0 | x | x | x | x | PORT1_LOCAL_RW_DATA 11 [11:0] ~ PORT8_LOCAL_RW_DATA 11 [11:0] |  | x | x |  | x | x |  |  | x | x | x
Bits | Fields | Descriptions
11:0 | PORTX_LOCAL_ RW_DATAY | These registers are used to contain the data to be written/read to/from the XD-12 drivers daisied to each channel for accessing the XD-12 drivers’ registers. These registers should be written before executing the relevant commands, the local-reading or local-writing command. It needs to be careful to use that these registers are differently mapped according to the CH_SEG [1:0] of the LOCAL WRITE/READ COMMAND registers CH_SEG = 2’b00 : PORT1 to PORT8 are mapped to the channel 1 to 8 in order. CH_SEG = 2’b01 : PORT1 to PORT8 are mapped to the channel 9 to 16 in order. CH_SEG = 2’b10 : PORT1 to PORT8 are mapped to the channel 17 to 24 in order. The data order to be transferred to the XD-12 drivers daisied in a channelX : PORTX_LOCAL_RW_DATA1 to the 1st driver, PORTX_LOCAL_RW_DATA2 to the 2nd driver, ….. The data order to be received from the XD-12 drivers daisied in a channelX : PORTX_LOCAL_RW_DATA1 from the last driver, PORTX_LOCAL_RW_DATA2 from the (last -1) driver, ….. Refer to the Figure 10. in detail.

## Slide 45
http://www.glbltech.com/
Confidential

## Slide 46
Package specification
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
TOP VIEW
Symbol | Dimensions in mm |  | 
 | Min | Typ | Max
A | 0.700 | 0.750 | 0.800
A1 | 0.000 | 0.020 | 0.050
A3 | 0.203 REF |  | 
D | 5.900 | 6.000 | 6.100
E | 5.900 | 6.000 | 6.100
D1 | 4.3 | 4.4 | 4.5
E1 | 4.3 | 4.4 | 4.5
k | 0.275 REF |  | 
b | 0.140 | 0.200 | 0.250
e | 0.400 BSC |  | 
Nd | 4.400 BSC |  | 
Ne | 4.400 BSC |  | 
L | 0.350 | 0.400 | 0.450
BOTTOM VIEW
Ne
D1
E1
Nd
L
A
A1
b
e
A3
k
E
D
N1
N4

## Slide 47
Footprint
http://www.glbltech.com/
Confidential
Global Technologies
XC-24
D
B
K
L
PIN #1 0.400x45’’
E
D1
E1
e
Symbol | Dimensions in mm |  | 
 | Min | Nom | Max
A | 0.7 | 0.75 | 0.8
A1 | 0.00 | 0.02 | 0.05
A2 | 0.203 REF |  | 
B | 0.15 | 0.2 | 0.25
D | 5.9 | 6 | 6.1
E | 5.9 | 6 | 6.1
D1 | 4.6 | 4.7 | 4.8
E1 | 4.6 | 4.7 | 4.8
e | 0.4 BSC |  | 
K | 0.25 REF |  | 
L | 0.3 | 0.4 | 0.5

## Slide 48
http://www.glbltech.com/
Confidential
Global Technologies and are trademarks of Solution Korea Company or its subsidiaries in the Republic of Korea and/or other countries. The products of Global Technologies reserve the right to make changes without further notice to any `products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Global Technologies does not convey any license under its patent rights nor the rights of others.
Global Technologies and are trademarks of Solution Korea Company or its subsidiaries in the Republic of Korea and/or other countries. Global Technologies owns the rights to a number of patents, trademarks, copyrights, trade secrets, and other intellectual property. Global Technologies reserves the right to make changes without further notice to any products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Buyer is responsible for its products and applications using Global Technologies products, including compliance with all laws, regulations and safety requirements or standards, regardless of any support or applications information provided by Global Technologies. “Typical” parameters which may be provided in Global Technologies data sheets and/or specifications can and do vary in different applications and actual performance may vary over time. All operating parameters, including “Typical” must be validated for each customer application by customer’s technical experts. Global Technologies does not convey any license under its patent rights nor the rights of others. Global Technologies products are not designed, intended, or authorized for use as a critical component in life support systems or any FDA Class 3 medical devices or medical devices with a same or similar classification in a foreign jurisdiction or any devices intended for implantation in the human body. Should Buyer purchase or use Global Technologies products for any such unintended or unauthorized application, Buyer shall indemnify and hold Global Technologies and its officers, employees, subsidiaries, affiliates, and distributors harmless against all claims, costs, damages, and expenses, and reasonable attorney fees arising out of, directly or indirectly, any claim of personal injury or death associated with such unintended or unauthorized use, even if such claim alleges that Global Technologies was negligent regarding the design or manufacture of the part. Global Technologies is an Equal Opportunity/Affirmative Action Employer. This literature is subject to all applicable copyright laws and is not for resale in any manner.
Global Technologies
XC-24