## Slide 1
XD12
The LED Current Sink Driver IC
General Description
The XD12 is a compact IC featuring 12-channel current sink control drivers optimized for LED lighting solution. The XD12 driver is used together with a XC24 controller as a companion chip. A lot of the XD12 drivers can be daisied each other to the XC24 channels and controlled through a serial interface by a XC24 controller.
The XD12 supports a feedback control for the LED power efficiency, and self-protection features like as a thermal protection and a LED Open/Short fault monitoring.
12 Channels
Application
LED back-lighting with local dimming control
Global Technologies

## Slide 2
XD12
Feature
Bi-directional 1-wire interface and configurable transmit rate
Daisied connection between devices and pin layout for designing single layer PCB
12 independent dimming control channels in a package
Maximum 40V headroom voltage
Configurable device’s max output current level (4/8/12/16/24/32/46/64mA)
12-bit max current control for dimming
16-bit brightness control in the 12-bit max current level
Support configurable black sub-frame insertion
Sink current accuracy ±2%
Sync controllability between devices
Flicker-less frame frequency switching
Configurable LED open detection and protection
Configurable LED short detection level (3/4/6/8/12/16/24/36V) and protection
Configurable FB operation level (0.4/0.5/0.6/0.7/0.85/1.0/1.15/1.3V)
Configurable over-temperature protection @ 130℃
Supply voltage 5.0V
24-PIN QFN 3030 package
Latch-up Immunity, ILATCH (JEDEC JESD78D Nov 2011) : ±100mA
ESD protection, ESDHBM (Norm: MIL 883 E Method 3015 Human Body Model) : ±2kV

## Slide 3
Application Circuit
Block Diagram
XD12
XC24
Fig. 1 Block Diagram
Fig. 2 Application Circuit

## Slide 4
Pin diagram (Top View)
XD12
Pin Name | Pin No. | I/O | Type | Description | Remark
VDD | 1 | - | Power | Supply voltage | 
VSS | 2 | - | GND | Ground | 
VSS | 3 | - | GND | Ground | 
DIO | 4 | I/O | Digital | Data In/Out | Internal PD, 48KΩ
VSS | 5 | - | GND | Ground | 
VSS | 6 | - | GND | Ground | 
O2 | 7 | O | Current Load | Current Sink 2 | If unused, connect to GND
O4 | 8 | O | Current Load | Current Sink 4 | If unused, connect to GND
O6 | 9 | O | Current Load | Current Sink 6 | If unused, connect to GND
O8 | 10 | O | Current Load | Current Sink 8 | If unused, connect to GND
O10 | 11 | O | Current Load | Current Sink 10 | If unused, connect to GND
O12 | 12 | O | Current Load | Current Sink 12 | If unused, connect to GND
VSS | 13 | - | GND | Ground | 
VSS | 14 | - | GND | Ground | 
Pin description
Fig. 3 Pin diagram
Table 1. Pin Description

## Slide 5
XD12
Pin Name | Pin No. | I/O | Type | Description | Remark
DDIO | 15 | I/O | Digital | Daisied Data In/Out | Internal PD, 48KΩ
VSS | 16 | - | GND | Ground | 
VSS /FB 1) | 17 | O | Digital | Open-drain output | If unused, connect to GND
VDD | 18 | - | Power | Supply Voltage | 
O11 | 19 | O | Current Load | Current Sink 11 | If unused, connect to GND
O9 | 20 | O | Current Load | Current Sink 9 | If unused, connect to GND
O7 | 21 | O | Current Load | Current Sink 7 | If unused, connect to GND
O5 | 22 | O | Current Load | Current Sink 5 | If unused, connect to GND
O3 | 23 | O | Current Load | Current Sink 3 | If unused, connect to GND
O1 | 24 | O | Current Load | Current Sink 1 | If unused, connect to GND
Pin description
Equivalent Circuits of individual pins
Pad Name | I/O | Internal Circuit | Description
VDD | - |  | Supply voltage
DIO | I/O |  | Data In/Out
DDIO | I/O |  | Daisied Data In/Out
Note : 1) In case of using as a FB out signal, it needs to set the FBOUT_E bit. If not using, it is recommended to
connect to GND. The FB out is an open-drain port.

## Slide 6
XD12
Equivalent Circuits of individual pins
Pad Name | I/O | Internal Circuit | Description
O1 ~ O12 | Current Sink |  | Current Load
VSS | - |  | Ground
VDD
Fig. 4 Equivalent Circuits of individual pins

## Slide 7
XD12
Maximum Absolute ratings (Ta = 25℃ unless otherwise noted)
Stresses beyond the Maximum Absolute ratings may cause permanent damage to the device
Note : 1) Surface mounted on FR-4 substrate PC Board 1” x 1” inch 2-oz copper plate
Parameter | Symbol | Value | Unit
Supply voltage | VDD | -0.3 ~ 6.5 | V
Sink output pin voltage | VO | 40 | V
Sink output current | IO | 64 | mA
DIO to GND | VDIO | -0.3 ~ VDD+0.3 | V
DDIO to GND | VDDIO | -0.3 ~ VDD+0.3 | V
Thermal Resistance |  |  | 
Junction to Ambient | RθJA | TBD 1) | ℃/W
Junction to Case | RθJC | TBD 1) | ℃/W
Power Dissipation on package | PTOT | TBD 1) | W
Junction temperature | TJ | -20 ~ 150 | ℃
Storage temperature | TSTG | -45 ~ 150 | ℃
Relative Humidity (non-condensing) | RHNC | 5 ~ 85 | %
Moisture Sensitivity | MSL | Maximum Floor Life-time | 3
Parameter | Symbol | Value | Unit | Remark
Electrostatic Discharge HBM ; Contact | ESDHBM | ±2K | V | C=100 pF, R=1.5 kΩ
Electrostatic Discharge CDM ; Contact | ESDCDM | ±500 | V | R=1 Ω
Electrostatic Discharge
Table 3. Electrostatic Discharge
Table 2. Maximum Absolute ratings

## Slide 8
XD12
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
Supply voltage |  |  |  |  |  | 
Operating voltage | VDD1) |  | 4.5 | 5.0 | 5.5 | V
Supply current |  |  |  |  |  | 
Quiescent Current | Is | Standby state, No LED current | - | - | 1.7 | mA
Operating Current 1 | IDD1 | All output sink current = 4mA | - | - | 1.8 | mA
Operating Current 2 | IDD2 | All output sink current = 8mA | - | - | 2.0 | mA
Operating Current 3 | IDD3 | All output sink current = 12mA | - | - | 2.2 | mA
Operating Current 4 | IDD4 | All output sink current = 16mA | - | - | 2.4 | mA
Operating Current 5 | IDD5 | All output sink current = 24mA | - | - | 2.8 | mA
Operating Current 6 | IDD6 | All output sink current = 32mA | - | - | 3.2 | mA
Operating Current 7 | IDD7 | All output sink current = 46mA | - | - | 3.8 | mA
Operating Current 8 | IDD8 | All output sink current = 64mA | - | - | 4.8 | mA
Oscillator |  |  |  |  |  | 
Internal MCLK | fOSC |  | -3% | 14.746 | +3% | MHz
In/Out |  |  |  |  |  | 
DIO, DDIO | VIL VIH | Input logic low level | - | - | 0.5 | V
 |  | Input logic high level | VDD * 0.8 | - | VDD | 
 | VOL VOH | Output logic low level | - | - | 0.5 | V
 |  | Output logic high level | VDD * 0.8 | - | VDD | 
 | RPD | Internal pull-down resistance | - | 48 | - | KΩ
Logic high time 2) | T1H, T0L |  | 6 | 8 | 20 | MCLK
Logic low time 2) | T1L, T0H |  | 3 | 4 | 10 | MCLK
Propagation delay | TD_DS | Downstream (DIO to DDIO) | - | - | 2.5 | ns
Propagation delay | TD_US | Upstream (DDIO to DIO) | - | - | 3.0 | ns
Electrical Characteristic (VDD =5.0V, Ta=25.0℃ unless otherwise noted)
Note : 1) The operation below VDD, 5V will limit a maximum LED sinking current and affect a current variation.
2) T1H ≥ T0H * 2, T0L ≥ T1L * 2, (T1H + T0H) = (T0L + T1L) ≤ 31
Logic ‘1’
Logic ‘0’
T1H
T0H
T1L
T0L
Table 4. Electrical Characteristic

## Slide 9
XD12
Electrical Characteristic (VDD =5.0V, Ta=25.0℃ unless otherwise noted)
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
Output |  |  |  |  |  | 
Driving voltage | VO | Headroom voltage VHD : 0.60V@ IO 4mA, 0.65V@ IO 8mA 0.70V@ IO 12mA, 0.75V@ IO 16mA 0.80V@ IO 24mA, 0.85V@ IO 32mA 0.90V@ IO 46mA, 0.90V@ IO 64mA | VHD | - | 40 | V
Short detection voltage 3) | VSD | Short detection level VSD : 3b’000=3V, 3b’001=4V 3b’010=6V, 3b’011=8V 3b’100=12V, 3b’101=16V 3b’110=24V, 3b’111=36V | VSD | - | - | V
Open detection voltage 3) | VOD |  | - | - | 0.25 | V
Sink current | IO | Device max current level : IO 3’b000 = 4mA, 3’b001 = 8mA 3’b010 = 12mA, 3’b011 = 16mA 3’b100 = 24mA, 3’b101 = 32mA 3’b110 = 46mA, 3’b111 = 64mA | - | - | 64 | mA
Current accuracy 4) | % | @ IO =Imax(8mA)*0.02 | -2 | - | +2 | %
 |  | @ IO = Imax(8mA)*0.1 | -2 | - | +2 | %
 |  | @ IO = Imax(8mA)*1 | -2 | - | +2 | %
LED off current | IOFF | Vo = 40V | - | - | 300 | nA
Feedback |  |  |  |  |  | 
FB threshold voltage (Logically ORed for 12-ch) | VFBA | FB level VFBA : 3’b000 = 0.40V, 3’b001 = 0.50V 3’b010 = 0.60V, 3’b011 = 0.70V 3’b100 = 0.85V, 3’b101 = 1.00V 3’b110 = 1.15V, 3’b111 = 1.30V | - | VFBA | - | V
FB hysteresis voltage | VFBH |  | 40 | 60 | 110 | mV
Thermal protection |  |  |  |  |  | 
Thermal cut off @TJ | TCUT | OFS_TEMP [3:0] = 0x8 | - | 130 | - | ℃
Thermal cut off hysteresis @TJ | THYS |  | 20 | 30 | 40 | ℃
Note : 3) If LED open or short event is happened, the corresponding channel will be turned-off under the function
enabled. If the thermal is happened, all channels output will be turned-off under the function enabled.
4) Under satisfying the power dissipation specification.

## Slide 10
XD12
Electrical Characteristic (VDD =5.0V, Ta=25.0℃ unless otherwise noted)
Characteristics | Symbol | Condition | Value |  |  | Unit
 |  |  | min | typ | max | 
VDD, VLED ramp up |  |  |  |  |  | 
VDD Ramp up time | TVDD |  |  |  | 1 | ms
VLED Ramp up time | TVLED |  | > TVDD |  |  | ms
Initialization after VDD, 5V stable |  |  |  |  |  | 
Internally required Init | TINIT |  | 5 |  |  | ms
Allowed 1st command | TFCMD |  | 5 |  |  | ms
Timeout : Internal timer starts after completing to receive a read-back command and stops after first response bit from a last daisied device |  |  |  |  |  | 
Internal Timeout 5) | TTIMEOUT |  | 539 | 556 | 573 | us
Note : 5) If the timeout will be expired, the internal communication logic will go to an initial state, so new command
transaction will be possible. The timeout function is configurable.
TVDD
TINIT
VDD
5V
Possible to receive commands
VLED
VLEDV
TVLED
(XD12 Power supply voltage)
(LED Source supply voltage)
Fig. 5 Power up sequence timing
Power Sequence
Important statement
Global Technologies reserves the right to change the above-mentioned information without prior notice.

## Slide 11
1. Dimming in Normal mode
XD12
Local dimming sequence
Fig.6 Head lighting
Dimming data
LD_MODE/LD_DIR
MAX_CURR_VREF
SF_PERIOD
SF_BFI_SIZE
Fig.7 Tail lighting
2. Dimming in X8 mode
Fig.8 Head lighting
Fig.9 Tail lighting
These data will be applied at a next vsync after being transmitted

## Slide 12
Register Map
XD12
Bits | Fields |  | Descriptions
0 | RST | 0 1 | NOP All internal logics are initialized to a default state and this bit will be auto-cleared after initializing.
4:0 | ID |  | If the XD12 will receive the ID-Gen command from the XC24 controller, then the ID value is automatically generated. The ID value is needed for proper reading, so, the ID-Gen command must be firstly executed by the XC24 controller before executing any commands. If all XD12 drivers daisied will receive the ID-Gen command, the last-located device will have the first number of ID, and the first located device will have the last number of ID, that is, the number of daisied devices. The ID value can not be written by a Host.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x00 | 0x000 | RST | x | x | x | x | x | x | ID [4:0] |  |  |  | 
RESET / ID
Bits | Fields |  | Descriptions
 |  |  | This register determines the dimming sequence. Even if the LD_MODE and LD_DIR value will be changed in the middle of current frame, the dimming sequence will keep the current mode to complete the current frame until a next frame start, and then, the new frame according to the changed LD_MODE or LD_DIR will begin dimming at a next SYNC command.
4 | LD_DIR | 0 1 | This bit determines the direction of modulated edge with increasing on time from a internal vsync. For details, refer to Fig. 6,7,8 and 9. Head Shift Lighting Tail Shift Lighting
0 | LD_MODE | 0 1 | This bit determines the dimming mode, Normal or X8 mode. The Normal mode is for general dimming sequence and the X8 mode is for 8 times repeated dimming sequence in one frame. For details, Fig. 6,7,8 and 9. Normal mode X8 mode
LD MODE
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x01 | 0x000 | x | x | x | x | x | x | x | LD_DIR | x | x | x | LD_MODE

## Slide 13
Bits | Fields | Descriptions
11:0 | SF_PERIOD | This register determines the length of sub-frame shown in Fig. 6, and if the value will be changed in the middle of a frame, the value will be applied in the next frame. Therefore, this advantage will be useful to switch the frame period during dimming without any flicker. If the value will be increased or decreased gradually to be met the changed frame period,100↔120hz, it results in nearly flicker-less. It needs to be careful to determine the SF_PERIOD that the value should be an integer number after being calculated by a follow formula : SF_PERIOD = (the frame period / SF_SIZE) / MCLK
SF PERIOD
Bits | Fields | Descriptions
7:0 | SF_SIZE | The SF_SIZE determines the total number of sub-frames in one frame shown in Fig. 6.
SF SIZE
Bits | Fields | Descriptions
10:7 | CH_SIZE | This value determines how many LD data will be transmitted for one time. This value is not needed to match with the number of enabled channels in the CHANNEL ENABLE register. The LD data to be transmitted will be mapped sequentially from channel 1 to channel n regardless of the corresponded CHx_EN bit activation.
4:0 | SF_X8_SIZE | The SF_X8_SIZE determines the number of sub-frame to be repeated 8 times in a frame, so the set value must be divided the SF_SIZE by 8. For more details, refer to the Fig. 8
XD12
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x02 | 0x000 | SF_PERIOD [11:0] |  |  |  |  | DELAY_SIZE [6:0] | x | x | x | x | x | LD_FORCE
CH SIZE / SF X8 SIZE
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x03 | 0x000 | x | x | x | x | SF_SIZE [7:0] |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x04 | 0x000 | x | CH_SIZE [3:0] |  |  |  | x | x | SF_X8_SIZE [4:0] |  |  |  | 
Bits | Fields | Descriptions
7:0 | SF_BFI | The SF_BFI_SIZE determines how many sub-frames are turned-off in a frame. The number should be less than the SF_SIZE in a Normal mode and the SF_X8_SIZE in a X8 mode and can be set to 0 to fully turn-on for a frame time. Even if the value will be changed, the value is kept until completing the current frame, and applied from a next frame. For more details, refer to the Fig. 6,7,8,9 and the number of sub-frame turned-on is as follows : = (SF_SIZE – SF_BFI_SIZE) @ Normal mode = (SF_X8_SIZE – SF_BFI_SIZE) @ X8 mode
SF BFI SIZE
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x05 | 0x000 | x | x | x | x | SF_BFI_SIZE [7:0] |  |  |  |  |  |  | 

## Slide 14
Bits | Fields | Descriptions
11:0 | CHx_EN | The CHx_EN determines which channel will be activated. The set value is independent of the value of the CH_SIZE. If the CHx_EN is not set, then the corresponding channel sink output including the its faults, OPENx, SHORTx, FBx, will be deactivated. The CHx_EN bits should be set consecutively, such as CH1_EN, CH2_EN, CH3_EN, and so on, and the number of enabled channels does not need to match the CH_SIZE value.
MAX CURRENT VREF
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x09 | 0x000 | CH12_EN | CH11_EN | CH10_EN | CH9_EN | CH8_EN | CH7_EN | CH6_EN | CH5_EN | CH4_EN | CH3_EN | CH2_EN | CH1_EN
XD12
Bits | Fields | Descriptions
11:0 | MAX_CURR_VREF | The MAX_CURR_VREF determines the maximum current value of a frame to be dimmed. If the max current level is set to 8mA, then the MAX_CURR_VREF value is proportional to the max current level, and so this value decides the max current reference of all blocks being dimmed for a frame. The set value will come into effect at the next internal vsync assertion even if the value is set during current dimming frame earlier than the next vsync.
CHANNEL ENABLE
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x08 | 0x000 | MAX_CURR_VREF [11:0] | x | x | x | x | x | x | x | x | x | RST2 | RST1
Bits | Fields | Descriptions
15:0 | LD_FIX | The LD_FIX register is used to continuously out a fixed value written in this register instead of LD data to be transmitted form a Host, regardless of the frame sync signal. This function is used only for device testing and activated when the TEST_EN bit and the LD_FIX_EN bit are all set.
LD FIX 1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x07 | 0x000 | x | x | x | x | x | x | x | x | LD_FIX [15:12] | x | x | LD_FORCE
LD FIX 2
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x06 | 0x000 | LD_FIX [11:0] | x | x | x | x | x | x | x | LD_FIX [15:12] | x | x | LD_FORCE

## Slide 15
Bits | Fields | Descriptions
10:8 | DEV_MAX_CURR_ LEVEL | The DEV_MAX_CURR_LEVEL determines the physical maximum current level of the device. The max dimming sink-current set by the MAX_CURR_VREF can not be beyond the DEV_MAX_CURR_LEVEL. 3b’000 : max 4mA 3b’011 : max 16mA 3b’110 : max 46mA 3b’001 : max 8mA 3b’100 : max 24mA 3b’111 : max 64mA 3b’010 : max 12mA 3b’101 : max 32mA
6:4 | SHORT_LEVEL | The SHORT_LEVEL determines the level at which a SHORT event occurs. 3b’000 : above 3V 3b’011 : above 8V 3b’110 : above 24V 3b’001 : above 4V 3b’100 : above 12V 3b’111 : above 36V 3b’010 : above 6V 3b’101 : above 16V
2:0 | FB_LEVEL | The FB_LEVEL determines the level at which a FB event occurs. 3b’000 : below 0.40V 3b’011 : below 0.70V 3b’110 : below 1.15V 3b’001 : below 0.50V 3b’100 : below 0.85V 3b’111 : below 1.30V 3b’010 : below 0.60V 3b’101 : below 1.00V
FAULT LEVEL
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0C | 0x000 | x | DEV_MAX_CURR_LEVEL [2:0] | x | x | x | SHORT_LEVEL [2:0] | x | x | x | FB_LEVEL [2:0] | FB_LEVEL [1:0] | 
XD12
Bits | Fields | Descriptions
3 | THERMAL | The THERMAL bit indicates whether the XD12 device has internally a thermal event from overheating due to high current for a long time. This bit will keep asserted as long as the internal THERMAL event is not cleared. The THERMAL threshold can be set by the OFS_TEMP of the LD CONTROL register. If the T_OFF_E bit of the FAULT MODE register is set, all output sink drivers will be turned-off under the THERMAL bit is set until the internal temperature goes down below the set level of the OFS_TEMP.
2 | SHORT | The SHORT bit indicates whether the XD12 output pin is short to a VLED line due to any soldering condition. The detection condition can be set by the SHORT_LEVEL of the FAULT LEVEL register and the SHORT ENABLE LEVEL register. This bit is set when the SHORT_DEC_EN1/2 bit is set and the SHORT event occurs in even one of the activated channels, and then, will be auto-cleared after readout this register, but the bit will be set again as long as the SHORT event is still valid. If the S_OFF_E bit of the FAULT MODE register is set, the corresponding output sink driver will be turned-off under this bit is set until the event is cleared.
1 | OPEN | The OPEN bit indicates whether the XD12 output pin is open in spite of being activated. The open level is fixed to 0.25V. This bit is set when the OPEN_DEC_EN bit is set and the OPEN event occurs in even one of the activated channels and then, will be auto-cleared after readout this register, but the bit will be set again as long as the OPEN event is still valid. If the O_OFF_E bit of the FAULT MODE register is set, the corresponding output sink driver will be turned-off under this bit is set until the event is cleared. It needs to follow below to determine the validity of the OPEN event. * in case that the OPEN and FB are simultaneously-asserted even if the LD data are all 0 * in case that the OPEN and FB are simultaneously-asserted even if the VLED remains at the max level for a long time.
0 | FB | The FB bit indicates whether the XD12 output pin’s headroom voltage is below the value set by FB_LEVEL of the FAULT LEVEL register. This bit is set when a FB event occurs in even one of the activated channels and then, will be auto-cleared after readout this register. This bit will be set again after readout as long as the FB event is still valid.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
RO | 0x0B | 0x000 | x | x | x | x | x | x | x | x | THERMAL | SHORT | OPEN | FB
FAULT STATUS

## Slide 16
XD12
Bits | Fields |  | Descriptions
11 | TIMEOUT_EN | 0 1 | The timeout function is disabled. So, if the device will not receive any response from other daisied devices on any read-back commands execution, internal communication logics can not recover its function to the standby state. Recommend this bit to be set. Internal timeout timer start counting from completion of some read-back commands and stops after receiving the first response bit from daisied devices. Even if the timer will be expired due to any no response, internal communication logics will be recovered to standby state in order to be possible to communicate again. The timeout will be expired at the time of MCLK * 8,192 and recommended to be set.
10 | FBOUT_E | 0 1 | NOP If this bit is set under the TEST_EN disabled, the FBOUT signal, active-low, will be driven out directly to the open-drain pin #17. The FBOUT represents the internal FB status of active channels in real time unlike the FB value in the FAULT STATUS register.
5 | OPEN_DET_EN | 0 1 | The LED OPEN detection is disabled. The LED OPEN detection can work under only the LD data are all zeros. In case that the LD data are all zero and the output headroom goes below 0.25V, then the OPEN event will be asserted.
4 | SHORT_DET_EN2 | 0 1 | The LED SHORT detection is disabled. The LED SHORT detection can work under only the LD data’s MSB 5 bits are not all zeros. In case that MSB 4 bits are not all zeros and the SHORT_LEVEL is set to 3V, the SHORT event will be asserted if the corresponding channel’s headroom goes above 3V.
3 | SHORT_DET_EN1 | 0 1 | The LED SHORT detection is disabled. The LED SHORT detection can work under only the LD data’s MSB 4 bits are not all zeros. In case that MSB 4 bits are not all zeros and the SHORT_LEVEL is set to 3V, the SHORT event will be asserted if the corresponding channel’s headroom goes above 3V.
2 | T_OFF_EN | 0 1 | Even if the THERMAL event happens, all channels’ output will be not off, but the flag can be visible through the FAULT STATUS register. If the THERMAL event happens, all channels’ output will be off, and the flag can be visible through the FAULT STATUS register. It is recommended to be set for a safety and for the operating condition, refer to the Electrical characteristics.
1 | S_OFF_EN | 0 1 | Even if the LED SHORT event happens, the corresponding channel output will be not off, but the flag can be visible through the FAULT STATUS register. If the LED SHORT event happens, the corresponding channel output will be off, and the flag can be visible through the FAULT STATUS register. The LED short detection condition can be configurable through the SHORT_LEVEL, the S1_EN bit and S2_EN bit is set. It is recommended to be set for a safe operation.
0 | O_OFF_EN | 0 1 | Even if the LED OPEN event happens, the corresponding channel output will be not off, but the flag can be visible through the FAULT STATUS register. If the LED OPEN event happens, the corresponding channel output will be off, and the flag can be visible through the FAULT STATUS register. The LED OPEN event can be detected if the channel headroom goes down below 0.25V.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0D | 0x800 | TIMEOUT_EN | FBOUT_E | x | x | x | x | O_EN | S2_EN | S1_EN | T_OFF_EN | S_OFF_EN | O_OFF_EN
FAULT MODE

## Slide 17
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0E | 0x000 | x | x | x | x | DELAY_CH1 [7:0] | x | x | x | x | x | x | x
DELAY_CH1
DELAY_CH2
DELAY_CH3
DELAY_CH4
DELAY_CH5
DELAY_CH6
DELAY_CH7
DELAY_CH8
DELAY_CH9
DELAY_CH10
XD12
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0F | 0x000 | x | x | x | x | DELAY_CH2 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x10 | 0x000 | x | x | x | x | DELAY_CH3 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x11 | 0x000 | x | x | x | x | DELAY_CH4 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x12 | 0x000 | x | x | x | x | DELAY_CH5 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x13 | 0x000 | x | x | x | x | DELAY_CH6 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x14 | 0x000 | x | x | x | x | DELAY_CH7 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x15 | 0x000 | x | x | x | x | DELAY_CH8 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x16 | 0x000 | x | x | x | x | DELAY_CH9 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x17 | 0x000 | x | x | x | x | DELAY_CH10 [7:0] | x | x | x | x | x | x | x

## Slide 18
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x27 | 0x848 | OFS_TEMP [3:0] |  |  |  | x | ICTL_GLB [2:0] |  |  | BGR_CTL [3:0] | x | x | x
DELAY_CH11
DELAY_CH12
Bits | Fields | Descriptions
7:0 | DELAY_CHx | The DELAY_CHx determines from which sub-frame to start dimming out. If this is set to n, then the dimming out starts at (n+1)th sub-vsync. Normally, the value can not exceed the (SF_SIZE-1) value. For more details, refer to the Figure. 6,7,8,9.
XD12
SERIAL CLOCK GEN
LD CONTROL
Bits | Fields | Descriptions
11:8 | SERIAL_CLK_LOW | These bits determine the number of MCLK of VDD level in logic low value ‘0’ or the number of MCLK of zero level in logic high value ‘1’ when the XD12 is driving the DIO pin on read-back. For more details, refer to Table. 4, Logic low time.
4:0 | SERIAL_CLK_HIGH | These bits determine the number of MCLK of VDD level in logic high value ‘1’ or the number of MCLK of zero level in logic low value ‘0’ when the XD12 is driving the DIO pin on read-back. For more details, refer to Table. 4, Logic high time.
DCLK PERIOD
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x18 | 0x000 | x | x | x | x | DELAY_CH11 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x19 | 0x000 | x | x | x | x | DELAY_CH12 [7:0] | x | x | x | x | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x28 | 0x000 | DCLK_RST_E | x | DCLK_PERIOD [9:0] |  |  |  |  |  |  | x | x | x
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x26 | 0x408 | SERIAL_CLK_LOW [3:0] |  |  |  | x | x | x | SERIAL_CLK_HIGH [4:0] |  | x | x | x
Bits | Fields | Descriptions
 |  | It is recommended to use the default value
Bits | Fields | Descriptions
11 | DCLK_RST_E | If this bit is set, the DCLK_PERIOD counter will be reset at every internal vsync. It is recommended to be set for expressing precise gradation at every frame sync.
9:0 | DCLK_PERIOD | An integer multiple of the DCLK_PERIOD must be equal to the SF_PERIOD. It is recommended to be set from 64 to 128 but depends on the system performance. Even if the SF_PERIOD value becomes different according to the frame period, it is better to select a value among 64 ~ 128 that can meet an integer multiple of the SF_PERIOD.

## Slide 19
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x2C | 0x080 | x | OSC_COMP_TH_P [10:0] |  |  |  |  |  |  |  |  |  | 
MCLK LOCK
Bits | Fields | Descriptions
11 | MCLK_LOCK_E | The MCLK LOCK function is used to calibrate the internal oscillator (=MCLK) to a target frequency owing to the temperature variation in a real-time, but for use, the exact period of SYNC commands must be continuously supplied to a XD. It should be careful that this bit must be cleared to 0 when changing the frame period, 100↔120hz, or free-sync mode especially. This bit should only be used when the SYNC command intervals are regular. This bit value will be refreshed with a written value at every internal vsync signal. 0 MCLK_LOCK function disabled 1 MCLK_LOCK function enabled
17:0 | MCLK_LOCK | The value determines the number of MCLKs between the SYNC commands. = SYNC command period (=frame period) / MCLK
XD12
OSC COMPENSATION
OSC COMPENSATION THRESHOLD POSITIVE / NEGATIVE
Bits | Fields | Descriptions
11 | OSC_POL | The compensation polarity 0 Positive characteristics 1 Negative characteristics
4:0 | OSC_COMP | This register is containing the current compensated value during MCLK_LOCK_E=1, and the value will be kept even if the MCLK_LOCK_E becomes disabled. If this register will be written to some value in the middle of working, the compensating start newly from the written value.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x29 | 0x000 | MCLK_LOCK [11:0] |  |  |  |  |  |  |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x2A | 0x01E | MCLK_LOCK_E | x | x | x | x | x | MCLK_LOCK [17:12] |  |  |  |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x2B | 0x00F | OSC_POL | x | x | x | x | x | x | OSC_COMP [4:0] |  |  |  | 
Bits | Fields | Descriptions
10:0 | OSC_COMP_TH_P OSC_COMP_TH_N | This value means the threshold that determines what to do with the compensation. The MCLK will be faster or slower 80khz per 184. Normally, it is recommended to use the default value. 1. In case of MCLK_LOCK > internal mclk counting value : if the difference > OSC_COMP_TH_P, then increase OSC_COMP by 1 and result in MCLK faster 2. In case of MCLK_LOCK < internal mclk counting value : if the difference > OSC_COMP_TH_N, then decrease OSC_COMP by 1 and result in MCLK slower 3. Else : keep the current state 4. The signs in the above equation, + and -, is exchanged each other if the OSC_POL is set.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x2D | 0x200 | x | OSC_COMP_TH_N [10:0] |  |  |  |  |  |  |  |  |  | 

## Slide 20
OP MODE
Bits | Fields |  | Descriptions
11 | TEST_EN | 0 1 | Normal operation For testing, there are two purposes for use as follows : 1. The MCLK divided by 16 is output to the DDIO pin for trimming the internal OSC. 2. Specially used with the LD_FIX_EN bit.
7 | LD_FIX_EN | 0 1 | Normal operation For testing, there are two purposes for use with the TEST_EN bit=1 as follows : 1. The MAX_CURR_VREF reg value is continuously out to a current control logics. 2. The LD_FIX value is continuously out to a current control logics without sync signals.
0 | ADDR_EXT | 0 1 | This bit is used to select which register group, the general registers or the OTP mirror registers, will be accessed. The OTP control registers address, 0x3A ~ 0x3F, can be commonly accessed regardless of this bit. The general registers can be accessed except for the OTP mirror registers. The OTP mirror registers can be accessed except for the general registers.
XD12
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3F | 0x0 | TEST_EN | x | x | x | LD_FIX_EN | x | x | x | x | x | x | ADDR_EXT
OTP ACCESS
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3C | 0x04 | x | x | x | x | x | x | x | x | OTP_WSEL [3:0] | SHORT | OPEN | FB
OTP WRITE
OTP RD/PROG
OTP PROTECT
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3E | 0x5A5 | PROTECT_EN/DIS [11:0] ※ enable (0x5A5), disable (0xA5A), need to disable for writing | x | x | x | x | x | x | ID [4:0] | x | x | RST2 | RST1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3B | 0x140 | OTP_PG_ACCESS_CYCLE [11:0] | x | x | x | x | x | x | ID [4:0] | x | x | RST2 | RST1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3A | 0x000 | x | x | x | x | x | x | x | x | OTP_PG_ACCESS_CYCLE [15:12] | x | x | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x3D | 0x000 | x | x | x | x | x | x | x | x | x | x | OTP_RD_START | OTP_PG_START
These registers can not go outside the Global Technologies.
OTP CRC
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x00 | 0x000 | x | x | x | x | OTP_CRC_CHECKSUM [7:0] | x | x | x | x | x | x | x

## Slide 21
These registers can not go outside the Global Technologies.
XD12
VREF CTL
OSC
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x02 | 0x10 | x | x | x | x | x | x | x | VREF_CTL [4:0] | x | x |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x03 | 0x40 | x | x | x | x | x | OFS_CH1 [6:0] | x | x | x | x |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x01 | 0x40 | x | x | x | x | x | OSC [6:0] | x | x | x | x |  | 
OFS 1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x04 | 0x40 | x | x | x | x | x | OFS_CH2 [6:0] | x | x | x | x |  | 
OFS 2
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x05 | 0x40 | x | x | x | x | x | OFS_CH3 [6:0] | x | x | x | x |  | 
OFS 3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x06 | 0x40 | x | x | x | x | x | OFS_CH4 [6:0] | x | x | x | x |  | 
OFS 4
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x07 | 0x40 | x | x | x | x | x | OFS_CH5 [6:0] | x | x | x | x |  | 
OFS 5
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x08 | 0x40 | x | x | x | x | x | OFS_CH6 [6:0] | x | x | x | x |  | 
OFS 6
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x09 | 0x40 | x | x | x | x | x | OFS_CH7 [6:0] | x | x | x | x |  | 
OFS 7
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0A | 0x40 | x | x | x | x | x | OFS_CH8 [6:0] | x | x | x | x |  | 
OFS 8
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0B | 0x40 | x | x | x | x | x | OFS_CH9 [6:0] | x | x | x | x |  | 
OFS 9
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0C | 0x40 | x | x | x | x | x | OFS_CH10 [6:0] | x | x | x | x |  | 
OFS 10
OFS 11
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0D | 0x40 | x | x | x | x | x | OFS_CH11 [6:0] | x | x | x | x |  | 

## Slide 22
XD12
GAIN 1
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1C | 0x40 | x | x | x | x | x | GAIN_CH2 [6:0] | x | x | x | x |  | 
GAIN 2
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1D | 0x40 | x | x | x | x | x | GAIN_CH3 [6:0] | x | x | x | x |  | 
GAIN 3
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1E | 0x40 | x | x | x | x | x | GAIN_CH4 [6:0] | x | x | x | x |  | 
GAIN 4
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1F | 0x40 | x | x | x | x | x | GAIN_CH5 [6:0] | x | x | x | x |  | 
GAIN 5
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x20 | 0x40 | x | x | x | x | x | GAIN_CH6 [6:0] | x | x | x | x |  | 
GAIN 6
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x21 | 0x40 | x | x | x | x | x | GAIN_CH7 [6:0] | x | x | x | x |  | 
GAIN 7
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x22 | 0x40 | x | x | x | x | x | GAIN_CH8 [6:0] | x | x | x | x |  | 
GAIN 8
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x23 | 0x40 | x | x | x | x | x | GAIN_CH9 [6:0] | x | x | x | x |  | 
GAIN 9
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x24 | 0x40 | x | x | x | x | x | GAIN_CH10 [6:0] | x | x | x | x |  | 
GAIN 10
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x1B | 0x40 | x | x | x | x | x | GAIN_CH1 [6:0] | x | x | x | x |  | 
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x26 | 0x40 | x | x | x | x | x | GAIN_CH12 [6:0] | x | x | x | x |  | 
GAIN 12
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x25 | 0x40 | x | x | x | x | x | GAIN_CH11 [6:0] | x | x | x | x |  | 
GAIN 11
OFS 12
These registers can not go outside the Global Technologies.
Acc | Addr | Default | B11 | B10 | B9 | B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
R/W | 0x0E | 0x40 | x | x | x | x | x | OFS_CH12 [6:0] | x | x | x | x |  | 

## Slide 23
Soldering Temperature Reflow Profile
XD12
Important statement
Global Technologies reserves the right to change the above-mentioned information without prior notice.
Fig 9. Reflow Soldering information
Parameter | Pb-free soldering conditions
Average ramp-up rate (217 ℃ to Peak) | 3℃/second max.
Time of Preheat temp (from 150 ℃ to 200 ℃) | 60 ~ 120 second
Time to be maintained above 217 ℃ | 60 ~ 150 second
Peak temperature | 260 +5/-0 ℃
Time within 5 ℃ of actual peak temp | 30 second
Ramp-down rate | 6 ℃/second max.
Time from 25℃ to peak temp | 8 minutes max.
Table 5. Reflow Soldering Parameter
JEDEC J-STD-020D

## Slide 24
Package specification
XD12
TOP VIEW
BOTTOM VIEW
Pin #1
E
D
Unit :mm
Symbol | Dimensions in mm |  | 
 | Min | Nom | Max
A | 0.50 | 0.55 | 0.60
A1 | 0.00 | - | 0.05
A3 | 0.152 REF |  | 
b | 0.15 | 0.20 | 0.25
b1 | 0.08 | 0.13 | 0.18
D | 2.90 | 3.00 | 3.10
D1 | 1.25 | 1.30 | 1.35
E | 2.90 | 3.00 | 3.10
E1 | 1.75 | 1.80 | 1.85
e | 0.40 BSC |  | 
K | 0.25 | 0.30 | 0.35
L | 0.25 | 0.30 | 0.35
SIDE VIEW
Fig 10. Package Outline
QFN 3030-24L Package Outline

## Slide 25
Recommended Footprint
XD12
is the trademark of Global Technologies Co., Ltd. or its subsidiaries in the Republic of Korea and/or other countries. The products of Global Technologies reserve the right to make changes without further notice to any products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Global Technologies does not convey any license under its patent rights nor the rights of others.
is the trademark of Global Technologies Co., Ltd. or its subsidiaries in the Republic of Korea and/or other countries. Global Technologies owns the rights to a number of patents, trademarks, copyrights, trade secrets, and other intellectual property. Global Technologies reserves the right to make changes without further notice to any products herein. Global Technologies makes no warranty, representation or guarantee regarding the suitability of its products for any particular purpose, nor does Global Technologies assume any liability arising out of the application or use of any product or circuit, and specifically disclaims any and all liability, including without limitation special, consequential or incidental damages. Buyer is responsible for its products and applications using Global Technologies products, including compliance with all laws, regulations and safety requirements or standards, regardless of any support or applications information provided by Global Technologies. “Typical” parameters which may be provided in Global Technologies data sheets and/or specifications can and do vary in different applications and actual performance may vary over time. All operating parameters, including “Typical” must be validated for each customer application by customer’s technical experts. Global Technologies does not convey any license under its patent rights nor the rights of others. Global Technologies products are not designed, intended, or authorized for use as a critical component in life support systems or any FDA Class 3 medical devices or medical devices with a same or similar classification in a foreign jurisdiction or any devices intended for implantation in the human body. Should Buyer purchase or use Global Technologies products for any such unintended or unauthorized application, Buyer shall indemnify and hold Global Technologies and its officers, employees, subsidiaries, affiliates, and distributors harmless against all claims, costs, damages, and expenses, and reasonable attorney fees arising out of, directly or indirectly, any claim of personal injury or death associated with such unintended or unauthorized use, even if such claim alleges that Global Technologies was negligent regarding the design or manufacture of the part. Global Technologies is an Equal Opportunity/Affirmative Action Employer. This literature is subject to all applicable copyright laws and is not for resale in any manner.
Unit :mm
Note: The reflow peak soldering temperature is peak 260°C and it is specified based on IPC/JEDEC J-STD- 020 “Moisture/Reflow Sensitivity Classification for Non-Hermetic Solid State Surface Mount Devices”
Dim | Value(mm) | Margin(Typ+)
X | 0.5 | +0.2
Y | 0.2 | 0
C | 0.4 | 0
X1 | 0.5 | +0.2
Y1 | 0.5 | +0.2
X2 | 1.4 | +0.1
Y2 | 1.9 | +0.1
X3 | 1.1 | +0.1
Y3 | 1.6 | +0.1
X4 | 3.2 | +0.2
Y4 | 3.2 | +0.2
G | 0.2 | 0
G1 | 0.3 | 0
G2 | 0.1 | 0
G3 | 0.1 | 0
G4 | 0.1 | 0
Fig 11. Recommended Footprint